## Slide 1: Design for school building
Prepared By:
Hani shkarnah
Supervisor: Eng. Monther dweikat
Faculty of Engineering & Information Technology
Department of Building Engineering
An-Najah National University

## Slide 2: Contents:
Site analysis
Architectural Design
Environmental Design
Structural system Design
Electro-Mechanical system Design
Quantity Survey and Cost

## Slide 3: Architectural design
Site analysis
The site is located in maajeen east of Nablus, about 660 m above sea level and 2 kilometers away from city center. Site has a total area of 5583 m2.

## Slide 4: Site analysis

## Slide 5: Ground Floor

## Slide 6: First Floor

## Slide 7: Second Floor

## Slide 8: Southern Elevation

## Slide 9: Northern Elevation

## Slide 10: Section A-A

## Slide 11: Section B-B

## Slide 12: Environmental Design
Component | U-value (w/m2-k)
External Wall | 0.492
Partition Wall | 2.585
Floor | 0.487
Roof | 0.498
Windows (Double glass, low e, 6 mm) | 1.493
New U value for building envelope

## Slide 13: Shading
Design Builder program ( 3D Model )

## Slide 14: Shading
Eastern windows (vertical shutters)
Southern windows (horizontal Louvers)

## Slide 15: Shading
Summer day (sun path 21/6 at 8:00 am )
Summer day (sun path 21/6 at 2:00 pm )

## Slide 16: Shading
Winter day (sun path 21/1 at 8:00 am )
Winter day (sun path 21/1 at 2:00 pm )

## Slide 17
Heating and cooling load
Cooling load 77.4 kw
Heating load 41.9 kw
Site and Source Energy
Thermal Design
Old total site energy
New total site energy

## Slide 18
Comfort PMV-Set
Old PMV graph
New PMV graph

## Slide 19: daylight analysis
D.F% | Space
3.64 | Meeting hall
5.23 | Reception
5.61 | Medical committee

## Slide 20: Acoustics Design

## Slide 21
RT60 (Reverberation Time)
Multi purpose

## Slide 22
RT60 (Reverberation Time)
Element | Finish material | Absorption coefficient(α) at each frequency |  |  |  |  |  |  |  |  | 
 |  | 63HZ | 125 HZ | 250 HZ | 500 HZ | 1000 HZ | 2000 HZ | 4000 HZ | 8000 HZ | 16000HZ | 
Ceiling | Acoustical Tile | 0.7 | 0.66 | 0.72 | 0.92 | 0.88 | 0.75 | 0.75 | 0.75 | 0.75 | 

## Slide 23
RT60 (Reverberation Time)
At 50 % occupancy | 
FREQ. | RT60
63Hz: | 1.1
125Hz: | 0.98
250Hz: | 0.91
500Hz: | 0.96
1kHz: | 0.57
2kHz: | 0.33
4kHz: | 0.17
8kHz: | 0.09
16kHz: | 0.1
Recommended
Clinic room
(0.4-0.6)
Old RT60 Values for Clinic Room
At 50 % occupancy | 
FREQ. | RT (60)
63Hz: | 0.51
125Hz: | 0.52
250Hz: | 0.49
500Hz: | 0.45
1kHz: | 0.44
2kHz: | 0.44
4kHz: | 0.36
8kHz: | 0.23
16kHz: | 0.23
New RT60 Values for Clinic Room

## Slide 24
RT60 (Reverberation Time)
Old RT60 Values for Manager Room
New RT60 Values for Manager Room
At 50 % occupancy | 
FREQ. | RT(60)
63Hz: | 0.98
125Hz: | 1.14
250Hz: | 1.16
500Hz: | 1.19
1kHz: | 1.16
2kHz: | 0.72
4kHz: | 0.43
8kHz: | 0.23
16kHz: | 0.26
At 50 % occupancy | 
FREQ. | RT (60)
63Hz: | 0.63
125Hz: | 0.66
250Hz: | 0.69
500Hz: | 0.72
1kHz: | 0.75
2kHz: | 0.81
4kHz: | 0.72
8kHz: | 0.5
16kHz: | 0.5
Manager office
room
(0.7-1.3)

## Slide 25
STC and IIC
For External Wall of Clinic Room
TL = 50 dB
External Wall

## Slide 26
STC and IIC
For Manger room adjacent to secretary office
TL = 46 dB
Internal Wall
Recommended Value 45 dB

## Slide 27
IIC For Ceiling
IIC = 70 dB

## Slide 28: Structural Design

## Slide 29: Codes and Loads
Concrete:
The required compressive strength after 28 days fʹc
fʹc=280kg/cm² (28 MPa) (B350) for slab and beams
Modulus of elasticity (E= 2.48*104MPa)
Reinforced Concrete unit weight = 25 (KN/m3).
Reinforcing Steel:
The yield strength of steel is equal to 4200 Kg/cm2 (420 MPa).
The modulus of elasticity is 2.04*105MPa
Codes
UBC-97 for Earthquake design
ACI 318-14 for RC structure design
Structural design

## Slide 30: Model Checks
Structural design
Compatibility Check
This check was done for three models, while the period was reasonable and all the structural elements are compatible and moving together, the Figures below show the major periods for the three models:
Sample block 1 :-

## Slide 31: Model Checks
Structural design
Equilibrium Check
Equilibrium check is done to ensure that all input date including loads and assignments are correct. The allowed percent of error is 5 %.
The figures below show the Base reactions (Dead, Live and superimposed) which will be checked manually with an acceptable error up to 5 % for Block 1, 2 and 3.

## Slide 32: Model Checks
Structural design
Deflection Check
According to ACI-318, the maximum allowed deflection Shall not exceed the length of the slab divided by 240.
For Block One:
Length of the slab = 8.4 m, The maximum allowable deflection = 35 mm,
From Etabs the maximum deflection is 33 mm < 35 mm so deflection check is ok.

## Slide 33: Model Checks
Structural design
Period Check
Check period:
According to UBC code the period (T) of the building shall not exceed a value of 40 percent of T obtained from method A in Seismic Zone 2.
T (from A method) = Ct (hn) 3/4 where:
hn is the height of structure in meters = 10.5 m, Ct is a constant = 0.0488
For Block 1:
By modeling, the structure has a period T =0.36 seconds.
Then T (from A method) = 0.28 seconds.
The period shall be less than 1.4 * T (from method A) = 1.4*0.28 = 0.4 seconds.
T of the building = 0.36 which is less than 0.4 seconds, So, the period is Ok.

## Slide 34: Slab Reinforcement
Structural design

## Slide 35
Structural design
Columns Reinforcement

## Slide 36
Structural design
Footing Dimensions:
Area Footing = P service / qall
Area of footing = 1693/ 350 = 4.8 m2
The length of footing = 2.4, the width of footing = 2.1
Assume thickness of footing is h= 500 mm so d = 500 – 70 = 430 mm
Footing Reinforcement
Sample Calculations of Footing (1):
P service = 1693 kN
P ultimate = 2252 kN

## Slide 37
Design of Wall Footings
The selected footing for design in shown in the figure below:
Sample calculations for wall footing (F6)
P service = 243 kN , P ultimate = 314 kN,
P service kN/m = 151 , P ultimate kN/m = 196
Length of wall = 1.6 m
Area of footing = 151 /350 =0.43 m2
Width of footing= 0.43 m2 / 2.2 = 0.19 m So try width of 0.9m.

## Slide 38
Structural design
Stairs Reinforcement

## Slide 39: Electrical Design

## Slide 40: Ground Floor socket plan

## Slide 41: Luminaires Layout
Old Main Luminaire
New Main Luminaire
100 lm/w
50 lm/w

## Slide 42: 3D Rendering View for Selected Rooms
Teacher room

## Slide 43: Teacher room
Average Illuminance
535 Lux
UGR = 17.7
Required illuminance
500 lux
Required uniformity
(>0.60)

## Slide 44: Mechanical Design

## Slide 45
Water Supply System

## Slide 46
Water Supply System

## Slide 47
Drainage system

## Slide 48
Rain Water Drainage

## Slide 49: Firefighting and Safety Design

## Slide 50
Emergency Fire Protection System

## Slide 51
Emergency Fire Protection System

## Slide 52: Quantity Surveying and Cost Estimation

## Slide 53
Directorate of Health | Total Direct Cost (Nis)
Structure work | 2,297,256
Mechanical Work | 240,500
Finishing Work | 1,158,506
Electrical Work | 294,801
Total direct project cost | 3,991,063
Unit Direct Cost = 3991063/2235 = 1786 Nis /m2
Cost Estimation
Unit Direct Cost = 352 JD /m2

## Slide 54
Thank You