## Slide 1: General board for full automatic washing machines

## Slide 2: A simple definition of our project
Design general board for full automatic washing machines that is capable of dealing with most of the types found in the Palestinian market

## Slide 3: Project Idea
The idea behind our project, that many machines are produced once and sold in our market without technical support, so the alternative solution of the customer if any fault occurs in the board of washing machine is to buy a new board from the global market which is cost and need a lot of time to get it in Palestine that is not acceptable, here starts the problem of the local market.

## Slide 4: How can we make it general ??
First we should figure out all components in the washing machines and know the algorithm and the flow chart of its process
Design drive circuit that fit most of types of actuator .
Choose a microcontroller capable of handling most of actuators and sensors.
Make some code modification to suit the sensor data

## Slide 5
The electrical components in the washing machine

## Slide 6
Actuators in washing machines

## Slide 7
- Water inlet valve
- Door lock
- Drain pump

## Slide 8
TRIAC was used for switching these loads at zero firing angle
Opto-Diac for isolation and make firing point more even in both +ve ,-ve AC
- MOV for protecting TRIAC circuit from any high instant voltages that generated from switching on and off inductive loads and also reduce noise waves .

## Slide 9: Motor
The board is designed for washing machines that contain universal motor

## Slide 10: Speed of the universal motor By zero crossing detector CCT

## Slide 11: The direction of rotation in the universal motor
Reverse the direction of rotation in the
universal motor depends on reversing
the current in the rotor only .

## Slide 12: Heater

## Slide 13: display
A liquid crystal display, or LCD with I2C module was used as a display pf this project.
Need 2 pins in the controller for serial data and serial clock and 2 pins for power.

## Slide 14
Inputs in washing machines

## Slide 15: Power switch ( selector ) :
It is just a selector to select at what program (washing type ) the washing machine will work “eg: cotton , sport wear , …. etc”

## Slide 16: Push buttons
4 push buttons were considered as inputs in this project:
Play/pause.
Temperature adjustment.
Rinse adjustment.
Spin speed adjustment.

## Slide 17: Pressure sensor
The pressure sensor is a device that detects the level of water that required to the clothes that will be washed

## Slide 18: thermistor
The thermistor (temperature sensor) acts as a feedback unit to the controller to obtain the temperature that is reached by the heater

## Slide 19: tachometer
The speed of the motor will be measured and sent to the controller as a feedback by the AC tachometer

## Slide 21: Feed back pin of the door lock

## Slide 22: The Type of the controller
We found that using Arduino is more cheaper and easier for controlling and still effective controller for this process .
We chose Arduino UNO.
UNO contains 18 I/O pins.
23 I/O pins are needed.

## Slide 23: Expanding I/O pins of the controller
we used 8-bit Shift Register for expanding output pins of UNo

## Slide 24
Designing all schematics and generating them to board files

## Slide 25: For board connected to digital pins

## Slide 26: For second board connected to digital pins

## Slide 27: For board connected to analog pins

## Slide 28: For push buttons board

## Slide 29
Transform to real boards

## Slide 30: Print CCT’s onto photo paper

## Slide 31: Put the photo paper on copper board under iron

## Slide 32: Removing photo paper

## Slide 33: Putting this copper board under ferric chloride acid

## Slide 34: Taking the board and drying it from the acid

## Slide 35: Erasing the protection ink by sharp fiber

## Slide 36: Puncture all pads and vias by a drill and weld all components

## Slide 37: The final results

## Slide 38
Programming general algorithm

## Slide 39: Economical study
The whole project costed 35$ and it will suit most of washing machines.
The average price of the manufactured boards sold in the market = 90 $ and it suits specific brands only.
Which means that it is economically feasible and money-saving

## Slide 40
Thank you