## Slide 1
Assessment and Redesign of Solitaire restaurant
An-Najah National University
Faculty of Engineering & Information Technology
Department of Building Engineering
Graduation Project (2)
Supervisor :Dr. Hasan Mather
Students:
Ahmad Ismail , Ayham Ebayeh , Aysar Abu Jaish , Yahya Qadous

## Slide 2
Outline :
Introduction
Project Description.
Architectural Analysis and Re-design
Environmental Analysis and Evaluation
Structural Analysis
Cost estimation
Results and Recommendation

## Slide 3
In this project an evaluation and a redesign for the architectural, structural, mechanical and environmental systems was made for solitaire restaurant.
Introduction:
Project problem:
The city of Nablus is a destination for many tourists , a noticeable increase in the number of restaurants has been observe. Thus, this study explored Solitaire restaurant to see if the restaurant meets the required specifications.

## Slide 4
Objectives:
Evaluation and redesign the architectural, structural , mechanical and environmental systems that achieves the comfort for users , taking the architectural aspects in consideration.
Methodology:
Then there was a data collection about the restaurant and the international standards.
A comparison with international standards will be done, restructuring and development of the building from the inside, to better organize the spaces, to ensure a smooth flow of work and the comfort of visitors.
4

## Slide 5
Description of the project :
Location :
The project locates in Beit Wazan village in north west of Nablus city on the land with an area of 1131 m2

## Slide 6
Site and land boundary
The total area of the site equals 1131 m2
Description of the project :

## Slide 7
Architectural analysis
Architectural analysis and redesign
This study conducted the site relationship with streets , garage and restaurant it self and study the functional spaces in the building by this analysis to reach results that help us to modify these spaces according to standards.

## Slide 8
Ground floor plan:
Architectural analysis and redesign
After
Before

## Slide 9
First floor plan:
Architectural analysis and redesign
After
Before

## Slide 10
Site before redesign
Architectural analysis and redesign

## Slide 11
Site after redesign
Architectural analysis and redesign

## Slide 12
West elevation before redesign
Architectural analysis and redesign
West elevation after redesign

## Slide 13
Architectural analysis and redesign
East elevation before redesign
East elevation after redesign

## Slide 14
Architectural analysis and redesign
south elevation before redesign
south elevation after redesign
14

## Slide 15
Architectural analysis and redesign
north elevation before redesign
north elevation after redesign
15

## Slide 16
Architectural analysis and redesign
Section A-A before redesign
Section A-A after redesign
16

## Slide 17
Architectural analysis and redesign
Section B-B before redesign
Section B-B after redesign
17

## Slide 18
Existing building
Description of the project :

## Slide 19: 3D photo for solitaire restaurant after redesign
19

## Slide 20: Parking suggestion 1
20

## Slide 21: Parking suggestion 2
21

## Slide 22
General information
Structural analysis
Design code :
American Concrete Institute ACI 318
.
American Society of Civil Engineers (ASCE) 7-98.
Materials :
Concrete.
f´c = 24 Mpa.
specific weight of Reinforced concrete (Ɣ) = 25 KN/m³
specific weight of block (Ɣ) = 12 KN/m³
Yielding strength of steel (Fy = 420 Mpa)

## Slide 23
Loads
Live Load= 3 KN/m²
Live Load of barking = 5 kn/m²
Superimposed dead load = 4 KN/m² (assumed)
Weight of Masonry wall = 21 KN/m (assumed)
General information
General information
Structural analysis

## Slide 24
Structural element used
Structural analysis
- Slab:
Solid slab with 15cm thickness for the restaurant floor.
One way and two way ribbed slab with thickness of 32 cm.
One way ribbed slab with thickness of 25 cm for the outside laundry.
- Columns:
The columns are dimensional (0.25* 0.6), (0.25* 1) m
- Shear walls:
Thickness 30 cm for walls.

## Slide 25
- Main beams:
The main beams dimensions are assumed to be 0.6m depth and 0.6m width .
-Secondary beams :
The secondary beams dimensions are assumed to be 0.32m depth and 0.4m width .
Structural element used
Structural analysis

## Slide 26
The structural layout after redesign The structural layout before redesign
26

## Slide 27
The building is one structural blocks.
Columns center lines after redesign
Structural layout for the building after redesign
Structural analysis

## Slide 28: Beam Layout
first floor
second floor
28

## Slide 29
Figure :3D model for the first part
Structural ETABS model
Structural analysis

## Slide 30
All checks will be done to make sure that the work was done properly according to ACI which is deflection, compatibility, equilibrium and internal forces check
ETABS checks
Structural analysis

## Slide 31: Deflection check:
Critical span length =10.80m
Deflection limit (Δ) = = 0.045m
From ETAB Deflection = Uz = 0.021m
The deflection in slab does not exceed the limit.
31

## Slide 32
Compatibility check
Compatibility check was done on ETAB, all element are moving together.

## Slide 33
Table :Equilibrium check for the first part
Equilibrium check
a) For Live Load:
From ETAB LL= 1108.2 KN.
Manual:
LL =657.75 KN “ first story
LL=455.16 KN “ second story
LL total=1112.91KN
%Error =0.42 % < 5 % it’s OK

## Slide 34
Table :Equilibrium check
Equilibrium check
Loads | ETABS (KN) | Parts | Manual | % Error
Live | 1108.2 | Slabs | 1112.91 | 0.42%
SID | 3460.86 | Slabs | 3605.83 | 4.1%
 |  | Slabs | 3834.92 | 
 |  | Columns | 450 | 
Dead | 9389.94 | Walls | 1324.75 | 0.5%
 |  | External walls | 2870 | 
 |  | Beams | 864 | 
Total (KN) |  |  | 9343.67 | 

## Slide 35
Internal forces check
Column 1:
From ETAB ultimate axial force = 99.13 KN.
Column weight =16.875 KN.
Slab weight = 23.7 KN.
Wall weight = 60.48 KN.
Total manual = 101.05 KN.
% error = 1.9% < 5% … Ok

## Slide 36
Beam:
Moment from ETAB = 13.51 KN.m.
Manual = WL2*Ln^2/16 = 12.6 KN.m
%error = 4.1% < 5% … Ok.
Slab:
Moment from ETAB = 8.12 KN.m.
Manual = WL^2/8 = 8.4 KN.m.
%error = 3.4 % < 5%… Ok.

## Slide 37
Site analysis
Environmental analysis and evaluation
Wind direction : the general direction in our country is from the north-west direction.
The noise: mainly from the street and the neighbor buildings.
The orientation of building the restaurant titles northward by an angle of 25 degrees.

## Slide 38
Site analysis
Environmental analysis and evaluation
Sun path the sun moves from east to west passing through the south. Therefor, the south west facad will be the one which exposed the most sun heat.

## Slide 39
Environmental analysis and evaluation
According to the sun path a treatment for the south west elevation was done with horizontal and vertical louvers. And a moving shading system was made as a treatment for the roof of the terrace.
Shading system

## Slide 40
The illuminance in the ground floor
Environmental analysis and evaluation
After Modification
Before Modification

## Slide 41
After Modification
Before Modification
The illuminance in the first floor

## Slide 42
Solar radiation on the elevation
Environmental analysis and evaluation
The solar radiation has three main components diffuses ,direct and reflected components the main solar radiation effect on the building is direct solar radiotin on the building elevation by using Revit to find the value of solar radiation on elevation , this value and its affect was taken into consideration in the HVAC system in the second part of the project.

## Slide 43
Solar radiation on the elevation
Environmental analysis and evaluated
North elevation
East elevation

## Slide 44
Solar radiation on the elevation
Environmental analysis and evaluated
South elevation
West elevation

## Slide 45: Cost estimation:
In this stage of the project will follow the parametric modeling for cost estimation.
The cost per square meter of such a project is estimated at 600 dollars/m2.
Total cost of the restaurant is around = 600*394.52 = 236800 $.
The cost per square meter of the Garage is estimated to be a bout = 300 dollars/m2.
Total cost of Garage is around= 274*300 = 82200 $.
Total cost for the Restaurant and the Garage is around = 319000 $.

## Slide 46
Results
1) A shortage of car parking lots.
2) There is a different between shop drawings and as built drawings.
3) The absence of an emergency exit in the event of a fire inside the restaurant.
4) There is no service elevator inside the restaurant.
5) The outside terrace need a suitable shading system.

## Slide 47
Thank You