## Slide 1
Graduation Project II
Design of Tubas Main Street
Bashar Hanoun, Noor Akhras & Aws Ammar
Dr. Amjad Issa

## Slide 2: Design of Tubas Main Street
Prepared by:
Bashar Hanoun
Noor Akhras
Aws Ammar
Under Supervision of:
Dr. Amjad Issa

## Slide 3: DESIGN OF TUBAS MAIN STREET
BASHAR HANOUN, NOOR AKHRAS & AWS AMMAR

## Slide 4
1
General Background
2
Objectives
3
Project Entrance
4
Methodology & Design Criteria

## Slide 5
5
Geometric Design
6
Pavement Design
7
BOQ & Cost Estimations
8
Conclusions & Recommendations

## Slide 6: Tubas city is one of the most important Palestinian cities because it’s connects Jenin city with Nablus city in addition to the Jordan Valley.

## Slide 7: Map of Tubas City and the location of Tubas Main Street

## Slide 8: Aerial Photos for the Entrance and Exit of the road.

## Slide 9
1
Evaluate Existing Road
2
Analyze Existing Road
3
Re-Design Geometric of existing Road
4
Quantities & Costs Estimated

## Slide 10: Methodology

## Slide 11: Site Investigation Road Inventory studies and data collection

## Slide 12: Al-Shaheed Intersection
16 meter , two way
8 meter , two way
10 meter , two way
20 meter , two way

## Slide 13: Data Collection

## Slide 14: Peak Hour Classification

## Slide 15: Tubas Roundabout Intersection
14 meter , one way
20 meter , two way
12 meter , one way

## Slide 16: Data Collection

## Slide 17: Peak Hour Classification

## Slide 18: Data Analysis PH and PHV calculation

## Slide 19: Overall PHF value for each Intersections

## Slide 20: PHF value per approach for both Intersections

## Slide 21: PH, PHV and PHF calculation after 20 years
Intersection | PH | PHV(veh/hr)
Al-Shaheed | 12:15-1:15 PM | 1792
Tubas Roundabout | 12:45-1:45 PM | 2171
Intersection | PHF
Al-Shaheed | 0.86
Tubas Roundabout | 0.99

## Slide 22: Warrants and Level of service
Warrant 1, Eight-Hour Vehicular Volume.( Not applicable ).
Warrant 2, Four-Hour Vehicular Volume.
Warrant 3, Peak Hour Delay/Volumes.
Warrant 4, Pedestrian Volume. ( Not applicable ).
Warrant 5, School Crossing. ( Not applicable ).
Warrant 6, Coordinated Signal System. ( Not applicable ).
Warrant 7, Crash Experience. ( Not applicable ).
Warrant 8, Roadway Network. ( Not applicable ).

## Slide 23: The result of warrants in Al-Shaheed intersection

## Slide 24: The Result of LOS of Al-Shaheed intersection

## Slide 25: The result of warrants in Al-Shaheed intersection after 20 years

## Slide 26: The Result of LOS of Al-Shaheed intersection after 20 years

## Slide 27: The result of warrants in Tubas Roundabout intersection

## Slide 28: The result of LOS of Tubas Roundabout intersection

## Slide 29: The result of warrants in Tubas Roundabout intersection after 20 years

## Slide 30: The result of LOS of Tubas Roundabout intersection after 20 years

## Slide 31: The result of warrants in New Tubas Roundabout intersection

## Slide 32: The result of LOS of New Tubas Roundabout intersection

## Slide 33: The result of warrants in New Tubas Roundabout intersection after 20 years

## Slide 34: The result of LOS of New Tubas Roundabout intersection after 20 years

## Slide 35: The New Tubas Roundabout intersection

## Slide 36: The New Design of New Tubas Roundabout

## Slide 37
Station | Design Speed (Km/hr) | Superelevation | Minimum Radius (m)
(0+000 – 0+370) | 50 | NON | 116
(0+370 – 2+800) | 70 | 6 % | 184
(2+800 – 8+200) | 50 | NON | 116
(8+200 – 9+120) | 40 | NON | 70
(9+120 – 9+396) | 50 | NON | 116

## Slide 38
WB-20
Height = 4.1 m Width = 2.6 m Length = 22.4 m

## Slide 40
Type of the Curve | Number
Simple curves | 26
Compound curves | 12
Reversed curves | 6

## Slide 42
Max. Grade  13 %
Note : All segments match the max grade except the following.
Station | Grade
(0+020 – 1+095) | 15.12 %
(7+075 – 7+615) | 13.97 %

## Slide 43
Type of Curve | Minimum K | Number
Crest Curve | SSD for V = 70  k = 17 for V = 50  k = 7 for V = 40  k = 4 | 9
Sag Curve | HSD For V = 70  k= 23 for V = 50  k = 13 for V = 40  k = 9 | 9

## Slide 44
We have two typical cross section scenarios:
Type of the Cross Section | Station
With Sidewalk ( Typical 1 ) | (0+000 – 1+500)
 | (7+500 – 9+396)
With Shoulder ( Typical 2 ) | (1+500 – 7+500)

## Slide 45
Typical Cross Section 1 ( with Sidewalk )

## Slide 46
Typical Cross Section 2 ( with Shoulders )

## Slide 47
Current ADT(Faisal Street) 31080 veh/day
Percentage (NRR) = 23 %  Take 25 %
Chart: Origin – Destination (800) Samples
| Fisal Street | Ring Road
Sales | 0.75 | 0.25
Estimation ADT(NRR) 7770 veh/day
25 %
Design ESAL (20 years) 2.9 Millions

## Slide 48
Travel lanes number (N = 2)  Satisfied
HCS software check:

## Slide 49
CBR Test

## Slide 50
Sample | CBR Value | Stations Represented
Sample 1 (0+850) | 27.4 % | (0+000 – 7+500)
Sample 2 (7+600) | 3.8 % | (7+500 – 9+396)

## Slide 51
0+000 – 7+500
7+500 – 9+396

## Slide 52
INT.1
INT.2
INT.3
INT.4
INT.5
INT.6
U-Turn

## Slide 53
INT.1

## Slide 54
U - Turn

## Slide 55
INT.2

## Slide 56
INT.3

## Slide 57
INT.4

## Slide 58
INT.5

## Slide 59
INT.6

## Slide 60
Vehicle Tracking Check

## Slide 61
Items | Estimation Cost (Million)
Cut & Fill | 4.79
Base Coarse | 1.41
Sub Base | 0.1
Pavement | 4.28
Marking | 0.22
Paving | 1.04
Signing & Cuties | 0.07
Walls & Guard Rail | 1.2
TOTAL PROJECT COST | 13.1 M

## Slide 62: Conclusion
Decreasing Congestion and Providing Accessibility
The Proposed Route not match AASHTO Classification
The design match AASHTO around 90%
In high fill segments, we need layers of Rock Block
The Current Solutions aimed at reduction the Traffic Jam
1
2
3
4
5

## Slide 63
It is recommended to consider the other alternative modified route for the entrance of the road in order to work 4-legs intersection.
Nablus Municipality is encouraged to attain the needed funds to construct the whole Ring Road.
Redesign intersections after street operating.
Reorganizing the area around the Road especially at the End .

## Slide 64
Complete all parts of the project surround Nablus-City.
Select the projects that are in the priory and short list according to the strategic plan.
Design a proper drainage system in order to avoid acceptable future problems in the road layers.
Design the thickness of the concrete walls.

## Slide 65
Prevent the placing of grafts in the street area.
February 2017
November 2017

## Slide 66
Check Current House Levels And Stabilize Street Levels.