## Slide 1
Handy
By : Emad Aghbar Mohammad Abdalraziq
Supervisors: Ashraf Armoush

## Slide 2: Outline:
Motivation
What is Handy
How it works
Technical choices
implementation
Challenges
Constraints
Future work

## Slide 3: Motivations:
Controlling presentation limits movement.
User has two choices:
  Sacrifice Full control in the sake of free movement
  Get full control but loose free movement
Presentation screen is not interactive enough.
Traditional solutions don’t give satisfying controls.

## Slide 4: Handy
Is a smart glove
Gives remote controlling capabilities over PC.
  Control PC using simple hand gestures.
Converts projector screen into a sudo-touch screen
Fun and more interactive presentation experience

## Slide 5: How Does it work …
Hand Gestures
  By only moving your hand, you can control screen.
  Simple hand gestures translated to computer commands.

## Slide 6: How Does it work …
Sudo touch screen
  Turning projecting surface into a touch screen

## Slide 7: Technical choices
Hardware:
  Reading hand gestures :
    Reading fingers
    Hand motion
  Creating touch surface :
    Wiimote and IR camera
    IR LED signals

## Slide 8: Reading hand gestures
Flex Sensors:
A variable resistor
  Placed on each finger
  Used to read fingers status
  Translated to commands via Arduino code

## Slide 9: Flex implementation:
Connection :

## Slide 10: Flex implementation:
Thresholds & readings :
Distorted signals Smooth signals

## Slide 11: Reading hand gestures
Motion sensor – BNO055:
  Contains gyroscope
  Installed on top of glove
  Reads 3-axis motion angles of the hand
  Angles reading converted to commands via Arduino Nano

## Slide 12: Glove – PC connection :
Arduino Nano :
  Main brain of the project
  Reads sensors data and processes them
  Handles connection between glove and PC

## Slide 13: Glove – PC connection :
Bluetooth:
  Connects glove to PC .
  Exchange commands and data between them.
  Cheaper and consumes low power compared to Wi-Fi .
  more consistent than IR .
  Gives suitable connection distance .

## Slide 14: Creating touch surface
  Wiimote and IR camera
    is a controller for Wii .
    Has so many capabilities .
    We are interested only in Bluetooth connection and IR camera .

## Slide 15: Creating touch surface
  IR LED signals
    IR LED and push Button installed in the index figure.
    Used to emit IR signals to be detected by IR Wiimote camera .
    Signals are translated to touch commands on screen using smoothBoard software .

## Slide 16: Technical choices
Glove Software:
  Arduino code
    Processes and exchanges data with PC .
  Driver Software
    JAVA language was used to write driver Software for glove data.
    Driver reads data from Bluetooth and converts it to PC commands .

## Slide 17: Technical choices
Touch screen Software:
  SmoothBoard software .
    Connects PC to the Wiimote via Bluetooth.
    Calibrates screen with the Wiimote IR camera.
    Converts IR signals to touch commands

## Slide 18: Full Connections :

## Slide 19: Challenges
Coming up with consistent design.
Reflecting sensors data smoothly on screen
Turning surface to touch screen :
  Image processing
  IR signals

## Slide 20: Constraints:
design for the glove and the parts on it
Some parts availability

## Slide 21: Future work
Data mining.
Adapt other social websites events.
Improve owner capabilities on dashboard

## Slide 22: Demo

## Slide 23: Thanks
احنا مش