## Slide 1
Green parking
Graduation Project 2
Prepared by:
Saja M. Sawafta
Ayat daher
Ameera mousa
Maisa sawafta
Supervisor : Dr. Muhannad Haj Hussien

## Slide 2
Introduction
Structural Design
Environmental Design
Mechanical Design
Architectural Design
Electrical Design
Outline:

## Slide 3: Introduction and objectives
1. Prepare and finalize the architectural design considering all other aspects of design.
2. Conduct an environmentally friendly structure as much as possible.
3. The design will respect the recommended value and standard for the different aspects
4. Solve most common problems in the existing parking.
5. Design a bridge to connect our parking to the engineering faculty.
6. Well integration for our proposed parking in the university campus

## Slide 4
Site location:
Location: Site is located to the southern-west of Nablus city, the area of the site is 724m2

## Slide 5
Site location:

## Slide 6
Site advantages:
1- Easily access for cars.
2- The slope of the land is moderate.
3- No surroundings of high building that prevent sun and wind.

## Slide 7
Architectural Design

## Slide 8
project
Parking
4 floors
B2 , B1 , Gf , F1
Offices and drawing room
1 floor
F2

## Slide 9: Parking level Programming
Item | number | dimensions | Total Estimated Area (m2)
Car | 100 | 5.5*2.5 | 1375
Elevators | 2 | 3*2.5 | 15 *4 = 60
Staircase | 1 | 2.5*5.5 | 13.75* 4 = 55
Ramps | The percentage 46 % |  | 2011.1
Total estimated area |  |  | 3501

## Slide 10: Offices level Programming
Item | number | dimensions | Estimated total Area (m2)
Class room | 5 | 10*13.5 & 7.5*13.5 7*13.5 & 7.1*13.5 7*13.5 | 531.8
Offices (Privet) | 4 | 2.4 *4.2 | 40.32
Offices (General) | 1 | 3.36*5.58 | 18.7
W.Cs | 2 | 3.9*4.9 &5.3*7.6 | 59.39
Circulation and corridors. | Percentage = 21% |  | 228.3
Total estimated area |  |  | 878.51

## Slide 11: Parking plan

## Slide 12: Vertical transportation
Stairs: The parking has one staircase which could be used by both students and employees.
Elevators: We use two elevators for both doctors and student.
Ramps: After trying different scenarios with different types of ramps, we find that type B is the very appropriate type from the circulation, movement and size capacity. This ramp is designed for two way traffic movements with slope17%.

## Slide 13
type B ramp

## Slide 14: parking layout

## Slide 15
Perpendicular (90 degree)

## Slide 16
Angled 75 Degree

## Slide 17: Parking specification
1- Access and exit for pedestrian

## Slide 19: Parking dimensions
Type of vehicles | dimensions
Car | 2.4 meters x 4.8 meters
Light Vans | 2.4 meters x 5.5 meters
Articulated Vehicles | 3.5 meters
Standard dimensions of vehicles :-

## Slide 20
We used this 2.5 *5.5 m for each car park with 75 angled and 2.5*6 with angled 90 degree

## Slide 21: offices and drawing classes level plan

## Slide 22: Elevations
west elevation

## Slide 23
east elevation

## Slide 24
South elevation

## Slide 25
North Elevation

## Slide 26: Sections
section A-A

## Slide 27
section B-B

## Slide 28: Three dimension views

## Slide 29
south –east elevation

## Slide 30
west-south elevation

## Slide 31
north elevation

## Slide 32
roof shot

## Slide 33
Garden- offices level shot

## Slide 34
Structural Design

## Slide 35
Structural Design:
Design Codes:
ACI -318-08 (American Concrete Institution) for reinforced concrete structural design.
UBC-97 (Uniform Building Code) for earthquake load computations.

## Slide 36
Structural Design:
Building Description:

## Slide 37
Property | Value
Compressive strength of concrete, (f’c) | 
Modulus of elasticity, (Ec) | 
Unit weight of plain concrete, | 
Unit weight of reinforced concrete, | 
Property | Value
Yield strength (fy) | 
Modulus of elasticity, (Ec) | 
Material :
Reinforcement steel
Structural Design:
concrete

## Slide 38
Structural Design:
Types of loads:
Type of load | Load KN/m2
Live load | 4 KN/m2
Super imposed dead load | 3 KN/m2

## Slide 39
Structural Design:
Structural System:
The system of the slab is two way slab(35 cm thickness) with Drop beams 65 cm

## Slide 40
Structural Design:
ETABS model:

## Slide 41
Structural Design:
Compatibility check

## Slide 42
Structural Design:
Deflection check:

## Slide 43
Structural Design:
Equilibrium check:
Load type | Hand results KN | SAP results KN | Difference %
Dead | 74977 | 71767.2 | 4.28%
Super imposed | 18345 | 18320.5 | 0.13%
Live | 18169.13 | 17628.2 | 2.98%

## Slide 44
Structural Design:
Slab reinforcement

## Slide 45
Structural Design:
Beam reinforcement

## Slide 46: Column grouping
Group number | Section dimension (m) | Column number | Axial force rang (kN)
1 | 600X400 | C1,C5, C6, C28,C29 | Less than 1000
2 | 600X400 | C2,C3, C12, C24 | 1000-1999
3 | 600X400 | C4,C7,C13, C18, C19,C26, C27 | 2000-2999
4 | 600X400 | C25 | 3000-3999
5 | 600 | C9,C15,C16 | 3000-3999
6 | 700 | C21, C22 | 4000-5000
7 | 800 | C8,C10, C11,C14,C17,C20, C23 | 6000-7000

## Slide 47
Structural Design:
Column reinforcement

## Slide 48
Structural Design:
shear wall reinforcement

## Slide 49
Structural Design:
Footing layout

## Slide 51
Structural Design:
Footing reinforcement

## Slide 52
Structural Design:
bridge reinforcement

## Slide 53
Environmental Design

## Slide 54: Design Environmental
1. Solar analysis
2. Solar shading
3. Thermal insulation
4. Acoustical design
5. Heating and cooling
6. Daylight

## Slide 55: Design Environmental solar analysis
Summer day
shadow in our building on 21-6 at 12:00 pm in
shadow in our building on 21-12 at 12:00 pm in
Winter day

## Slide 56: Design Environmental
Solar Shading
As we know the sun is concentrated on the east elevation in the morning so the heating gain is huge.
Solution:
Using vertical louvers to prevent sun exposure, in order to reduce heat gain..

## Slide 57: Design Environmental
Value of thermal coefficient
U value (W/m2.k) | outer structure element of the building | number
0.5 | The external wall | 1
0.39 | Exposed horizontal roof | 2
0.39 | Exposed leaning roof | 3
2.46 | External window | 4
Thermal Insulation:
The goal: The achieved thermal coefficient U for all new and air-conditioned buildings should be not more than the U-value of the specified code

## Slide 58: Design Environmental
Thermal Insulation:
Exterior wall
U value from design builder
U = 0.34 > 0.5 ok

## Slide 59
Acoustical Design: The goal of acoustical design is to reduce of unwanted noise, which is referred to as noise control.
According to specifications of the offices, the required RT60 is ( 0.6– 0.8) s
RT60=2.12 s
After modification
RT60=0.62 s

## Slide 60
RT for parking floor is also very high and need to modify it by using an absorption material such as Heraklith C.
it is a fire resistance, acoustic performance, ease of installation, and attractive appearance for underground garages

## Slide 61
STC Calculations:
For inner wall ( between the classroom):
For external wall (for classroom 1)
-STC for classroom must be >42
STC=43
Required STC level (50-55)
STC=54

## Slide 62
Heating and cooling:
cooling capacity=97KW/m2
heating capacity=45KW/m2

## Slide 63
Daylight Factor = 0.726
Daylight

## Slide 64
Daylight
We notice that the daylight factor is less than required so we solved this problem by using skylight tubes in class rooms and parking floors
Required Lux of the classrooms and offices is 500 lux so we need 6 skylight tubes and we distribute as a grid.

## Slide 65
Mechanical Design

## Slide 66: Mechanical Design
Mechanical design involves many aspects including :
      Water Supply System.
      Drainage Water System.
      HVAC system.
      Fire fighting & emergency exits.

## Slide 67
Water Supply System

## Slide 68: Mechanical Design
Drainage system
Pipe size for W.CS=4”
Pipe size for Lavatory = 2’’.
      Black water: W.CS
      Grey water: Lavatory.

## Slide 69: Mechanical Design
Drainage system for the offices floor

## Slide 70
Drainage system for the parking floors

## Slide 71
HVAC system

## Slide 72
Ventilation system

## Slide 73: Fire System and Safety
Sprinkler fire system

## Slide 74
Fire system
Dry powder Portable Fire Extinguisher(in labs)

## Slide 75: Fire System and Safety
Fire-hose-system

## Slide 76
Electrical Design

## Slide 77: Lighting
Indoor lighting
1- Offices and class rooms floor :
We used LED for corridors , bathrooms and classrooms

## Slide 78
lamp type used in class rooms

## Slide 79
lamp type used in storage areas and corridors

## Slide 80
lamp type used in bathrooms

## Slide 81
lamp type used in offices

## Slide 82
2- parking : we used florescent lamp in the parking floors

## Slide 83: lighting requirements
U0 | Glare rating | Lux (avg) | Type of area | 
0.6 | 19 | 500 | Drawing room | 
0.4 | 28 | 100 | Circulation and corridors | 
0.4 | 25 | 300 | Ramps during the day | indoor Car park
0.4 | 25 | 100 | Parking areas | 
0.4 | 25 | 300 | bathroom | 
0.6 | 19 | 500 | Offices | 

## Slide 84: Dialux –values

## Slide 85
1- class rooms :

## Slide 86
2- corridor

## Slide 87
3-bathrooms

## Slide 88
4- offices

## Slide 89
5- parking

## Slide 90: Elevators

## Slide 91: Occupancy sensors

## Slide 92
sensors plan

## Slide 93
Load (KW.h) | Electrical equipment
22.4 | elevators
0.05 | sensors
197.581 | light
0.4 | electrical gate
35 | LCD projectors
85.32 | Electricity Socket
61.536 | fan coil unit
402.287 | Total load
electrical loads

## Slide 94: Solar cells
8045.74 KWh/month | Total demand /month
5470 KWh/ month | From solar cells avg. value
67.9 % | Percentage

## Slide 95
Parking -Lamp distribution

## Slide 96
Offices -Lamp distribution

## Slide 97
offices -socket distribution