## Slide 1: First Bicycle Network in Palestine
An-Najah National University
Engineering & IT Faculty
Civil Engineering Department
Prepared By:
Amro Al-Wawi
Anas Najeh’
Bayan El-Hout
Omar Al-Sahili
Supervised By:
Prof. Sameer Abu-Eisheh

## Slide 2: Report Outline
Methodology
Design Criteria
Amro Al-Wawi
Data Analysis
Bayan El-Hout
Omar Al-Sahili
Data Collection
Cost
Specifying
Study
Final Design
Final Design
EIA
Conclusion
Anas Naje’
Introduction
Final Design
Objectives
EIA

## Slide 3: INTRODUCTION
General Background
Importance of the Project
Problem Definition

## Slide 4: OBJECTIVES
Specifying the existing conditions
for Jericho city’s network
Performing the required studies and analysis
Designing the Network

## Slide 5
METHODOLOGY
Specifying Study Area
Data
Collection
Data
Analysis
Design criteria
Potential impacts
Final Design

## Slide 6: Specifying Study Area

## Slide 7: Jericho City Map
Amman St.
Al-Istiqlal Uni. St.
Tal Es-Sultan St.
Nile St.
AlQuds St.
Terra Santa St.
Jummezeh St.
City Center

## Slide 8: Specifying Questionnaire Sample

## Slide 9: Specifying Questionnaire Sample
School Students
Local citizens
Tourists

## Slide 10: DATA COLLECTION
Inventory study
Vehicle & bicycle counts
Pedestrians counts
Questionnaires

## Slide 11: DATA ANALYSIS
Vehicles
Bicycles
Pedestrians
Traffic
School Students
Local Citizens
Tourists
Ques.
Vehicles
Bicycles
Pedestrians
Traffic

## Slide 12: Traffic Analysis
Facility Type | Multilane-highway |  | Bicycle Lane |  | Pedestrian | 
Direction | NB | SB | EB | WB | EB | WB
Parameter | (D) 3.5 | 2.3 | 18(S) | 18 | 5.86 | 5.86
LOS | A | A | B | B | C | C
Al-Quds Street
Facility Type | Multilane-highway |  | Bicycle Lane |  | Pedestrian | 
Direction | EB | WB | EB | WB | EB | WB
Parameter | (D) 4.0 | 2.9 | 23(S) | 23 | 9.56 | 9.56
LOS | A | A | A | A | C | C
Amman Street
Facility Type | Multilane-highway |  | Bicycle Lane |  | Pedestrian | 
Direction | NB | SB | EB | WB | EB | WB
Parameter | (D) 1.2 | 1.6 | 22(S) | 22 | 3.03(Vp) | 3.03
LOS | A | A | B | B | C | C
Al-Istiqlal Uni. Street

## Slide 13: Traffic Analysis
Facility Type | Multilane-highway |  | Bicycle Lane |  | Pedestrian | 
Direction | WB | EB | EB | WB | EB | WB
Parameter | (D) 2.4 | (D) 2.5 | - | - | 1.67 (Vp) | 1.67
LOS | A | A | - | - | C | C
Tal Al-Sultan Street

## Slide 14: Questionnaire Analysis
Chart: Do you use bicycle for going to school or work ?
| Yes % | No %
Do you use bicycle for school ? | 47.5524 | 52.4476
Chart: What is your evalution for the safety for cyclists ?
| Safe % | Medium % | Dangerous %
What is your evalution for the safty for cyclists ? | 32.1678 | 55.9441 | 11.8881
Chart: 
| Yes % | No %
Do you think designing a new network would make you use bicycles more ? | 94.4056 | 5.5944

## Slide 15: DESIGN CRITERIA
Elements of D.
Design
Criteria
D. Vehicle
D. Speed
Intersection D.
Signs
Marking

## Slide 16: Design Criteria
Design Vehicle Standard Bicycle
Design Speed
Pav. Level Terrain 24 km/h

## Slide 17: Design Criteria
Shared Used Path
On Road Facilities
Elements of Design

## Slide 18: Design Criteria
On Road Facilities
Bicycle Lane
Shared Lane

## Slide 19: Design Criteria
Shared Use Path

## Slide 20: Final Design

## Slide 21: City Center Area Map

## Slide 22: City Center Area
ellipse roundabout 30m x 40m
2 lanes - 4 m per lane
Parking
Bicycle lanes

## Slide 23
City Center Area Design
Before
After

## Slide 24: Amman Street Map
Amman St.

## Slide 25: Amman Street
Sec # | Type of Facility | width of facility | WB Lane | median | EB Lane | EB parking | S SW | ROW
1 | SUP | 3.5 | 6 | 1 | 4.0* | 2.1 | 1.4* | (18)*
2 | SUP | 3.5 | 6 | 1 | 6 | 2.1 | 1.4 | 20
3 | SUP | 3.5 | 7.5 | 4.5 | 7.5 | NP | 3.0 | 26

## Slide 26: Amman Street Design

## Slide 27: Al-Istiqlal Uni. Street Map
Amman St.
Al-Istiqlal Uni. St.

## Slide 28: Al-Istiqlal Uni. Street
Sec # | Facility | E-SW | NB Park | NB BL | NB Lane | SB Lane | SB BL | SB Park | W-SW | ROW
1 | Bicycle L | 1.5 | NP | 1.5 | 3.0 | 3.0 | 1.5 | NP | 1.5 | 12
2 | Bicycle L | 1.5 | NP | 1.5 | 3.9 | - | 1.5 | 2.1 | 1.5 | 12
3 | Bicycle L | 1.5 | NP | 1.5 | 3.0 | 3.0 | 1.5 | NP | 1.5 | 12
4 | Bicycle L | 1.4 | 2.1 | 1.5 | 3.0 | 3.0 | 1.5 | NP | 1.5 | 14

## Slide 29: Al-Istiqlal Uni. Street Design

## Slide 30: Tal Es-Sultan Street Map
Amman St.
Al-Istiqlal Uni. St.
Tal Es-Sultan St.

## Slide 31: Tal Es-Sultan Street
Before Traffic Light
Sec# | Type of Facility | E SW | NB P. | NB BL | NB Lane | SB Lane | SB BL | SB P. | W SW | ROW
1 | BL | 3.0 | 2.1 | 1.5 | 3.3 | 3.3 | 1.5 | 2.1 | 3.0 | 20
After Traffic Light
Sec # | Type of Facility | E SW | NB BL | NB P. | NB Lane | SB Lane | SB P. | SB BL | W SW | ROW
2 | BL | 2.5 | 1.5+0.3 | 2.1 | 3.6 | 3.6 | 2.1 | 1.5+0.3 | 2.5 | 20

## Slide 32: Tal Es-Sultan Street Design
Notes: Check notes

## Slide 33: Al-Quds Street Map
Amman St.
Al-Istiqlal Uni. St.
Tal Es-Sultan St.
AlQuds St.
Abdl Nasir St.

## Slide 34: Al-Quds Street
Jamal Abdl Nasir Street
Al-Quds Street
Sec # | Type of Facility | N SW | EB Park | EB bicycle lane | EB-Lane | WB-Lane | WB bicycle lane | WB Park | S SW | ROW
1 | Bicycle Lane | 3 | 2.1 | 1.5+ 0.1 | 3.3 | 3.3 | 1.5+0.1 | 2.1 | 3 | 20
Sec # | Type of Facility | W SW | SB Bicycle lane | SB Lanes | NB Lanes | NB Bicycle lane | E SW | ROW
2- Bef. Bridge | bicycle lane | 1.7 | 1.5 + 0.2 | 6.6 | 6.6 | 1.5+0.2 | 1.7 | 20
3- at Bridge | Bicycle lane | 1.0 | 1.2 | 3.3 | 3.3 | 1.2 | 1.0 | 11
4- after Bridge | Bicycle lane | 1.7 | 1.5 +0.2 | 6.6 | 6.6 | 1.5 +0.2 | 1.7 | 20

## Slide 35: Al-Quds Street Intersection Design

## Slide 36: Al-Quds Street Design

## Slide 37: Terra Santa Street Map
Amman St.
Al-Istiqlal Uni. St.
Tal Es-Sultan St.
AlQuds St.
Terra Santa St.

## Slide 38: Terra Santa Street
Section # | Type of Facility | Shared Use Path | NB park | NB Lane | SB Lane | SB Park | W SW | ROW
1 | Shared use Path | 3.8 | 2.1 | 3.0 | 3.0 | 2.1 | 2.0 | 16
Section # | Type of facility | E SW | NB BL | NB Lane | SB Lane | SB BL | SB park | W SW | ROW
2 | bicycle lane | 2.0 | 1.5+0.1 | 3.3 | 3.3 | 1.5+0.1 | 2.1 | 2.1 | 16

## Slide 39: Terra Santa Street Design

## Slide 40: The Final Network Map
Amman St.
Al-Istiqlal Uni. St.
Tal Es-Sultan St.
Nile St.
AlQuds St.
Terra Santa St.
Jummezeh St.

## Slide 41: The Final Network Summary
Summary Road Network Lengths |  |  | 
No. | Street | Length(m) | Facility
1 | Jamal Abdl Nasir Street | 275 | Bicycle lanes
2 | Al-Quds Street | 875 | Bicycle lanes
2 | Terra Santa Street | 460 | Shared Use Path + Bicycle lanes
3 | Tal Es-Sultan Street | 3785 | Bicycle lanes
4 | Amman Street | 3170 | Shared Use Path
5 | Al-Istiqlal Uni. Street | 2435 | Bicycle lanes
Total Length = 12 km |  |  | 

## Slide 42
Scoping
Baseline Conditions
Monitoring and Auditing
Mitigation Measures
Environmental & Social Statement
Social and Environmental
Impacts
Environmental and Social Aspects

## Slide 43
Environmental and Social Aspects
Social Impacts - Higher potential of accidents
Source: Portland Department of Transportation(2005)

## Slide 44
Social Impacts – Longer Travel Time
Environmental and Social Aspects

## Slide 45
Action | Impact | Value | Mitigation measure | Responsibility
Construction |  |  |  | 
Road construction | Traffic delay | -1 | Work Off peak | contractor
 | noise | -3 | Through day time | contractor
 | dust | -2 | Use water and cover trucks | contractor
 | Construction Waste | -2 | Disposal plan to remove waste | Contractor and municipality
 | Pedestrian discomfort and harassment | -4 | Preamble radio programs and signs | Media and police
Road marking | Traffic delay | -3 | Preparing alternative routes | Police
 | Odor for workers | -1 | Wearing masks | Contractor
Operation |  |  |  | 
More Bicycles usage | Conflict between modes | -2 | Preparation for vehicle and bicycle drivers | Police and media
 | Higher potential of accidents | -1 | Preparation for vehicle and bicycle drivers | Media and organizations
 | Better health | +3 | - | -
 | More attractive mean of transportation | +2 | Enhancing agricultural | 
 | Tourism encouragement | +4 | Tour programs | Tourism center
Less numbers of cars | Reduce emissions | +2 | illustrating of results | Media
 | Less noise | +2 | - | -
 | Reduce fuel consumption | +4 | Illustrating the results | Media
 | Save money | +4 | Illustrating the total | Media
 | Slower traveling | -1 | Giving advantages for cyclists in movement | Police and Ministry
Different mean of transportation | New businesses in the city | +3 | Ease of establishment | Municipality
 | More guides required | +2 | Tourism interest | Municipality

## Slide 46
Summary Roads Network |  |  | 
No. | Item | Activity Performed | Cost ($)
1 | Total of Preliminaries | Mobilization | 15,000
2 | Total of Earth Works | Excavation, Remove of obstructs | 16,450
3 | Total of Sub Base and Base Course | Sub-Base, Base Coarse | 68,650
4 | Total of Bituminous Construction | Prime Coat, Binder | 120,135
5 | Total of Miscellaneous Works | Curbstone, Painting, Blocks | 438,265
 | Total Cost = 658,500 $ |  | 
Project Total Cost

## Slide 47
SUMMARY and
CONCLUSIONS

## Slide 48: Any Questions ?