## Slide 1: Graduation Project 2-68591/1 A comparative study between traditionally designed Residential Buildings (Al-Jenan Housing-Jenin) and a green building model
Prepared by:
Under the supervision of: Dr. Mutasem Babaa
Heba Amad
Mohammad Daraghma
Osaid Masri
Zaid Marmash

## Slide 2: Outline
Introduction.
Site analysis.
Architectural design.
Structural design.
Environmental design.
Electro mechanical design.
Comparing between traditional buildings and green buildings.
Al-Maqdisi Project.
Quantity survey & cost.

## Slide 3: Introduction
What is the idea of the project ?
What is the main objectives of the project ?

## Slide 4: Site analysis
Al-Jenan Housing is located at Jenin, Palestine.

## Slide 5: Topography & Area
The land has a slight slope (6% slope), the lowest point elevation is 65.5m and the highest point is 71.5m. The piece of land selected for the buildings has a total area of 1456 m2

## Slide 6: Architectural design

## Slide 7: Project program
Function | Area()
Guest room | 12.2
Dining room | 9.5
Living room | 16.4
Kitchen | 13
Bedroom 1 | 15
Bedroom 2 | 12.8
Master bedroom | 15.5
Master bathroom | 4.5
Bathroom | 4.8
Balcony | 3.6
Total | 107.3
Function | 
Guest room | 12.2
Dining room | 9.5
Living room | 16.4
Kitchen | 13
Bedroom 1 | 15
Bedroom 2 | 12.8
Master bedroom | 15.5
Master bathroom | 4.5
Bathroom | 4.8
Balcony | 3.6
Total | 107.3
The project has a total of three buildings, each building has four floors and a garage.
The total area for each floor is 250m which is divided into two apartments.

## Slide 8: Architectural plans
Site plan
Traditional design

## Slide 9: Architectural plans
Site plan
Green design

## Slide 10: Architectural plans
Garage

## Slide 11: Architectural plans
Master plan

## Slide 12: Architectural plans
Elevations
South elevation
North elevation

## Slide 13: Architectural plans
Elevations
East elevation
West elevation

## Slide 14: Architectural plans
Elevations
South elevation
North elevation

## Slide 15: Architectural plans
Elevations
East elevation
West elevation

## Slide 16: Architectural plans
Sections
Section A-A
Section B-B

## Slide 17: Architectural plans
3D model

## Slide 18: Architectural plans
3D model

## Slide 19: Architectural plans
3D model

## Slide 20: Architectural plans
3D model

## Slide 21: Structural Design
Codes & Standards:
    ACI -318-11 for reinforced concrete structural design.
    UBC -97 for earthquake design.
    ASCE 7 2010 for load combinations.

## Slide 22: Structural Design
Design data:
      Concrete strength for slabs and beams, f’c=24 mpa.
      Concrete strength for columns and shear walls ,f’c=28 mpa.
      Steel yield strength fy=420 mpa.
      Bearing capacity for soil =350 kN/m2.
      Live load= 2.5 (kN/m2).
      Super imposed dead load=4 (kN/m2).

## Slide 23: Structural Design
Lateral loads:
    The city of structure is Jenin.
    The seismic zone factor. Z=0.2.
    The soil profile is type Sc.
    The acceleration seismic coefficient Ca=0.24
    The velocity seismic coefficient Cv=0.32.
    The Seismic importance factor is 1.
    The structural design type is intermediate, R=5.5.

## Slide 24: Structural Design
Slab
25cm ribbed slab

## Slide 25: Structural Design
Beams layout

## Slide 26: Structural Design
Columns and footing layout

## Slide 27: Structural Design
Model

## Slide 28: Structural Design
Validity of ETABS model
There are three main checks that must be performed on the model before design, these are:
  Compatibility Check
  Equilibrium Check
  Internal forces check

## Slide 29: Structural Design
Compatibility Check
The compatibility of the structure is checked by making sure all the elements of the structure move together.
The check was OK.

## Slide 30: Structural Design
Equilibrium Check
The equilibrium check was performed by comparing the results of the base reactions from ETABS to the manual calculations.
 | ETABs results | Manual calculations | % error
Dead | 9322.07 | 9799.39 | 4.8%
Wall | 8242.58 | 7900.72 | 4.3%
SID | 7734.88 | 7692.56 | 0.55%
Live | 3170.03 | 3152.69 | 0.55%

## Slide 31: Structural Design
Internal forces check
The internal forces check is performed by comparing the results of manual and ETABS calculation for one column, beam and slab.
 | ETABs results | Manual calculations | % error
Column | 1351.66 | 1345.44 | 0.4%
Slab | 19.28 | 20.73 | 6.9%
Beam | 108.47 | 104.8 | 3.3%

## Slide 32: Structural Design
Slab reinforcement

## Slide 33: Structural Design
Beams reinforcement

## Slide 34: Structural Design
Beams reinforcement

## Slide 35: Structural Design
Columns reinforcement

## Slide 36: Structural Design
Columns reinforcement

## Slide 37: Structural Design
Footing reinforcement

## Slide 38: Structural Design
Footing reinforcement

## Slide 39: Structural Design
Water tank reinforcement

## Slide 40: Environmental Design
3D model for the traditional design.

## Slide 41: Environmental Design
3D model for the green design.

## Slide 42: Environmental Design
Passive solar techniques

## Slide 43: Environmental Design
Materials used in buildings
External wall
Traditional Green

## Slide 44: Environmental Design
Materials used in buildings
Internal slab
Traditional Green

## Slide 45: Environmental Design
Materials used in buildings
Flat roof
Traditional Green

## Slide 46: Environmental Design
Glass type
Traditional
Single clear glass (6mm).
No thermal break.
Green
Double low emittance clear glass (6mm/13mm).
Aluminum frame with thermal break.

## Slide 47: Environmental Design
Palestinian requirements |  | Green building |  | Traditional building | 
Element | Value | Value | Fit/Not | Value | Fit/Not
External walls | 0.5 w/m2.k | 0.481 | Fit | 1.982 | Not
External roof | 0.39 w/m2.k | 0.373 | Fit | 2.869 | Not
Internal floor | 0.46 w/m2.k | 0.426 | Fit | 1.811 | Not
Glass | 2.1 w/m2.k | 1.761 | Fit | 5.778 | Not

## Slide 48: Environmental Design
System loads (Wh/m2)

## Slide 49: Environmental Design
Thermal analysis
Electricity Intensity [kWh/m2] | District Cooling Intensity [kWh/m2] | District Heating Intensity [kWh/m2]
51.98 | 63.08 | 67.25

## Slide 50: Environmental Design
Thermal analysis
Electricity Intensity [kWh/m2] | District Cooling Intensity [kWh/m2] | District Heating Intensity [kWh/m2]
37.41 | 32.79 | 21.22

## Slide 51: Environmental Design

## Slide 52: Al-Maqdisi Project
Al-Rashid building
Is a five story traditional Palestinian residential building.
Located at Nablus city.

## Slide 53: Al-Maqdisi Project
Chart: 
| never | rarely | occasionally | quite often | very often
The day | 0.138 | 0 | 0.586 | 0.241 | 0.034
The night | 0.138 | 0 | 0.345 | 0.345 | 0.172
Chart: 
| never | rarely | occasionally | quite often | very often
The day | 0.029 | 0.059 | 0.353 | 0.353 | 0.206
The night | 0.059 | 0.176 | 0.382 | 0.235 | 0.147
Winter case
Autumn case

## Slide 54: Al-Maqdisi Project
Chart: 

## Slide 55: Al-Maqdisi Project
Chart: 

## Slide 56: Environmental Design
Daylight factor

## Slide 57: Environmental Design
Daylight factor
Appartment | Zone | Average daylight factor (%)
Appartment 1 | Master bedroom | 1.736
 | Bedroom1 | 3.192
 | Bedroom2 | 1.835
 | Living room | 2.936
 | Kitchen | 4.306
Appartment2 | Master bedroom | 1.648
 | Bedroom1 | 3.194
 | Bedroom2 | 1.895
 | Living room | 2.760
 | Kitchen | 4.252
Total | 2.758 | 

## Slide 58: Electro-Mechanical Design
Drainage system
Storm water.
Grey water.
Black water.

## Slide 59: Electro-Mechanical Design
Water distribution system
Cold water.
Hot water.
Grey water
(flush tanks).

## Slide 60: Electro-Mechanical Design
Water distribution system
 | Vertical | Horizontal | Meters | Branches
Diameter of pipes | 2 in | 1 in | 1 in | ½ in Critical ¾ in
We used for the last two floors auxiliary pumps 12,6 psi respectively.

## Slide 61: Electro-Mechanical Design
Water distribution system
Water tank.
Domestic hot water tank.
Grey water tank.

## Slide 62: Electro-Mechanical Design
Under floor system
Main heating system.
Evacuated tubes.
Boiler.

## Slide 63: Electro-Mechanical Design
VRF system

## Slide 64: Electro-Mechanical Design
VRF system
Zone | Max Design Capacity (Kw) | Ton Refrigerator Capacity (RT) | Capacity of indoor unit (RT)
Bedroom1 | 0.93 | 0.264441 | 0.5
Bedroom2 | 0.95 | 0.2701279 | 0.5
Master bedroom | 0.8 | 0.227476 | 0.5
Guest & living room | 1.5 | 0.426518 | 0.5
Dining room | 1.5 | 0.426518 | 0.5

## Slide 65: Electro-Mechanical Design
Sound Transmission Class.
 | Internal walls | External walls
Layers | 20 mm plaster board on lath | Stones 70 mm.
 | Hollow concrete block (thickness 140 mm) | Concrete 130 mm.
 |  | XPS Polystyrene 55 mm.
 | 20 mm plaster board on lath | Block 100 mm.
 |  | 20 mm plaster board.
STC value | 50 dB | 57 dB

## Slide 66: Electro-Mechanical Design
Photovoltaic system

## Slide 67: Electro-Mechanical Design
Photovoltaic system
19140 Wp can be produced per year.

## Slide 68: Electro-Mechanical Design
Artificial lighting
Type of room | Level of illuminance (lux)
Bedroom | 300 - 400 (Task)
Bathroom | 100 - 200
Dining room | 100 - 200
Guest room | 200 - 300
Living room | 200 - 300
Kitchen | 400 - 500
Corridor | 100 - 150
Balcony | 100 - 150
Stairs | 100 - 150

## Slide 69: Electro-Mechanical Design
Artificial lighting

## Slide 70: Electro-Mechanical Design
Artificial lighting

## Slide 71: Electro-Mechanical Design
Artificial lighting

## Slide 72: Electro-Mechanical Design
Sockets

## Slide 73: Electro-Mechanical Design
Sockets
Space | Single outlet (normal) | Special load
Kitchen | 4 | ---
Dining room | 2 | ---
Living room | 2 | 1
Guest room | 2 | 1
Master bedroom | 3 | 1
Master bathroom | 1 | ---
Bedroom | 3 | 1
Bathroom | 1 | 1
Bedroom | 3 | 1
Balcony | 1 | ---
Floor | No. of socket (2 A) | No. of socket (10 A) | No. of branches (3Ø2.5mm)
1st floor | 44 | 12 | 26
2nd floor | 44 | 12 | 26
3rd floor | 44 | 12 | 26
4th floor | 44 | 12 | 26

## Slide 74: Electro-Mechanical Design
Branches

## Slide 75: Quantity Survey and Cost
 | Total cost ($) | Unit cost ($/)
Excavation works | 10251 | 8.2
Civil works | 203071.68 | 162.5
Architectural works | 330718.71 | 264.6
Mechanical works | 107030 | 85.7
Electrical works | 63426 | 50.8
Total | 714497.39 $ | 571.8 $
 | Total cost ($) | 
Excavation works | 10251 | 8.2
Civil works | 203071.68 | 162.5
Architectural works | 330718.71 | 264.6
Mechanical works | 107030 | 85.7
Electrical works | 63426 | 50.8
Total | 714497.39 $ | 571.8 $