## Slide 1: Feasibility Study for Thermoforming Production Plant

## Slide 2: Introduction
Problem statement
The Palestinian market consumes yearly large quantities of different thermoformed plastic products like disposable dishes, cups, fruits and sweets containers; it is expected that the demand on such products is continuously increasing and exceeds the supply. However, almost all of these products are imported from outside Palestine and there are no considerable local producers. Such a problem can be solved by establishing a local thermoforming industry.

## Slide 3: Introduction
Objectives
    Conduct a proper and sufficient market study.
    Perform relevant technical study covering machinery, layout, etc.
    Perform the necessary financial analysis to judge on the feasibility of such industry.
    To support in providing Palestine Palestinian market with sufficient need of thermoforming products.
    To improve the project team skills in feasibility studies.

## Slide 4: Introduction
Scope of the work
The feasibility study consists mainly of market study, technical study and financial study as shown below

## Slide 5
Literature Review
There are two main subjects we studied about:
Thermoforming production process
How to prepare an industrial feasibility study

## Slide 6: Literature Review
Definition of thermoforming
Principle of thermoforming
Applications of thermoforming
Forming Processes
Thermoforming production process

## Slide 7: Literature Review
Definition of Industrial Feasibility study
Industrial Feasibility study Divisions:
Market study
Technical study
Financial study
Industrial Feasibility Study

## Slide 8: Methodology
Identified products
Containers and lids
Cups
Sweet Containers
Eggs containers

## Slide 9: Methodology
Production process
* Determine what process would be used to produce the identified products.
* Determine the raw materials which would be used.
* Study the dimensions of the production processes which were chosen.

## Slide 10: Methodology
Market
* Determine the volume of demand and the Market share of each product.
* Study the desires of customers according to the dimensions of the products.
* Study the cost of manufacturing and importing.
* Study the availability of raw material in the local market.

## Slide 11: Methodology
Data Collection Tools
a- Interviews
b- Questionnaires
* Supermarket Questionnaire
* Manufactures Questionnaire
* Importers Questionnaire

## Slide 12: Methodology
Technical Study
Defining Stages of Production processes
Main Equipment ,Machines and Row material needed for the factory
Facility Planning and Plant layout
Human resources needed and the organization structure of the factory
Facility location

## Slide 13: Methodology
Financial Study
Determines the Start-up Capital
Determines the Operational Cost
Financial Analysis for the factory
Determine Break-Even Quantities

## Slide 14: Results & Analysis
Importers and manufactures questionnaires analysis
Chart: الاستيراد مقابل التصنيع
| كمية الكاسات بالكرتونة / سنة | علب واغطية | علب الحلويات | الصحون
التصنيع | 474500 | 333900 | 62050 | 301700
الاستيراد | 794000 | 228500 | 30000 | 389000
Imported quantities vs. National quantities

## Slide 15: Results & Analysis
Chart: الكاسات
| التصنيع | الاستيراد
كمية الكاسات بالكرتونة / سنة | 474500 | 794000
Chart: 
| التصنيع | الاستيراد
الصحون | 301700 | 389000
Chart: 
| التصنيع | الاستيراد
علب الحلويات | 62050 | 30000
Chart: 
| التصنيع | الاستيراد
علب واغطية | 333900 | 228500
Market share for each product

## Slide 16: Results & Analysis
Production quantities for the identified product
Identified products quantities and market shares

## Slide 17: Results & Analysis
Main Equipment ,Machines and Row material needed for the factory
Thermoforming Production Machine
Products Molds
Crushing Machine
Sheets Extruder
Packaging Machine

## Slide 18: Results & Analysis
Facility Location
Main criteria used to choose the facility location
Closeness to customers
Closeness to the crossing borders
Competitive land price
Availability of manpower
The land belongs to Palestinian Authority ( classified as A region)
Area where the factory is located

## Slide 19: Results & Analysis
Human resources needed in the factory
Categories | Number
Manager | 1
Secretary | 1
quality control supervisor | 1
production line supervisor | 1
Technician for maintenance | 1
Accountant | 1
Stores supervisor | 1
Sales and Purchasing supervisor | 1
Marketing supervisor | 1
Workers | 5
Total | 13
Human Recourses needed in the factory

## Slide 20: Results & Analysis
Organization Structure of the factory

## Slide 21: Results & Analysis
Determines the Startup Capital Amounts
the startup capital consists of the following elements
Land Price
Construction Cost
Electricity Cost
Production Equipment cost
Water System cost
Products Mold Cost
Other Supportive Production Cost

## Slide 22: Results & Analysis
Determines the Operational Cost
the operational cost consists of the following elements
Row Material Cost
Energy Consumption Cost
Total Salaries
Depreciation Cost
Insurance Cost
Other Related Cost

## Slide 23: Results & Analysis
Financial Analysis for the factory
We Identified the total monthly production cost and then distributed it among
the identified product as shown in table below
Identified Product | Production Cost Proportion
Cups | 0.42
Cans and their Covers | 0.14
Sweet Containers | 0.02
Plates | 0.42

## Slide 24: Results & Analysis
Determine Unit Cost from each Product
We defined the unit as one cartoon for each product, so the unit cost
is equal to cost per cartoon
Total product cost per period = product proportion from the production cost + Raw Material Cost
Cost per Cartoon = Total Product cost / # of product produced per period
Net profit per cartoon
Gross Profit per cartoon = Cartoon Selling Price - Cost per Cartoon
Net Profit per Cartoon = Gross Profit per cartoon - Gross Profit per cartoon * Direct Tax

## Slide 25: Results & Analysis
Breakeven Quantities
we computed the total number of cartoons needed to be produced
from each product to achieve factory’s breakeven state by using the
below equation
Fixed cost assigned to the product – (profit per unit * # of units needed) = 0

## Slide 26: Results & Analysis
Project Evaluation
We used many criteria to evaluate the feasibility of the project which are :
Payback Period = Cost of Investment \ Annual Cash Flow
Cost of investment = Startup Capital Cost + Raw Material cost
Rate of Return = Annual Profit \ Cost of Investment
Net Present Value = ∑ {Net Period Cash Flow/ (1+R) ^T} - Initial Investment

## Slide 27: Results & Analysis
Sensitivity Analysis
We applied the sensitivity analysis on the increasing the market share
for each product vs the net profit as shown below
Chart: Market share Vs Cups and Plates profit
| 0.15 | 0.2 | 0.25 | 0.3 | 0.35 | 0.4 | 0.45 | 0.5
cups profit | 1019374.5 | 1359166 | 1698957.5 | 2038749 | 2378540.5 | 2718332 | 3058123.5 | 3397915
plates profit | 3685969.5 | 4914626 | 6143282.5 | 7371939 | 8600595.5 | 9829252 | 11057908.5 | 12286565
Chart: Market share Vs Cans and Sweet containers Profit
| 0.1 | 0.15 | 0.2 | 0.25 | 0.3 | 0.35 | 0.4 | 0.45 | 0.5
cans and their covers profit | 1231615 | 1847422.5 | 2463230 | 3079037.5 | 3694845 | 4310652.5 | 4926460 | 5542267.5 | 6158075
sweet containers profit | 189180 | 2161381.5 | 2881842 | 3602302.5 | 4322763 | 5043223.5 | 5763684 | 6484144.5 | 7204605

## Slide 28: Conclusions
There are two main sources for covering the west bank demand which are importing and manufacturing without appearance for importing form Israel
Breakeven quantity from the Cups, Cans and their Covers, Sweet Containers
and plates per month respectively equals to 6094 , 668, 101 and 1683 cartoons.
Annual profit from the identified products = 5,087,254 NIS
Rate of Return = 56.4 % which is an attractive return for an investor who is new in the market and for the investors who owns similar investments, is very acceptable rate

## Slide 29: Conclusions
Payback Period = 1.77 years , which is a short period and attractive to invest in this project
Net Present value equals to 6,292,704.78 NIS using interest rate = 2.30 % from the Housing Bank for Trade and Finance . The NPV represents a positive value, so this a good indicator of project’s profitability
Plant layout

## Slide 30: Recommendations
We recommends to construct the thermoforming factory in Tulkarem, at the main way of Balaa’ Town
To improve the factory market shares from each product after one year of construction
To import the specified raw material with its associated chemical characteristic to decrease the amount of scrap
To study of increase the variety of product in order to increase the factory market share.
To hire qualified employees to increase and improve the factory productivity