## Slide 2
Project Abstract :
The Concept : "HULK" is an integrated mechatronic system designed to bridge the gap between human intent and robotic execution through a natural gesture-controlled interface.
System Mechanism : The system utilizes a wearable smart glove equipped with resistive flex sensors to capture finger orientation, transmitting data wirelessly via Bluetooth to a robotic hand that replicates the movement in real-time.
Key Achievement: We successfully developed a low-cost, high-response system with a latency of less than 70-90ms, making it suitable for applications in prosthetics, hazardous environment handling, and teleoperation.

## Slide 3
Introduction
The Evolution of HMI: Human-Machine Interaction (HMI) has evolved from simple buttons to advanced touchscreens and now to natural gesture-based control.
Robotic Interaction: The challenge in robotics is to create a control system that feels like an extension of the human body.
Why a Robotic Hand? The human hand is one of the most complex tools; replicating its movement allows for high-precision tasks in various fields such as:
Prosthetics: Helping individuals with limb loss.
Hazardous Environments: Remote handling of dangerous materials.
Space & Deep Sea: Teleoperation where humans cannot go.

## Slide 4
Problem Statement & Objectives
The Problem:
*Complexity and high cost of traditional robotic control systems.
*Lack of intuitive "natural" interfaces for teleoperation and prosthetics.
*The need for high-precision feedback in remote handling.
Main Objectives:
Design & Build: Develop a functional 5-finger robotic hand using low-cost components.
Intuitive Control: Implement a wearable glove system that mirrors human hand gestures.
Wireless Integration: Establish a reliable, low-latency Bluetooth communication link.
Signal Optimization: Apply hardware and software filtering (RC circuits) to ensure smooth and stable movement.

## Slide 5
Hardware Components & Tools
1-
-4.5" Flex Sensors: Resistive sensors that change value based on finger bending.
-Voltage Divider Circuit: Using 22kΩ resistors to convert resistance to measurable voltage.
-RC Low-Pass Filter: 10µF capacitors to stabilize the signal and remove noise.

## Slide 6
Hardware Components & Tools
2-
Wireless Link :
HC-05 Bluetooth Modules: Operating in Master/Slave configuration at 38,400 bps.
Processing Unit :
2x Arduino Uno: High-performance, low-cost microcontrollers for data processing and PWM control.
3-

## Slide 7
Hardware Components & Tools
4-
Actuation & Power :
High-Torque Servos: For precise mechanical movement.
External Supply: 7.4V / 8.4V Li-ion battery

## Slide 8
System Methodology & Workflow
1-
Signal Acquisition (The Glove)
-Flex sensors detect finger bending
(Analog data).
-Arduino Uno processes the analog signals and converts them to digital values.
Signal Conditioning
Applying the RC Low-Pass Filter to eliminate mechanical noise and hand tremors.
Mapping the sensor values (0–1023) to Servo angles (0°–180°).
2-

## Slide 9
System Methodology & Workflow
3-
Wireless Transmission
-Data is packaged and sent via the HC-05 Master module.
-The HC-06 Slave receives the data and passes it to the main Processing Unit.
Execution (The Robotic Hand)
The Arduino Uno interprets the received angles.
PWM (Pulse Width Modulation) signals are sent to the High-Torque Servos to move the fingers accordingly.
4-

## Slide 10
Flow Chart

## Slide 11
Mechanical Design & 3D Printing
1-
3D Printing Specifications :
-Material: High-quality PLA for a lightweight yet rigid
-structure.Precision: Printed with specific tolerances to allow smooth joint rotation without mechanical friction.

## Slide 12
String-Driven Actuation:
-Direct control using High-Tension Nylon Strings connected to the servo horns.
-Each finger is actuated by a dedicated servo, allowing for independent and precise grasping movements.
2-
Mechanical Design & 3D Printing

## Slide 13
Budget & Resource Efficiency
Low-Cost Innovation: The total project cost was minimized by utilizing 3D printing and off-the-shelf hobbyist electronics
Cost-Benefit: While commercial gesture-controlled hands cost thousands of dollars, "HULK" achieves similar functionality at a fraction of the cost, making it accessible for educational and low-income prosthetic research
Sustainability: Use of PLA (Polylactic Acid) ensures the mechanical structure is biodegradable and environmentally friendly.
Gesture replication

## Slide 14
Future Work & Upgrading Possibilities
Muscle Sensors (EMG): Transitioning to Electromyography (EMG) sensors to detect small muscle electrical impulses for "hand-free" control instead of flex sensors
OpenCV Visual Operating: Implementing an OpenCV application to track pre-applied focusing points on a hand or object, executing robotic commands based on visual motion detection
Haptic Integration: Adding Force Sensitive Resistors (FSR) to allow the user to "feel" the robotic hand's grip pressure in real-time

## Slide 15
Testing Video :

## Slide 16
Thank You
Any Questions?