## Slide 1
An-Najah National University Faculty of Engineering Building Engineering Department
“ Design of Ramallah Municipality”
Supervisor : Eng. Hind Tbaileh
Prepared By:
Alaa Sawalha
Ahmad Othman
Ghaith Ismail
Waleed Salameh

## Slide 2: Contents:
Introduction
Site Description
Architectural Design
Structural Design
Environmental Design
Electro-mechanical Design
Fire fighting and Safety Design
Quantity survey and cost

## Slide 3: Introduction :
Our project present a design of Ramallah Municipality. The main objective is to design a municipality building that provides all services and comfort to employees and citizens taking into consideration the architectural, environmental, structural, and electro-mechanical aspects.

## Slide 4: Site Description:
The site for the project is in Ramallah city, located about 605.83 meter from the city center . (2 min by car)

## Slide 5: Architectural Design

## Slide 6: Building Description :
The Municipality Building has 5 floors
Basement , ground, first, second and third floor
The total area of municipality is 6400 m2, each floor has an area of 1280m2.

## Slide 7: Bubble Diagram:

## Slide 8
Old areas of floors
Total area : 3145 m2
Floor | Area(m2)
BS | 1280
GF | 1280
F1 | 1280
F2 | 1280
F3 | 1280
New areas of floors
Total area : 6400 m2

## Slide 11: Old Plans Of Municipality :
Basement floor
Ground floor

## Slide 12
First floor
Second floor

## Slide 13: Site Plan:
New Plans Of Municipality :

## Slide 14: Basement Floor:

## Slide 15:  Parking :
Old Parking of municipality

## Slide 16:  Parking :
New Parking of municipality

## Slide 17: Ground Floor:

## Slide 18: First Floor:

## Slide 19: Second Floor:

## Slide 20: Third Floor:

## Slide 21: East Elevation:

## Slide 22: West Elevation:

## Slide 23: North Elevation:

## Slide 24: South Elevation:

## Slide 25: Sections:

## Slide 26: Sec A-A

## Slide 27: Sec C-C

## Slide 28: 3D Model:

## Slide 29: 3D Model:

## Slide 30: 3D Model:
CSC Teller in GF

## Slide 31: 3D Model:
Offices in F1

## Slide 32: Structural design

## Slide 33: Building description
Consist of five floor

## Slide 34: Design codes
ACI -318-08 (American Concrete Institution) for reinforced concrete structural design.
UBC-97 (Uniform Building Code) for earthquake load computations.

## Slide 35: Materials property
Structural Item | Compressive Strength(Mpa)
Slab ,beams ,columns , shear walls | 28
MAT Foundation | 24
Structural Item | Yield strength(Mpa)
Steel | 420

## Slide 36: Building modeling:
Zone (1)
Zone(2)
Zone (3)

## Slide 37: Structural System
The system of the slab is tow way solid slab with drop beams
Beam girder system were used in zone(2)
Beam girder system

## Slide 38: Program inputs
Loads
modifiers
Type of load | Load KN/m2
Dead load | -----
SD load | 4
Live load | 4
Masonry wall | 6
Curtain walls | 0.6
Structural Item | Moment Modifier
slab | 0.25
beams | 0.35
columns | 0.001
Shear walls | 0.7

## Slide 39: Models checks:
Compatibility check
Equilibrium Checks
Internal forces checks
Deflection checks

## Slide 40: Compatibility check
Compatibility check for zone(2)

## Slide 41: Equilibrium Checks
Load type | ETABS(KN) | Manual(KN) | Error %
Dead load | 24195.8 | 23545.4 | 2.7
SD loud | 9928.5 | 10203.46 | 2.7
Live load | 5358.66 | 5358 | 0.01
Error % Doesn’t exceed 5 %
Dead load | 35080 | 35068.35 | 0
SD loud | 16034.6 | 15725.52 | 1.9
Live load | 11501.4 | 11502 | 0.01
Dead load | 24931.5 | 25276 | 1
SD loud | 13081.2 | 12811.6 | 2
Live load | 7178 | 7200 | 0.3
Zone
Zone(1)
Zone(2)
Zone(3)

## Slide 42: Internal forces checks
Slab | ETABS(KN.m) | Manual(KN.m) | Error %
Slab (1) | 100.25 | 95.6 | 4.6
Slab(2) | 20.2 | 19.7 | 2.5
Slab(3) | 45 | 41.8 | 7.6
Beam | ETABS(KN.m) | Manual(KN.m) | Error %
Beam(1) | 1266.1 | 1290 | 1.8
Beam(7) | 1057.5 | 1027 | 2.9
Beam(16) | 492.8 | 497.4 | 1
column | ETABS(KN) | Manual(KN) | Error %
Column(1) | 1123 | 1102.3 | 1.8
Column(2) | 846 | 805 | 5
Column(3) | 586.2 | 588.2 | 0.3
Error % Doesn’t exceed 10 %

## Slide 43: Deflection checks
Zone | Max. deflection allowed | Max. deflection by ETABS
Zone(1) | 25.75 mm | 25 mm
Zone(2) | 47.7 mm | 40 mm
Zone(3) | 21.83 mm | 21.2 mm

## Slide 44: Seismic design
Period Check
Modal Mass Participation Ratios (MMPR)
Base Shear Check
Drift Check

## Slide 45: Seismic design data
Seismic zone is 2A (Z=0.15) because the building is on Ramallah
Importance factor I=1
Force reduction factor (R) =5.5 (Building Frame System- Shear Walls)
Soil profiles in the project is (SD).
Acceleration-dependent seismic coefficients, Ca=0.22
Velocity-dependent seismic coefficients, Cv= 0.32

## Slide 46: Period Check:
T=Ct*(hn)3/4 = 0.478 sec.
Zone | Max Period allowed | Period by ETABS
Zone(1) | 0.478 sec | 0.383 sec
Zone(2) | 0.478 sec | 0.462 sec
Zone(3) | 0.478 sec | 0.444 sec

## Slide 47: Modal Mass Participation Ratios (MMPR)
Zone (1)
Zone (2)
Zone (3)

## Slide 48: Base Shear Check
Zone | Weight (1D+1/4L) | Base shear
Zone(1) | 35420.4 KN | 3542 KN
Zone(2) | 53990 KN | 5399 KN
Zone(3) | 41724.4 KN | 4173 KN

## Slide 49: Drift Check
Zone | story | ΔSy(mm) | ΔSx(mm) | Δmy (mm) | Δmx(mm)
Zone(1) | Story(1) | 0.28 | 3.43 | 1.1 | 13.2
 | Story(5) |  |  |  | 
Zone(2) | Story(1) | 17.3 | 14.29 | 66.6 | 55.7
 | Story(5) |  |  |  | 
Zone(3) | Story(1) | 12.4 | 11.87 | 47.74 | 45.5
 | Story(5) |  |  |  | 
Δmy and Δmx less than 100mm

## Slide 50: Slab Design

## Slide 51: Beams Design

## Slide 52: Columns Design

## Slide 53: Shear Walls Design

## Slide 54: Stairs design

## Slide 55: Mat Foundation Design:
Bearing capacity for soil (Qall) = 200 KN/m2
Thickness = 100cm

## Slide 56
Environmental Design

## Slide 57: Environmental design

## Slide 58: In this phase of project, full analysis has been made using Design Builder program for simulation.

## Slide 59: Environmental Design Analysis
Material used.
Shading Effect Analysis
Site and Building Thermal Analysis

## Slide 60: Material Used – External Wall
5 cm Lime Stone.
10 cm Cast Concrete.
5 cm Extruded Polystyrene
10 cm Concrete Block.
1 cm Cement Plaster.

## Slide 61: Material Used – Roof (Out)
0.45 cm Roofing asphalt
4 cm cast concrete.
8 cm concrete.
17 cm light weight concrete block.
2 cm cement plaster.

## Slide 62: Material Used – Internal Floor
3 cm Terrazzo tile.
3 cm mortar.
7 cm sand and gravel.
30 cm concrete.
2 cm cements plaster.

## Slide 63
Material Used – Internal Partitions
2 cm cements plaster.
10 concrete block
2 cm cements plaster.

## Slide 64
Dbl LoE (e2=.1) Clr 6mm/13mm Arg Glass

## Slide 65
Through the use of Design Builder program and after checking the North direction.
Sun effect on the building 21-june (12pm)

## Slide 66
Sun effect on the building 21-Jan (12pm)

## Slide 67
Site & Building Thermal Analysis
Using Design Builder.

## Slide 68
Design Builder Parameters.
HAVC System : VRF Units.
Fuel is Electricity from Grid.
System is used for Heating & Cooling.
Building is used from 8:00 AM to 2:00 PM.

## Slide 73
Total net site energy after improvements were made increased as shown in the following table 64.3 kWh/m2
Environmental design

## Slide 74
Net not comfort hours in the building before improvements =1766.00 hr
Net not comfort hours in the building after improvements = 2111 hr
Environmental design

## Slide 75: Electrical Design

## Slide 80
Circuit Breakers

## Slide 81
G.F Floor D.B

## Slide 82
1st Floor D.B

## Slide 83
2nd Floor D.B

## Slide 84
3rd Floor D.B

## Slide 86: Electrical Design
Ground floor lighting plan

## Slide 87: Electrical Design
Luminaries used in the ground floor

## Slide 88: Electrical Design
3D rendering view for selected rooms
Office

## Slide 89: Electrical Design
3D rendering view for selected rooms
Meeting room

## Slide 90: Electrical Design
3D rendering view for selected rooms
Resturant

## Slide 91: Acoustical Design

## Slide 92: Reverberation time(RT60):
Values for materials used in the rooms

## Slide 93
Reverberation time "RT60" calculations for meeting room and office using Ecotect programme
Meeting room: Volume: 180.45 m³. Surface Area: 197.229 m². Assume the room full capacity of occupants = 120 person.
From the table shown ,the allowable RT60 value for meeting rooms range between (0.4 – 0.7)s and RT60 at deferent frequencies and capacity range is between (0.39 – 1.27)s
also The room has a poor RT60 at the high and low frequencies, because the RT60 at low frequency is more than 0.7, and at the high frequency it is less than 0.4.

## Slide 94
Office Volume: 44.300 m³. Surface Area: 78.140 m². # of occupants = 4
The allowable RT60 value for Office range between (0.7- 1.3)s Room RT60 at deferent frequency and capacity range between (0.20 – 0.75)s The room has poor RT60 at high frequency because the RT60 at the high frequency is less than 0.75

## Slide 95: Sound Transmission Loss (STC):

## Slide 96
For Director room adjacent to Secretary office

## Slide 97: IIC For Ceiling
IIC = 70 dB

## Slide 98: Mechanical Design

## Slide 99: Mechanical Design
Fixture units and collector,Zone 1
Water Supply :

## Slide 100
Fixture units and collector,Zone 2

## Slide 101
Fixture units and collector,Zone 3

## Slide 102
Water demand = 13771.2 litre /week.
Old number of tanks = 13
New number of tanks = 18
Total number of fixture unit for building = 392 F.U.(old 178)
Mechanical design

## Slide 103: Mechanical design
Water drainage system : -
Main drainage line from municipality

## Slide 104: Mechanical design
Water drainage system : -
Drainage system in bathrooms and kitchens is as shown

## Slide 105: Mechanical design
Distribution of tanks on the roof

## Slide 106: Mechanical design
Drainage of rain water
Rain water tank size = 80 m3

## Slide 107: Mechanical design
Sanitation system : -

## Slide 108: Mechanical design
HVAC system design
VRF system was used in the municipality building , the outdoor units specifications is as shown
Total cooling load = 145 kw
Total heating load = 85 kw

## Slide 109: Mechanical design
HVAC system design
specifications of fan coil used is as shown

## Slide 110: Mechanical design
HVAC system design
Ground floor HVAC system layout

## Slide 111: Mechanical design
HVAC system design
First floor HVAC system layout

## Slide 112: Firefighting and Safety Design

## Slide 113: Firefighting and Safety Design
Fire fighting sprinklers system that used in the basement floor

## Slide 114: Firefighting and Safety Design
Fire fighting suspended automatic fire extinguisher CO2 that used in the ground floor

## Slide 115: Firefighting and Safety Design
Fire fighting suspended automatic fire extinguisher CO2 that used in the first floor

## Slide 116: Firefighting and Safety Design
Fire fighting suspended automatic fire extinguisher CO2 that used in second floor

## Slide 117: Firefighting and Safety Design
Fire fighting suspended automatic fire extinguisher CO2 that used in third floor

## Slide 118: Firefighting and Safety Design
Escape and Evacuation plans

## Slide 119: Firefighting and Safety Design
Escape and Evacuation plans

## Slide 120: Firefighting and Safety Design
Escape and Evacuation plans

## Slide 121: Firefighting and Safety Design
Escape and Evacuation plans

## Slide 122: Quantity Surveying and Cost Estimation

## Slide 123
Ramallah Municipality | Total Direct Cost (Nis)
Structure work | 583,521 ILS
Mechanical Work | 5,493,632 ILS
Finishing Work | 707,630 ILS
Electrical Work | 448,000 ILS
Total direct project cost | 12,958,745 ILS
Unit Direct Cost =12,958,745 ILS
/ 7822 = 1657 Nis /m2
Unit Direct Cost = 326 JD /m2

## Slide 124: “Thank You”