## Slide 1: Current monitoring by magnetic field sensing for overhead High voltage transmission lines (HVTL)
Submitted by: Tasneem Yacoub
Supervisor: Ms. Khadija Mayyaleh
Presented in partial fulfillment of the requirements for Bachelor degree in Electrical Engineering
An-Najah National University
Faculty of Engineering and Information Technology
Electrical Engineering Department

## Slide 2: Outline
Introduction.
Project idea.
Methodology.
Conclusion.
Recommendations

## Slide 3: Introduction
Every day the demand for having and delivering more power has been increased, but many faults in overhead transmission lines (HVTL) may occur due to environmental conditions, so monitoring the parameters like current over these lines become so important to detect the problem rapidly and solve it.
So monitoring current by magnetic field sensing is important and recommended because it solves traditional problems for the current transformers and it reduces workers' direct contact with live lines greatly.
At present, several techniques and devices are used for monitoring some parameters of the transmission lines. For phase currents they measured by current transformers (CTs), but they have problems. So non-connect transmission line current monitoring is recommended.
Using mobile as a sensor

## Slide 4: Project idea
Based on the Biot–Savart law, the distribution of emanated magnetic field from the phase currents can be determine from the phase current and the source positions. Therefor it is possible to determine the currents of the conductors inversely by measuring the emanated magnetic field.
In this work, a method devised to estimate the current in the conductors in each of them by mobile magnetometer installed on the tower will be presented.

## Slide 5: Magnetic field generated by sagging overhead transmission lines
For the three phase of HVTL the magnetic field radiated from each of the conductors is governed by the Biot–Savart law and catenary equation.
Biot-Savart low =
The catenary equation
mechanical parameter = W/H
The magnetic field vector at a point is + +
As of linearity of Biot–Savart law, we can apply the superposition principle to generalize the equations and calculate the magnetic field vector with j number of conductors and i number of sensing point
The product of and A can be denoted as position matrix P so we can write
Bi = P * Ij
And the inverse current reconstruction problem becomes
Ij = P-1 * Bi

## Slide 6: The magnetic field sensor in mobile
A magnetic sensor is a sensing chip that has a magnetoresistive element. sense in the magnetic vector for detecting the behavior of magnetic body that is based on a variation of the resistance value of the magnetoresistive component.
A magnetic field sensor (also known as magnetometer) reports the ambient magnetic field, as measured along the three sensor axes x, y, z.
This sensor can read a magnetic field within microTesla.

## Slide 7: Block diagram of the hardware system

## Slide 8: Current and sag reconstruction (one execution time) flow chart

## Slide 9: Current and sag reconstruction (run-time) flow chart
Restore new
By1, By2, By3

## Slide 10: Hardware system

## Slide 11: Three phase system with mobile application
A three-phase system in power lab was used and by create a mobile application using Android studio
the Earth’s magnetic field remains constant at a point in space.

## Slide 12: Results of three phase system
The measured current for the three phases was 2.5 A for each phase, the reconstructed current for the three phases shown in the following figures:-
The error in the reconstructed current here = 7.7%
Chart: Time
| 0.01 | 0.02 | 0.03 | 0.04 | 0.05
recunstructed current | -1.2398 | -2.379 | 2.2795 | -2.3779 | 2.2917
Current phase A | -0.51684 | -2.5776 | 2.5651 | -2.5863 | 2.1579

## Slide 13: Results of three phase system
The measured current for the three phases was 2.5 A for each phase, the reconstructed current for the three phases shown in the following figures:-
The error in the reconstructed current here = 11.5%
Chart: Time
| 8.0000000000000002E-3 | 1.4999999999999999E-2 | 0.02 | 2.8000000000000001E-2 | 3.5000000000000003E-2
Recunstructed current | -0.48194 | -2.4053 | 2.381 | -3.0128 | 2.5107
Current phase B | -0.51684 | -2.5776 | 2.5651 | -2.5863 | 2.1579

## Slide 14: Results of three phase system
The measured current for the three phases was 2.5 A for each phase, the reconstructed current for the three phases shown in the following figures:-
The error in the reconstructed current here = 5.1%
Chart: Time
| 5.0000000000000001E-3 | 6.0000000000000001E-3 | 1.2E-2 | 1.7000000000000001E-2 | 2.5000000000000001E-2
Recunstructed current | 0.025221 | 0.39075 | 2.2563 | -2.3315 | 0.98968
Current phase C | 0 | 0.51978 | 2.3776 | -2.3776 | 1.0168

## Slide 15: Single phase system with Matlab mobile application
A Single-phase system with three conductor feed three different devices (heater, Washer, Dishwasher) was used with Matlab mobile application: -

## Slide 16: Single phase system with Matlab mobile application
The data from the sensor then saved on the Matlab drive: -

## Slide 17: Single phase system with Matlab mobile application
The reconstruct the current for the heater.
The measured current of the heater is about 6.5 A
The error in the reading = 7.69 %

## Slide 18: Error causes
Error in the reading of the mobile sensor.
The nearby magnetic fields like: - ground magnetic field, magnetic field of devices, etc.
The main problem is the sample frequency, since in the build application the max sample frequency can be used = 100 Hz, and that affect the samples used to recontract the current a lot.

## Slide 19: Tri-axis TMR sensor and magnetometer of mobile phone
The results that we got can be better if we use the Tri-axis TMR sensor and that for some reasons: -
The sample rate of the magnetometer of mobile phone = 100 Hz, but the Tri-axis TMR sensor sampling frequency is 1 MHz. that make the reading from the sensor more accurate.
The Tri-axis TMR has high sensitivity of 10 nT, but the sensitivity magnetometer of mobile phone is 1 microTesla.

## Slide 20: Conclusion
At the end of this research and studying the estimation of current with a sensor array with mobile as sensors equal to number of conductors, placed at support tower and with the modeled system, it shows that this technique can be used to reconstruct the current, with an error due to a small sample rate used in the mobile application. The necessity of applying it on the ground to reap the benefits desired from it, since the current and sag monitoring prevents direct communication with the network and helps to monitor the network and discover network errors as soon as they occur.

## Slide 21: Recommendation
One of the most important work is to locate the fault in the network using magnetic field sensing.
Using the same idea to monitor the current under different conditions such as wind and snow

## Slide 22: The End
Thanks' for your listening