## Slide 1: SPEED SweepUp Stairs
- Jood Hamdallah & Saleh Sawalha
- Dr.Manar Qamhieh

## Slide 2: Why Speed ?
Never done before.
Climbing the stairs pattern .
Sweeping the stairs

## Slide 3: Table of contents 01 04 02 03
Technique & Movement
Challenges & Design
Constraints
Future work

## Slide 4: Technique & Movement 01

## Slide 5
Part A
Main part
Part B

## Slide 6: Camera
OAK-d Full HD Camera
The camera is connected with raspberry pi 4 model B .
Using AI Model for stairs detection.

## Slide 7: Movement steps
Moving
forward
1st step
2nd step
Moving
Part A up
3rd step
Moving Main part up
4th step
Moving
right & left
5th step
Moving
Part B up

## Slide 8: Moving forward
Stepper & DC motors are used for moving forward.
Navigation System: Limit Switches, IR sensors, & Camera were implemented to detect stairs.
01

## Slide 9: Moving Part A up
If ( 2 Limit Switches Pressed) {
While (Height != 19 cm) {
Part A UP
}
}
A
02

## Slide 10: Moving forward
Move forward again until all of
Part A is on the first stair.
03

## Slide 11: Moving main part up
Parts A & B moving down to
raise the main part.
Part A back to the same position
Part B goes down until reach the
Limit switch
A
B
04

## Slide 12: Moving forward
After the last move forward,
the two parts that responsible
for sweeping will be on the
first stair.
05

## Slide 13: Moving right & left
At this stage the robot starts
moving right and left to sweep
the stairs.
The robot toggles the direction
in two cases: if one of the two
switches is hit or the IR
did not detect object
06

## Slide 14: Moving Part B up
At this stage all the parts of
the robot are on the first stair.
B
07

## Slide 15: 02 Challenges & Design

## Slide 16: First challenge:
Limit of stair width
Vertical design
Bi-directional wheels
Up and down movement

## Slide 17: Vertical design
35cm
Drivers
Micro Controllers
Motors
57cm

## Slide 18: Bi-directional wheels
Difficult to turn wheels on stairs.
Using the OMNI wheels.
Main base of the robot speed.

## Slide 19: Up & down movement
Two Nema 23 connected with lead screw
Lead screws connected with both parts A & B
Part A & B connected to main part with sliders

## Slide 20: Second challenge:
Cleaning

## Slide 21: 03
Constraints

## Slide 22: Constraints
Cost Limitations
High Power Consumption
Heavy Weight

## Slide 23: Future work 04

## Slide 24: Future work
Smart Stair Navigation
Enhancing Cleaning System
Self-Emptying and Maintenance Features
Advanced AI Model for Obstacle Avoidance & Stair Recognition

## Slide 25: Thanks!
Do you have any questions?
Speed wake up we finished ! !
💤💤💤💤