## Slide 1: Graduation Project 2 Structural Analysis and Design of Optical and Nursing College
Under Supervision of:
Eng. Abdalhakeem Aljawhari MSc,CE

## Slide 2
Prepared By :-
Adel
Abdalhi
Basel
Nassar
Mohammad
Diab
Tareq
Ziad

## Slide 3
Project Description
The Optical and Nursing College building area covers about 1240 m2 which is located in Najah University new campus – Palestine next to faculty of medicine. The total building height is 28.3 m. The building consists of seven floors, and has two entrances with deferent levels.

## Slide 4
Site and geology
Qall=350 Kn/m2
Friction angle (ɸ) = 300
Specific weight (ɣ) = 18 Kn/m3
Type of soil is Loosing Rock
It is recommended to consider isolated and/or continuous footings.

## Slide 5
1
2
3
A 3D model will be constructed and analyzed using ETABS 2016 program taking into consideration the effects of dynamic Loads.
Columns and Beams will be represented as line elements
Slabs and shear walls will be modeled as area elements.
4
5
The connections between the footings and the column necks will be represented as pin connections.
Ultimate design method will be used for analyzing the structure.
  Design philosophy

## Slide 6
Dead load
Superimposed dead load
Masonry loads on the shear walls.
Water loads on tanks
Soil load
Live loads
Earth Quick loads
Loading

## Slide 7
  Computer programs:
ETABS 2016 was used to analyze and design the structural elements.
AutoCAD Was used for Structural detailing.
Safe 2016 was used for Design Footing.
Sap2000 was used for Design Stairs.
ETABS 2016 was used for Design Water Tank.

## Slide 8
Dimensions of structural element were used in project :
Slab:
Tow way solid slab 20 cm
Beams:
B400*400 (Width * Depth)
B450*700 (Width * Depth)
Shear Wall:
S 25 cm ( Thickness)
S 20 cm ( Thickness)
Column:
G1 (350 *450 )
G2 (400*500 )
G3 (500*600 )
G4 (400*400 )

## Slide 9
LATERAL LOADS
According to Palestine seismic map in figure and the project location, seismic zone is 2B.
→ Z=0.2 UBC (97) - TABLE 16-I
Site Soil Classification is Sc UBC(97) - TABLE 16-J
Weight of structure:
The effective seismic weight:
W=Wdead+Wsd+0.25W live

## Slide 10
LATERAL LOADS
Determination of structure period:
Using Reloph Method to calculate the period of structure:
Assume 1 kN/m2 as Earth Quick in x direction distributed in each floor.

## Slide 11
LATERAL LOADS
Determinations of base shear using static lateral force procedure:

## Slide 12
LATERAL LOADS
Determinations of base shear using static lateral force procedure:

## Slide 13
LATERAL LOADS
Horizontal force in each floor from equation 30-15-UBC:-

## Slide 14
LATERAL LOADS
Response spectrum that is defined in UBC-97
Response spectrum is an elastic response spectrum for 5 percent equivalent viscous damping used to represent the dynamic effects of the Design Basis Ground Motion for the design of structures.

## Slide 15
LATERAL LOADS
The center of mass and center of rigidity
An eccentricity equal to 0.25L is acceptable by the code, where L is the total length of the structure at the eccentricity direction.:
values of eccentricity is small than 0.05L for each direction
= 0.05 * 40 = 2

## Slide 16
THREE DIMENSIONAL STRUCTURE ANALYSIS
The modeling starts with building each block using ETABS 2016 by first defines: materials, sections as one-dimensional elements (columns and beams) and two-dimensional elements (slabs and shear walls), and loads (gravity and lateral loads), then draws each element relative to specific grid system on ETABS 2016.

## Slide 17
THREE DIMENSIONAL STRUCTURE ANALYSIS
Loads on ETABS
Load pattern

## Slide 18
THREE DIMENSIONAL STRUCTURE ANALYSIS
Seismic load:
UBC code was used to define the load using equivalent static method and response spectrum and figure 4.14 shows the definition for UBC-97.

## Slide 19
THREE DIMENSIONAL STRUCTURE ANALYSIS
Load Combinations:

## Slide 20
THREE DIMENSIONAL STRUCTURE ANALYSIS
mass source
Definition of response spectrum function

## Slide 21
THREE DIMENSIONAL STRUCTURE ANALYSIS
Definition of load cases for response spectrum

## Slide 22
Verifications of structural analysis
Strength check
Columns and beams should be checked for shear and torsion. In addition, for columns refer to ACI-318M-11 should be between 1% and 8%but for practical and economic consideration, for Beams ρ is recommended to be less than for singly.
After run and design of the structure, there were no red elements, so there were not any shear or torsion problems that would cause the elements to be over stressed.

## Slide 23
Verifications of structural analysis
Drawing structural model check

## Slide 24
Verifications of structural analysis
Drawing structural model check

## Slide 25
Verifications of structural analysis
Compatibility of structural model
By making start animation for the deformed shape of ETABS model, it can be noticed that the structural elements are compatible and all of them are moving together. Figure 4.20 shows the deformed shape.

## Slide 26
Verifications of structural analysis
Equilibrium

## Slide 27
Verifications of structural analysis
Equilibrium

## Slide 28
Verifications of structural analysis
Lateral loads check
Periods:
For maximum displacement in X-direction, 𝑈𝑋 = 0.67 mm, 𝑇𝐸𝑇𝐴𝐵𝑆,𝑋 = 0.235 sec For maximum displacement in Y-direction, 𝑈𝑌 = 0.79 mm, 𝑇𝐸𝑇𝐴𝐵𝑆,𝑌 = 0.202 sec From Chapter 2, period from hand calculation, 𝑇ℎ𝑎𝑛𝑑 = 0.29 sec
𝑇𝐸𝑇𝐴𝐵𝑆,𝑋 = 0.235 sec < 1.4×𝑇ℎ𝑎𝑛𝑑
𝑇𝐸𝑇𝐴𝐵𝑆,𝑌 = 0.202 sec < 1.4×𝑇ℎ𝑎𝑛𝑑

## Slide 29
Verifications of structural analysis
Lateral loads check
Seismic load check

## Slide 30
Verifications of structural analysis
Stiffness irregularity – soft story:

## Slide 31
Verifications of structural analysis
Weight (mass) irregularity

## Slide 32
Verifications of structural analysis

## Slide 33
Verifications of structural analysis

## Slide 34
Verifications of structural analysis

## Slide 35
Verifications of structural analysis

## Slide 36
Verifications of structural analysis
Stress Strain relationship (internal equilibrium)

## Slide 37
Verifications of structural analysis
Stress Strain relationship (internal equilibrium)

## Slide 38
Verifications of structural analysis
Check slab for deflection :

## Slide 39
Verifications of structural analysis
Story drift:
∆𝑆 for story 1 = 0.000481 m
∆𝑀= 0.7 × 5.5 × 0.000481 = 0.00185 m
𝑇𝑋 = 0.235 sec < 0.7 sec
0.025𝐻 = 0.025 × 5 = 0.125 m
∆𝑀= 0.00185 m < 0.025𝐻 = 0.125 m → OK
∆𝑆,𝑚𝑎𝑥 for remaining stories = 0.000844 m
∆𝑀= 0.7 × 5.5 × 0.000844 = 0.00325 m
0.025𝐻 = 0.025 × 4 = 0.1 m
∆𝑀= 0.00325 m < 0.025𝐻 = 0.1 m → OK

## Slide 40
Design of Slab
Assume slab thickness equal 20 cm.
Assume beams of continues spans to be 400 mm width and to have thickness of 400 mm

## Slide 41
Design of Slab
Wide-beam shear check
From Safe, max Vu = 77 kN ,as shown in figure.
Ok

## Slide 42
Design of Slab
Wide-beam shear check
Ok

## Slide 43
Design of Slab
Design the slab for flexure

## Slide 44
Design of Beams
.
Design of Beam for flexure

## Slide 45
Design of Beams
These rules were followed in shear design of beams for intermediate resisting frames case.
.

## Slide 46
Design of Beams
.
Design of Beam for shear force

## Slide 47
Design of Beams
.
Summary of beams group design

## Slide 48
Design of Columns
.
Slenderness check for the columns
No slenderness in the column, and can be classified as short column

## Slide 49
Design of Columns
.
Ok

## Slide 50
Design of Columns
.

## Slide 51
Design of Columns
.
The following rules are followed in shear design of columns for intermediate resisting frame case.

## Slide 52
Design of Columns
.
summary of columns

## Slide 53
Foundation Design.
.
Expected value | Soil Property
350 KN/(m^2) | Bearing Capacity
18 KN/(m^3) | Specific weight (ɣ)
30 degree | Friction angle (Ø)
……. | Stiffness factor for soil (K)

## Slide 54
Footing layout .
.

## Slide 55
Footing table.
.
Footing Num | Reinforced concrete |  |  | Blinding concrete |  |  | Bottom Reinforcement in Both Direction(mm) | Top Reinforcement in Both Direction(mm)
 | L(m) | B(m) | H(m) | L(m) | B(m) | H(m) |  | 
F1 | 1.80 | 1.80 | 0.4 | 2.0 | 2.0 | 0.5 | Ф14@150mm | ф12@250mm
F2 | 2.00 | 2.00 | 0.5 | 2.20 | 2.20 | 0.6 | Ф14@150mm | ф12@250mm
F3 | 1.70 | 1.70 | 0.4 | 1.90 | 1.90 | 0.5 | ф14@150mm | ф12@250mm
F4 | 1.50 | 1.50 | 0.4 | 1.70 | 1.70 | 0.5 | ф14@150mm | ф12@250mm
F5 | 2.20 | 2.20 | 0.5 | 2.40 | 2.40 | 0.6 | ф16@150mm | ф12@250mm
F6 | 4.00 | 4.00 | 0.5 | 4.20 | 4.20 | 0.6 | ф14@150mm | Ф14@150mm
F7 | 1.20 | 1.20 | 0.4 | 1.40 | 1.40 | 0.5 | Ф14@150mm | ф12@250mm

## Slide 56
Footing analysis.
.
Ultimate and surfaces loads on footing.
Pu(KN) | Ps(KN) | Footing num
Pu=1375 | Ps=1054 | F1
Pu=1726 | Ps=1313.4 | F2
Pu=1408 | Ps=1005 | F3
Pu=971 | Ps=700 | F4
Pu=2118.5 | Ps=1611 | F5

## Slide 57
Footing analysis.
.

## Slide 58
Footing analysis.
.

## Slide 59
Footing analysis.
.

## Slide 60
Footing analysis.
.

## Slide 61
Footing design.
.

## Slide 62
Footing detailing .
.

## Slide 63
Combined footing:
.
Footing Num | Reinforced concrete |  |  | Blinding concrete |  |  | R.Bottom Short (mm) | R.Bottom Long(mm) | R.Top Short(mm) | R.Top Long(mm)
 | L(m) | b(m) | h(m) | L(m) | b(m) | h(m) |  |  |  | 
CF1 | 4.2 | 3.3 | 0.7 | 4.4 | 3.5 | 0.8 | Ф16@150 | Ф16@150 | Ф16@150 | Ф16@150

## Slide 64
Deflection check.
.

## Slide 65
Stress check.
.

## Slide 66
Punching check:
.

## Slide 67
Combined footing design :
.

## Slide 68
Combined footing design :
.

## Slide 69
Combined footing design :
.

## Slide 70
Detailing of Combined footing :
.

## Slide 71
Detailing of Combined footing :
.

## Slide 72
wall footing design :
.

## Slide 73
Deflection check:
.

## Slide 74
Stress check:
.

## Slide 75
Design of wall footing:
.
long steel
1ф14/150mm

## Slide 76
Detailing of wall footing:
.

## Slide 77
Design of Stairs
.

## Slide 78
Design of Stairs
.

## Slide 79
Design of Stairs
.

## Slide 80
Design of Stairs
.

## Slide 81
Design of Stairs
.
  Design for flexural:

## Slide 82
Design of Stairs
.
  Design for flexural:

## Slide 83
Design of Water Tank
.
We assume dimensions for tank 6m × 6m × 4m
So L/h= 6/4 = 1.5 between (1-2), it’s considered as median tank.
Allowable stress below the base is 350 KN/m2 And fc assumed 45 Mpa and fy=420 Mpa
four 3D model were made for the base ,roof and walls on ETAB with this dimensions.
1) First one : soil without roof
2) Second one: soil with roof
3) Third one : water without roof
4) Fourth one : water with roof

## Slide 84
Design of Water Tank
.
Thickness of water tank:
Thickness of wall = 30 cm
Thickness of base= 35 cm
Thickness of roof = 20 cm

## Slide 85
Design of Water Tank
.

## Slide 86
Design of Water Tank
.
Vertical steel on the middle region from water and soil.
We display M22 and read the max moment. It is shown in the figure below.

## Slide 87
Design of Water Tank
.

## Slide 88
Design of Water Tank
.
Mu = 50 KN.m
ρ = 0.001<0.0033
As =0.00333 *1000*280=924mm2
(5Φ16/m) (1Φ16/200 mm)
Shrinkage steel in the transverse direction of main steel
Asmin= 0.0018*1000*350=636mm2 (6Φ12/1Φ12/ m) (mm)
Mu = 16 KN.m
ρ = 0.0022<0.0033
As =0.00333 *1000*175=577.5mm2
(5Φ12/m) (1Φ12/200 mm)
Shrinkage steel in the transverse direction of main steel
Asmin= 0.0018*1000*200 = 360mm2(5Φ12/m) (1Φ12/200 mm)

## Slide 89
Design of Water Tank
.

## Slide 90
Design of Shear Wall
.
Walls loads will be taken from ETABS and designed manually.

## Slide 91
Design of Shear Wall
.

## Slide 92
Design of Shear Wall
.
check result from ETABS

## Slide 93
Design of Shear Wall
.

## Slide 94
Design of Shear Wall
.

## Slide 95
Design of Shear Wall
.
summary of shear wall

## Slide 96
.