## Slide 1
3D Seismic Design Of Ahmad Odeh Hotel
Prepared By : - Yasmeen Bsharat
- Abeer Saleh
Under Supervision of: Dr. Abdul Razzaq Touqan
2016-2017

## Slide 2
Outline
1 Project description.
2 Seismic Design Parameters .
3 Structural System Type.
4 Model.
5 Model Check.
6 Slabs & Beams.
7 Special Shear Walls Design.
8 Special Boundary Element Design.
9 Footings Design.

## Slide 3
Project Description
The Ahmad Odeh Hotel is located in Beat Wazan in Nablus.
Its consists of two blocks separated by seismic joints.
Block A and Block B consist of six floors and a basement.
We design block A.
Total Building Area = 5400.97m²

## Slide 4: The Codes Used in This Project
The Codes used in this project are the following :
  ACI 318-14 (American Concrete Institute).
1
  IBC2015 (International Building Code).
2
  ASCE-7 (2010).
3

## Slide 5
Load Types
Live Load
(5)
Public rooms and Corridors
(4.79 )
Private rooms and Corridors (1.92 )
Office
(2.4 )
Restaurant
(4.79 )
Super Impose Dead Load
(5)
Tiles
Mortar & Filling
Plaster
Partitions
Slab Own Weight (5)

## Slide 6
Seismic Design Parameters
Risk Category

## Slide 7
Seismic Design Parameters
Importance Factor, I
Site Class (C)

## Slide 8
Seismic Design Parameters
Seismic Zone Factor, Z
Seismic Zone for Nablus is 2B
Factor (Z) = 0.20
Z = 0.20
S1 = 1.25 x Z = 1.25 x 0.2 = 0.25
SS = 2.5 x Z = 2.5 x 0.2 = 0.5

## Slide 9
Seismic Design Parameters
Site Coefficients, Fa , Fv

## Slide 10
Seismic Design Parameters
Spectral response acceleration parameters. SDS , SD1
Fv=1.55
SM1 = Fv x S1 = 0.3875
SD1= SM1 = 0.3875
SS=0.5
Fa=1.2
SMS = Fa x SS = 0.6
SDS= SMS = 0.6
S1=0.25

## Slide 11
Seismic Design Parameters
Seismic Design Category (D)
Seismic design category is determined based on:
- Risk category
- Values of SDS and SD1.

## Slide 12
Structural System Type
Building frame system (special concrete shear walls).
R=6
=2.5
Cd=5

## Slide 13
Load Combinations
  1.4D
1
  1.2D + 1.6L
2
  1.2D + 1.0L + 1.0E
3
  0.9D + 1.0E
4

## Slide 14: ETABS Model

## Slide 15: ETABS Model Checks
Compatibility
Equilibrium
Stress - Strain
Base Shear
Serviceability
Stability
Period
Checks

## Slide 16: ETABS Model Checks
1 Compatibility

## Slide 17: ETABS Model Checks
2 Equilibrium
TABLE: Base Reactions |  |  | 
Load Case | Fz ETABS (kN) | Manually (kN) | %Difference
Dead | 26006.31 | 26198.64 | 0.7
Live | 9155.35 | 9140.70 | 0.16
SID | 8792.16 | 8778.05 | 0.16
Wall | 7809.89 | 7881.30 | 0.9

## Slide 18: ETABS Model Checks
3 Stress – Strain (For Slab)
From ETABS:
𝑀22= =6.3 𝑘𝑁.𝑚
By Hand:
𝑀22= = = 6.4 𝑘𝑁.𝑚
Error = 1.5 % <10% then OK.
Make check on story five (5) at elevation 18.7 for live load.

## Slide 19: ETABS Model Checks
3 Stress – Strain (For Beam)
From ETABS:
𝑀33= = =114.165 𝑘𝑁.𝑚
By Hand:
𝑀22= = = 116.623𝑘𝑁.𝑚
Error = 2.15 % <10% then OK.
Make check on beam (B4) at story 6
span to be checked L=7.25m

## Slide 20: ETABS Model Checks
3 Stress – Strain (For Column)
From ETABS:
P L = 80.16 kN
By Hand:
P L = L.L*𝐴 = 3*26.2=78.6 𝑘𝑁
Error = 1.9 % <10% then OK.
Make check on column (P6) at story 6
Tributary area= 26.2 m2

## Slide 21: ETABS Model Checks
4 Period
Story | Area (m2) | SID (kN/m2) | Total Mass (M) (Ton) | Force (F) (KN) | M* | F*
1 | 296.09 | 5 | 623.2 | 296.09 | 0.000224 | 0.177654
2 | 189.3 | 5 | 484.3 | 189.3 | 0.001748 | 0.35967
3 | 273.94 | 5 | 617.9 | 273.94 | 0.007569 | 0.95879
4 | 269.09 | 5 | 640.4 | 269.09 | 0.036023 | 2.018175
5 | 269.09 | 5 | 607.4 | 269.09 | 0.000607 | 0.26909
6 | 269.09 | 5 | 607.4 | 269.09 | 0.094906 | 3.363625
7 | 300.9 | 1.5 | 365.3 | 300.9 | 0.078938 | 4.42323
Total |  |  |  |  | 0.220016 | 11.57023
Story | Area (m2) | SID (kN/m2) | Total Mass (M) (Ton) | Force (F) (KN) |  | 
1 | 296.09 | 5 | 623.2 | 296.09 | 0.000224 | 0.177654
2 | 189.3 | 5 | 484.3 | 189.3 | 0.001748 | 0.35967
3 | 273.94 | 5 | 617.9 | 273.94 | 0.007569 | 0.95879
4 | 269.09 | 5 | 640.4 | 269.09 | 0.036023 | 2.018175
5 | 269.09 | 5 | 607.4 | 269.09 | 0.000607 | 0.26909
6 | 269.09 | 5 | 607.4 | 269.09 | 0.094906 | 3.363625
7 | 300.9 | 1.5 | 365.3 | 300.9 | 0.078938 | 4.42323
Total |  |  |  |  | 0.220016 | 11.57023
By Applying a 1kN/m2 force in (X-Direction).
Thus, Period = = 0.866sec
% Difference = ....OK.
Period Check By (Rayleigh Method):
Check if T
Ta = Cthnx
= 0.0488*28.30.75 = 0.599 sec
T (0.864) , but its acceptable

## Slide 22: ETABS Model Checks
5 Base Shear
R = 6
I = 1.25
SDS = 0.6
SD1 = 0.3875
Define Equivalent Static Force

## Slide 23: ETABS Model Checks
5 Base Shear
Determine of Base shear using IBC2015
Cs=
W = 40870.12 kN
V= 0.094*40870.12 = 3841.79 kN
Tx = 0.864sec
Sa=
V=Cs*W
By Hand:
V ETABS= 3834.2624 kN
Error % =
From ETABS:

## Slide 24: ETABS Model Checks
6 Serviceability
Story | h m | Load Case |  | mm
Story8 | 3.2 | RS-X Max | 20.8 | 48
Story7 | 3.2 | RS-X Max | 19.6 | 48
Story6 | 3.2 | RS-X Max | 21.2 | 48
Story5 | 3.2 | RS-X Max | 21.6 | 48
Story4 | 5.2 | RS-X Max | 33.6 | 78
Story3 | 2.7 | RS-X Max | 12.8 | 40.5
Story2 | 2.95 | RS-X Max | 12.4 | 44.25
Story1 | 4.65 | RS-X Max | 2.8 | 69.75
Story | h m | Load Case |  | 
Story8 | 3.2 | RS-X Max | 20.8 | 48
Story7 | 3.2 | RS-X Max | 19.6 | 48
Story6 | 3.2 | RS-X Max | 21.2 | 48
Story5 | 3.2 | RS-X Max | 21.6 | 48
Story4 | 5.2 | RS-X Max | 33.6 | 78
Story3 | 2.7 | RS-X Max | 12.8 | 40.5
Story2 | 2.95 | RS-X Max | 12.4 | 44.25
Story1 | 4.65 | RS-X Max | 2.8 | 69.75
should be less than allowable story drift, .
is less than allowable story drift, ... Ok

## Slide 25: ETABS Model Checks
7 Stability
Story | h mm | kN | mm | kN | 
Story8 | 3200 | 1107.88 | 20.8 | 234.23 | 0.008
Story7 | 3200 | 6482.30 | 19.6 | 867.17 | 0.011
Story6 | 3200 | 16153.12 | 21.2 | 1846.46 | 0.014
Story5 | 3200 | 25952.58 | 21.6 | 2279.90 | 0.019
Story4 | 5200 | 36488.77 | 33.6 | 2793.55 | 0.021
Story3 | 2700 | 44573.09 | 12.8 | 3082.77 | 0.017
Story2 | 2950 | 53416.88 | 12.4 | 3258.64 | 0.017
Story1 | 4650 | 63918.91 | 2.8 | 3320.00 | 0.003
Story | h mm |  |  |  | 
Story8 | 3200 | 1107.88 | 20.8 | 234.23 | 0.008
Story7 | 3200 | 6482.30 | 19.6 | 867.17 | 0.011
Story6 | 3200 | 16153.12 | 21.2 | 1846.46 | 0.014
Story5 | 3200 | 25952.58 | 21.6 | 2279.90 | 0.019
Story4 | 5200 | 36488.77 | 33.6 | 2793.55 | 0.021
Story3 | 2700 | 44573.09 | 12.8 | 3082.77 | 0.017
Story2 | 2950 | 53416.88 | 12.4 | 3258.64 | 0.017
Story1 | 4650 | 63918.91 | 2.8 | 3320.00 | 0.003
max =
max =
Which means that the P – delta effect can be disregarded.

## Slide 26: Design and Detailing
Slab Design
One way Solid Slab in Y-direction
Thickness = 200mm.

## Slide 27: Design and Detailing
Beam Design
Design The Beam For Flexure
According to calculations from several load combinations we notice that negative Mu is occurring due to (1.2D+L+E) combination, where positive Mu is occurring due to (1.2D+1.6L) combination.

## Slide 28: Design and Detailing
Special Shear Wall Design
We selected wall (W1) in the 6th floor to be designed

## Slide 29: Design and Detailing
Special Shear Wall Design
Check shear walls for out plane shear force ()
Thus, no need for out plane shear reinforcement
Shear name | Length ( m | kN | kN
W1 | 4.1 | 16 | 463.9
W2 | 4.1 | 16 | 463.9
W3 | 1.4 | 128 | 158.4
W4 | 2.25 | 19 | 254.6
W5 | 2.25 | 4 | 254.6
W6 | 6.25 | 133 | 707.1
W7 | 2.25 | 16.3 | 254.6
W8 | 6.25 | 74 | 707.1
W9 | 6.25 | 114 | 707.1
W10 | 4.7 | 78 | 531.7
W11 | 2.4 | 27 | 271.5
W12 | 3.8 | 10 | 429.9
W13 | 3.8 | 8 | 429.9
W14 | 2.9 | 33 | 328.1
Shear name |  |  | 
W1 | 4.1 | 16 | 463.9
W2 | 4.1 | 16 | 463.9
W3 | 1.4 | 128 | 158.4
W4 | 2.25 | 19 | 254.6
W5 | 2.25 | 4 | 254.6
W6 | 6.25 | 133 | 707.1
W7 | 2.25 | 16.3 | 254.6
W8 | 6.25 | 74 | 707.1
W9 | 6.25 | 114 | 707.1
W10 | 4.7 | 78 | 531.7
W11 | 2.4 | 27 | 271.5
W12 | 3.8 | 10 | 429.9
W13 | 3.8 | 8 | 429.9
W14 | 2.9 | 33 | 328.1

## Slide 30: Design and Detailing
Special Shear Wall Design
Design shear wall for in plane shear force
Check whether
Thus, we need minimum reinforcement ratio, (.
Minimum reinforcement per meter of wall is:
Use 2mm bars (
Spacing (S) =
, use s=450mm

## Slide 31: Design and Detailing
Special Shear Wall Design
Design the wall for flexure and axial forces
Shear name | Length | kN |  |  |  | mm | No. of bars | Spacing (S) mm
W1 | 4.1 | 1207 | 698 | 0.0025 | 2050 | 12 | 20 | 200
Shear name | Length |  |  |  |  |  | No. of bars | Spacing (S) mm
W1 | 4.1 | 1207 | 698 | 0.0025 | 2050 | 12 | 20 | 200
Check for ETABS
As you see the point within the curve, so it’s ok

## Slide 32: Design and Detailing
Special Shear Wall Design
Reinforcement detailing for shear wall (W1)

## Slide 33: Design and Detailing
Special Boundary element Design
Check if we need to design a special boundary element
If maximum compressive stress in the wall greater than 0.2.
Thus, we need to design a special boundary element for wall.
Maximum compressive stress (
Shear name |  | 0.2 | Need / not need
W1 | 2.72 | 6.4 | Not
W2 | 2.32 | 6.4 | Not
W3 | 6.61 | 6.4 | Need
W4 | 2.72 | 6.4 | Not
W5 | 1.51 | 6.4 | Not
W6 | 7.38 | 6.4 | Need
W7 | 3.50 | 6.4 | Not
W8 | 7.09 | 6.4 | Need
W9 | 6.73 | 6.4 | Need
W10 | 3.98 | 6.4 | Not
W11 | 3.12 | 6.4 | Not
W12 | 2.77 | 6.4 | Not
W13 | 2.50 | 6.4 | Not
W14 | 3.12 | 6.4 | Not
Shear name |  |  | Need / not need
W1 | 2.72 | 6.4 | Not
W2 | 2.32 | 6.4 | Not
W3 | 6.61 | 6.4 | Need
W4 | 2.72 | 6.4 | Not
W5 | 1.51 | 6.4 | Not
W6 | 7.38 | 6.4 | Need
W7 | 3.50 | 6.4 | Not
W8 | 7.09 | 6.4 | Need
W9 | 6.73 | 6.4 | Need
W10 | 3.98 | 6.4 | Not
W11 | 3.12 | 6.4 | Not
W12 | 2.77 | 6.4 | Not
W13 | 2.50 | 6.4 | Not
W14 | 3.12 | 6.4 | Not

## Slide 34: Design and Detailing
Special Boundary element Design
We selected wall (W6) in the basement floor to be designed

## Slide 35: Design and Detailing
Special Boundary element Design
Calculate distance from extreme compression fiber to neutral axis (c)
Use
We find (c) using ETABS and its equal 1.39 …ok

## Slide 36: Design and Detailing
Special Boundary element Design
Find the dimensions of special boundary element
a = max
b
Use b=0.4m

## Slide 37: Design and Detailing
Special Boundary element Design
Longitudinal reinforcement
Longitudinal reinforcement for the web of the wall
(kN) > =586.9kN
Since (,
Longitudinal reinforcement for special boundary element
Reinforce the special boundary element as special column with minimum area of steel.
(Use 14)

## Slide 38: Design and Detailing
Special Boundary element Design
Transverse reinforcement
Transverse reinforcement for the web of the wall
(kN) > =586.9kN
Spacing (S) =
Use @ 450mm.

## Slide 39: Design and Detailing
Special Boundary element Design
Transverse reinforcement
Transverse reinforcement for special boundary element
= a* b = 0.8*0.4 = 0.32 mm2
==mm2

## Slide 40: Design and Detailing
Special Boundary element Design
Transverse reinforcement
Transverse reinforcement for special boundary element
Smax = 100mm
= 0.009* = 0.007*=532mm2
Use stirrup (6 legs)
= 0.007* = 0.007*=252mm2
Use stirrup (3 legs)
Smax = Min
Smax = Min

## Slide 41: Design and Detailing
Special Boundary element Design
Reinforcement detailing for shear wall (W6)

## Slide 42: Design and Detailing
Footings Design
Check if we need to use mat foundation
If. Thus, we need to use mat foundation
From ETABS =51919 kN

## Slide 43: Design and Detailing
Check if we need to use mat foundation
If we assume that, we have single footings and wall footings and checks if it is suitable.
We draw calculated dimensions of footings in AutoCAD, and we recognize that assumed footings type not suitable in our structure.
Therefore, we used mat foundation
Footings Design

## Slide 44: Design and Detailing
The plan view of mat foundation
We used h = 1200mm
Footings Design

## Slide 45: Design and Detailing
Check for deflection
Allowable displacement in the mat foundation is10mm.
The maximum displacement of the footings joints is shown in figure and it is approximant equal 10mm… ok
Footings Design

## Slide 46: Design and Detailing
Check for stress
Bearing capacity of the soil ( ) =270 kN/m2
The maximum stress is shown in figure and it is less than 270 kN/m2
Footings Design

## Slide 47: Design and Detailing
Check punching shear
Column name | Column dimensions (cm) | Ultimate shear (kN) | (mm) | (kN) | 
P6 | 60*60 | 4325.3 | 4(600+1125) = 6900 | 9507 | Ok
P12 | 55*55 | 2436.3 | 2(1112.5)+1675 = 3900 | 5374 | Ok
S12 | 45*45 | 950 | 2*1012.5 = 2025 | 2790 | Ok
Column name | Column dimensions (cm) | Ultimate shear (kN) |  |  | 
P6 | 60*60 | 4325.3 | 4(600+1125) = 6900 | 9507 | Ok
P12 | 55*55 | 2436.3 | 2(1112.5)+1675 = 3900 | 5374 | Ok
S12 | 45*45 | 950 | 2*1012.5 = 2025 | 2790 | Ok
Footings Design

## Slide 48: Design and Detailing
Check for wide beam shear
Column strip width = 2m
Wide beam shear capacity of column strip =
Capacity is greater than ultimate. Thus, it is ok
And the same for
Footings Design

## Slide 49: Design and Detailing
Design for flexure
In X-direction, use for both bottom and top reinforcement
In Y-direction, use for both bottom and top reinforcement.
Footings Design