## Slide 1: 3D Scanner
Bashar Mu’ala
Ahmad Khader

## Slide 2: 3D Scanner
3D Scanner: is a device that analyzes a real-world
object or environment to collect data on its shape and possibly its appearance. The collected data can then be used to construct three dimensional models useful for a wide variety of applications.

## Slide 3: Difference between 2D & 3D Scanners
2D scanner is a device that optically scans images, printed text, handwriting, or an object, and converts it to a digital image.
3D scanner used to analysis 3D objects, also it concerns with the outer shape of the object.

## Slide 4: Main Idea
The main idea behind this project is to obtain the outer surface of the object . so the straight forward way that we considered is to slice the object to thin slices using a laser pointer formed into a line and aimed into the object, this laser line will take the outer shape of the thin part of object at this moment a camera positioned at a known angle captures an image of the object. And send it somehow to the PC “to be tilled later” , then rotate the object so that laser line covers another part of the object, repeat these steps until the whole object is scanned .

## Slide 5: Main Idea cont.
At PC side prepare the pictures remove everything except the lighted part of the object , then group all pictures together each in its correct position as its distance from the laser rod The result is a digital image similar to the word object shape .

## Slide 6: Applications
industrial design “CAD/CAM”.
Orthotics and Prosthetics
entertainment industry in the production of movies and video games
Reverse engineering
inspection and documentation of cultural artifacts.

## Slide 7: Technical

## Slide 8: Tools Needed
PIC microcontroller.
Digital camera.
Laser diode.
Lenses “to convert laser beam from a point into straight line”.
Stepper motors.

## Slide 9: How does it Works

## Slide 10: Capturing Images
First of all we take two images of the object each step first one while the laser is on, the other one while the laser off. After that we rotate the object, we repeat these steps for all object(360°).

## Slide 11: Subtraction
We subtract the lasered image with the one that we took without laser both of them has been taken from the same view of object. The result image will look like

## Slide 12: Threshold
After subtraction we make thresholding for the image this step is essential for the next step.

## Slide 13: Skeletonization
We shrink the laser line in the image to get the core “the middle region” of the line.

## Slide 14: Get Points
We read the points from the Skeletonized image “by scanning pixels”, and calculate it’s coordinates.

## Slide 15: Equations & Calculations
After we get the points of each image we make a large complex calculations to find the coordinate of each point in 3-dimentional view.

## Slide 16: Surface Reconstruction
Is the process that reconstruct s a surface from its sample points.
The input can be co-ordinates of the point cloud in 3D and output is a piecewise linear approximation of the surface

## Slide 17: Output
The user have the choice to pick either
  VRML (Virtual Reality Modeling
  Language).Can be imported using 3dmax
  ,AutoCAD and many other graphics soft
  wares.
  Point cloud format: used by AutoCAD and point cloud viewer .

## Slide 18: Point Cloud
3D scanners usually creates a point cloud of geometric samples on the surface of the subject. These points can then be used to show the shape of the subject (in a process called surface reconstruction).

## Slide 19: Problems
As all of you know there is no
project without a problems.

## Slide 20: 1.Speed
The first and the most difficult problem is the speed of the scanning process, first it took about 18 minutes to make full scan. We managed to reduce the time by modifying the equations and
quality choice.

## Slide 21: 2.Noise
There are a lot of noise in the captured image due to the changing in intensity of the light, we limit this problem by modifying the subtraction process.
Before After

## Slide 22: 3.Cost
Most of the industrial 3D scanner is tooooo expensive
Either on the hardware or software level. We try to make it as cheap as possible by making our 3D scanner from very simple tools.

## Slide 23: What about scanning human face?

## Slide 24: Solution…
Face Scanner: It may be impractical to rotate the person being scanned. In this case, you should probably consider rotating the laser and the camera in a circle around the persons head rather than spinning the person.

## Slide 25: Cont.…
It has been made especially for scanning the face of the human being but at the same time it can scan any object, the output will be a 3d object, can be useful in a lot of industrial fields.

## Slide 26: Face Scanner