## Slide 1: Graduation Project
Motorized Gyroscope Manufacturing
Students:
Ashraf Jodeh
Ameer Hasan
Bashar Alqerm
Yousof Odeh

## Slide 2: Contents
Abstract
What is Gyroscope ?
History
Problem Definition
Gyroscopic Principles
Manufacturing (Mechanical and Electrical parts)
Experiment

## Slide 3: Abstract
The idea of this project is to design and manufacture a gyroscope which is driven by an electric motor to make it spin indefinitely.

## Slide 4: What is the Gyroscope?
The gyroscope is a device for measuring or maintaining orientation, based on the principles of angular momentum.

## Slide 5: History of Gyros.
Basically, a gyroscope is a top, a self-balancing spinning toy, put to instrumental use.

## Slide 6: Cont.
John Serson who is the first one use a top as an instrument when he invented the "Whirling speculum" (or Serson's Speculum) in 1743. “Artificial Horizon”
In 1817, German Johann Bohnenberger used the instrument as an actual gyroscope.
In 1852, Leon Foucault used the gyroscope in an experiment to see the Earth's rotation.

## Slide 7: Cont.
In 1860, electric motors used to make the gyroscope spin indefinitely. .
In 1909, Elmer A. Sperry built the first automatic pilot for aircraft using gyroscopes.

## Slide 8: Cont.
20th century, gyroscope used in black box navigational systems and for inertial guidance systems for ballistic missiles.
Today the MEMS (Micro Electro-Mechanical System) gyroscopes have enabled exciting applications in portable devices.

## Slide 9: Problem definition
Gyroscope is very important tool used for various controls in high technology vehicles and devices, and takes a good place in research and development.
Thus the study of gyroscope behavior is so important for engineering students.

## Slide 10: Gyroscopic Principles
The gyroscope exhibits two predominant characteristics:
1. Rigidity in Space
2. Precession

## Slide 11: 1. Rigidity in Space
The spinning rotor inside a gyro instrument maintains a constant attitude in space as long as no outside forces change its motion. This stability increases if the rotor has great mass and speed.

## Slide 12: 2. Precession
Another characteristic of gyros is precession, which is the tilting or turning of the gyro spinning axis as a result of applied forces.

## Slide 13: Electrical and Mechanical parts

## Slide 14: The Universal Motor

## Slide 15: General Description:
Universal or series motors are those having brushes, a wound rotor, and a wound stator. They are compatible with both AC and DC power.
They are also distinguished by their noisiness. These motors produce so much noise because the brushes rub on the slotted armature.

## Slide 16: Uses
Manufacturers use universal motors because they are smaller and much lighter than induction motors. An example of this type is that found in a portable drill or a Dremel tool.
Basically the DC motor characteristics that can be run on AC.

## Slide 17: Comparison to Induction Motors:
A 3/4 Hp induction motor...runs at 1075 - 3450 RPM, is about 6" long x 6" diameter and weighs about 19 pounds. If we compare this with a universal motor with 3/4 horsepower output, we see a speed increase of about 15,000 RPM, a size reduction to about 6" long x 3" diameter {1/4 of the volume} and a weight reduction of greater than 85%.

## Slide 18: Advantage
The weight difference is huge: Universal motors are much lighter than induction motors
Torque goes clear down to stall torque (DC motors will stall at a high RPM)
Lower cost
Variable speeds

## Slide 19: Disadvantage:
Non reversible (one direction)
Noisy
universal motors are usually relatively inefficient- around 30% for smaller motors
and up to 70-75% for larger ones.
the commentator has brushes that wear, so they are much less often used for
equipment that is in continuous use

## Slide 20: Tachometers

## Slide 21: Tachometer, What’s That?
Tachometer is used for measuring rotational speed
Can be used to measure speed of a rotating shaft
Can also be used to measure flow of liquid by attaching a wheel with inclined vanes

## Slide 22: What Are the Different Types of Tachometers?
Tachometers can be classified on the basis of data acquisition – contact or non contact types
They can also be classified on the basis of the measurement technique – time based or frequency based technique of measurement
They can also be classified as analog or digital type

## Slide 23: Typical Specifications of a Non Contact Type Tachometer
Display 5 digits large LCD
Range: 2.5 - 99,999 RPM
Distance: 50 to 1,000 mm; 12 to 40 inches.
Resolution: 0.1 RPM<1000 RPM (2.5 to 9,999 RPM)
1.0RPM >1000 RPM
Measurement angle: at less than 120 degrees.
Range selection: Auto
Laser Output Power: <1mW class II
Sampling Time: 1.0 seconds (over 60 RPM)
Memory: Last value, Max Value, Min. Value
Time base: Quartz crystal
Circuit: Exclusive one-chip LSI circuit
Battery: 4 X 1.5V AA
Weight: 300g/0.65lb
Size: 190 X 72 X 37 mm

## Slide 24: Block Diagram of a Digital Tachometer
Optical / Magnetic Sensor
Signal Conditioning
Microcontroller
Memory
Display
External
Port (to controller)

## Slide 25: Microcontroller
Not essential, but is generally the norm to have a microcontroller
Compute the speed
Can store the readings
Can output values to a display unit
Give out warning signal when speed reduces / increases beyond set margins
Transfer data to external controller
We used the aurdino as a microcontroller

## Slide 26: What is Arduino?
A programmable micro controller for prototyping electromechanical devices
You can connect Digital and Analog electronic signals:
Sensors (Gyroscopes, GPS Locators, accelerometers)
Actuators (LEDS or electrical motors)

## Slide 27: Arduino Components

## Slide 28: Bearings
The typical structure for bearings involves :
- inner race
- outer race
- Inner ring
- Outer ring
- separator or ( cage )
- Balls or rollers

## Slide 29: As we see in the figure :

## Slide 30: Types of rolling element bearings 1. ball bearing ( spherical rolling elements )
single row double row single row double row
Angular cotact angular contact deep-groove radial deep-groove radial

## Slide 31
single row deep-groove Double row deep-groove grooved race thrust
Externally self-aligning Internally self-aligning

## Slide 32: 2. roller bearings (cylindrical rolling elements ) single row straight double row straight single row tapered double row tapered roller bearing roller bearing self-aligning roller bearing roller bearing self–aligning single row spherical double row spherical needle roller tapered roller thrust roller bearing

## Slide 33: Bearing materials
the responsibility for achieving the design objectives ( selection the best material best geometry ) lies with the specialized designer working in the bearing industry .
The material of ball & races :
1 . high carbon chrome steel : hardened and tempered for optimum strength and toughness .
2. stainless-stee : used when corrosion resistance is needed or elevated temp.
3. Cobalt : for higher temp applications .
* the separator material include :
phenolic ,bronze , phosphor bronze , or alloy steels such as AISI 4130 .

## Slide 34: Procedure for selecting an appropriate bearing for our project :
1. shaft of the motor and the disc .
- diameter = 10 mm .
- Fᵣ =20 N .
- shaft speed = 4500 rpm .
- design life specification is 10 years of operation , 50 days/year, 20 hr/day .
- design reliability specification is R =90 percent .
- the shaft is uniform load .
Ld = 10 yr * (50 days/yr) *(20 hr/day) (60 min/hr) 4500 rev/min = 27 X10^8 revolutions .
From table of reliability Kr = 1
From table of impact factor IF = 1.1

## Slide 35: Pe = Xd *Fr + Yd*Fa Xd1= 1 Yd1= 0 Xd2 =0.55 Yd2 = 1.45 Pe1 =(1)(20)= 20 N Pe2 =(0.55)(20) = 11 N Pe1>Pe2 Select the larger Pe1= 20 N [ Cd(90) ]req =( 27 x10^8 /(10^6) )⅓(1.1)(20) = 306.3 N Select bearing type (6000)

## Slide 36
Pse =Xs*Fsr + Ys * Fsa
Xs1= 1 Ys1 = 0
Xs2= 0.6 Ys2 = 0.5
(Pse)1 =(1)(20) =20 N
(Pse)2 =(0.6)(20) =12 N
(Pse)1>(Pse)2
Select the large r( Pse)1 = Cs
Select bearing number (6000)
Type of bearing for the shaft is ( 6000)

## Slide 37
2. standing shaft
- diameter = 40 mm
- Fa =200 N .
- shaft speed = 4500 rpm
- R =90 percent Kr = 1
- the shaft is uniform load IF = 1
Ld = 27x 10^8 rev.
[ Cd(90) ]req = 4442.0005 n
Select bearing type (6008)
( Pse)2 = Cs = 100 n
Select bearing number (6008)
Type of bearing for the shaft is ( 6008)

## Slide 38
3. shaft that will connect the body of disk with body standing .
- diameter = 12 mm
- Fᵣ =15 N .
- shaft speed = 4500 rpm
- R =90 percent Kr = 1
- the shaft is uniform load IF = 1
- Ld = 27x 10^8 rev.
[ Cd(90) ]req = 229.75 N
Select bearing type (6002)
( Pse)1 = Cs = 15 n
Select bearing number (6002)
Type of bearing for the shaft is ( 6002)

## Slide 39: Specifications
Mass of rotating disk = 1.2Kg.
The radius of the rotating disk = 0.1 m.
The distance from the disk to the weight = 0.2m.
Motor speed ranged (1-1000)r.p.m.

## Slide 40: Material
Really, I do not know the type of material which being used. But I will try to predict it from machining processes.

## Slide 41: Material
Structure machining :
At low cutting speed, I obtained a continuous chips with built-up edge. and The formation of these chips start cycle then break off.

## Slide 42: Material
That mean I have a low carbon steel (ductile material). as shown in figure (1).
Fig.(1):Continuous Chips

## Slide 43: Material
Disk machining:
At low cutting speed, I obtained a discontinuous chips and high tool chips friction.

## Slide 44: Material
That mean I have high carbon steel (brittle material). as shown in figure (2).
Fig.(2): Discontinuous Chips

## Slide 45: Connecting
Using some types of bolts, pins and Shielded Metal Arc Welding and Argon Arc Welding to connect parts of the structure.

## Slide 46: Connecting
Why argon:
Using Argon Arc Welding to connect the boxes of bearings with the structure.
It is more suitable welding for thin parts because it gives a narrow bead and no splatter.

## Slide 47: Conclusion
As we know we built these apparatus to verify the relation between spinning velocity, applied torque with precessional velocity.

## Slide 48: Conclusion
Chart: Applied torque T (N.m)
| 3.9199999999999999E-2 | 9.8000000000000004E-2 | 0.25600000000000001
Y-Values | 2.1 | 5.175 | 8.422
Precessional velocity is directly proportional with applied torque as shown in figure(3).
Fig.(3): Torque vs. Precessional velocity

## Slide 49: Conclusion
Chart: Spin velocity ω (r.p.m)
| 250 | 500 | 750 | 1000
spin velocity ω vs. Experimental Precessional velocity | 2.1 | 1.098 | 0.763 | 0.574
precessional velocity is inversely proportional with spinning velocity as shown in figure(4).
Fig.(4): Precessional velocity vs. Spin velocity

## Slide 50: Sources of error
The error of apparatus is 10.2% induced by friction of bearing and huge vibration caused by universal motor.
Therefor, We used dampers and coupling joint to reduce these vibrations and improving accuracy.

## Slide 51: Thank You.