## Slide 1
3D Seismic Design Of Mosque and Municipality of
Rawabi City
Prepared By : Noorah Ismail
Dana Nassar
Saja Abu Thraa
Samah Hindeya
Under Supervision of: Monther Thiab
2018-2019

## Slide 2
Structural Analysis and Design of
Mosque and Municipality of
Rawabi City under
Seismic load

## Slide 3
Outline
1 Project description
2 Seismic Design Parameters
3 Challenges
4 Model Checks
5 Structural Element Design
6 Footing Design
7 Stairs Design
8 Dome Design
9 Recommendations

## Slide 4
Project Description
The project is located in Rawabi which is far 9 Km north of Ramallah
It consists of two blocks separated by seismic joints
Block A and Block B consist of six floors include the basement
We design the two Blocks A & B
Total Building Area = 12548.6m²

## Slide 6: Loads
Loads
Gravity
Dead
Live
Lateral
seismic
wind

## Slide 7
Load Types
Live Load
(5)
(3)
Super imposed dead loads
(3 KN/m2)
Mosque Floors
Municipality Floors
Gravity Loads
GF & BF Mosque
Barking Floors in Mosque
Municipality Floors

## Slide 8: The Codes Used in This Project
The Codes used in this project are the following :
  ACI 318-14 (American Concrete Institute)
1
  UBC 1997 (Uniform Building Code)
2
  ASCE-7 (2010)
3

## Slide 9: Materials Types
Concrete
Structural element | Compressive strength(fc’) (MPa)
Slab, beam | 24
Column, footing, shear wall, Stair | 28
Reinforcement Steel
Yielding strength (Fy) = 420MPa
Modulus of elasticity (Es) = 200GP

## Slide 10: Material
Materials Unit Weight
Material | Unit weight, γ (KN/m3)
Plain concrete | 23
Reinforced concrete | 25
Tiles | 26
Filling material | 23

## Slide 11
Structural System Type
Building frame system
Intermediate concrete shear walls

## Slide 12
Seismic Design Parameters
For Ramallah City, seismic zone is 2A
Seismic zone factor, Z = 0.2
Importance Factor , I = 1.25
  Over strength factor, R = 5.5
 | Block 1 | Block 2
Soil type | SC | SC
Ca | 0.18 | 0.18
Cv | 0.25 | 0.25

## Slide 13
Load Combinations
  1.4D
1
  1.2D + 1.6L
2
  1.2D + 1.0L + 1.0E
3
  1.2D + 1.6L + 0.5(Lr or S or R)
4
The Ultimate load combinations used in design
  0.9D + 1.0E
5

## Slide 14
Load Combinations
  D
1
  D +L
2
  D +0.75L +0.75(0.7E)
3
  D +0.7E
4
The service load combinations used in checks are
  0.6D+0.7E
5

## Slide 15
Computer programs
ETABS
Word and Excel
AutoCAD
SAFE
SAP
2000

## Slide 16
Challenges
irregularity and discontinuity
of the vertical
structural element
First challenge

## Slide 17
Challenges
Block 1
Block 2

## Slide 18
Challenges
Model Name | Period | Mode
Together Model | 0.422 | Mode 106
Mosque Model | 0.421 | Mode 98
Municipality Modal | 0.331 | Mode 6

## Slide 19
Inclined surfaces (slabs) with drop beams structures are often highly differentiated
Second Challenge

## Slide 20
Model Name | Flat slab mosque |  | Inclined slab mosque | 
Axial Force | Beam | Column | Beam | Column
 | 00.00 | 1961 | 30.08 | 2434
Shear Force | 106.7 | 15.3 | 40.7 | 79.83
Moment Force | 116.98 | 27.6 | 68.6 | 575.23
Comparison between inclined and flat mosque
Model Name | Period
Flat slab mosque | 0.421
Inclined - slab mosque | 0.382

## Slide 21: Inclined
Why ?
Decrease in moment
Increase in axial

## Slide 22: Inclined
Why ?
Increase in moment
Increase in axial

## Slide 23: ETABS Model Checks
Compatiity
Equilibrium
Base Shear
Participating mass ratio
Checks
Period
Drift

## Slide 24: ETABS Model Checks
1 Compatibility

## Slide 25: ETABS Model Checks
1 Compatibility

## Slide 26: ETABS Model Checks
2 Equilibrium
TABLE: Base Reactions |  |  | 
Load Case | Fz ETABS (kN) | Manually (kN) | %Difference
Dead | 145374.4338 | 140050.02 | 3.65
Live | 45520.6815 | 455776.06 | 0.12
SID | 32542.7373 | 32575.94 | 0.1
Together

## Slide 27: ETABS Model Checks
2 Equilibrium
Ibraheem AL-Khalil Flat Mosque
TABLE: Base Reactions |  |  | 
Load Case | Fz ETABS (kN) | Manually (kN) | %Difference
Dead | 12448.1237 | 12225.23 | 1.80
Live | 33362.743 | 33311.95 | 0.037
SID | 26141.2487 | 26100.51 | 0.0043

## Slide 28: ETABS Model Checks
2 Equilibrium
TABLE: Base Reactions |  |  | 
Load Case | Fz ETABS (kN) | Manually (kN) | %Difference
Dead | 129322.04 | 128546.7 | 1.39
Live | 33362.7417 | 35788.1 | 8.9
SID | 26141.2474 | 28722.08 | 6.7
Ibraheem AL-Khalil Inclined Mosque

## Slide 29: ETABS Model Checks
2 Equilibrium
TABLE: Base Reactions |  |  | 
Load Case | Fz ETABS (kN) | Manually (kN) | %Difference
Dead | 26543.9471 | 25600.24 | 3.55
Live | 10924.11 | 11021.4 | 0.72
SID | 6565.265 | 6612.84 | 0.72
Rawabi Municipality

## Slide 30: ETABS Model Checks
3 Period
TABLE: Period |  |  |  | 
Model Name | Period | Ta | 1.55*Ta | Period <1.55*Ta
Together | 0.422 | 0.764 | 1.184 | OK
 | 0.421 | 0.764 | 1.184 | OK
 | 0.379 | 0.764 | 1.184 | OK
 | 0.331 | 0.344 | 0.5332 | OK
Ibraheem AL-Khalil Flat Mosque
Ibraheem AL-Khalil Inclined Mosque
Rawabi Municipality

## Slide 31: ETABS Model Checks
4 Participating mass ratio
TABLE: Period |  | 
Model Name |  | Mode Number
Together | 0.9105 | 106
 | 0.9495 | 98
 | 0.9124 | 109
 | 0.9632 | 6
Ibraheem AL-Khalil Flat Mosque
Ibraheem AL-Khalil Inclined Mosque
Rawabi Municipality
Participating mass ratio

## Slide 32: ETABS Model Checks
5 Base Shear
TABLE: Base Shear |  |  |  | 
Model Name | V | Fx | Fy | V< Fx &Fy
Together | 18196 | 26869.6176 | 21776.6598 | OK
 | 14601 | 20214.2717 | 15437.5332 | OK
 | 16419.41 | 28706.5335 | 29216.3578 | OK
 | 3295 | 3492 | 4193.376 | OK
Ibraheem AL-Khalil Flat Mosque
Ibraheem AL-Khalil Inclined Mosque
Rawabi Municipality

## Slide 33: ETABS Model Checks
6 Drift
TABLE: Period |  |  |  | 
Model Name | Drift Manual | Drift Etabs X | Drift Etabs Y | V< Fx &Fy
Together | 99 | 1.19E-18 | 1.19E-18 | OK
 | 99 | -7.80626E-18 | 1.19262E-18 | OK
 | 84.5 | 8.67362E-19 | 6.07153E-18 | OK
 | 84.5 | 0.001513 | 0.00087395 | OK
Ibraheem AL-Khalil Flat Mosque
Ibraheem AL-Khalil Inclined Mosque
Rawabi Municipality

## Slide 34: Inclined
Flat slab model | Inclined slab model
600*600 | 800*800
400*400 | 600*600
300*400 | 600*600
300*600 | 600*600
300*800 | 450*800

## Slide 35
Members
Slabs
Shear walls
Beams
Columns
Staircase
Footing

## Slide 36: Design and Detailing
Slab Design
Check wide beam shear
= × × λ××bw × d= 98 kN
From ETABS, the result of V13 and V23 within the range of(-98)and(98).
< Vu

## Slide 38: Design and Detailing
Slab Design
Check wide beam shear
= × × λ××bw × d= 128.6 kN
From ETABS, the result of V13 and V23 within the range of(-128.6)and(128.6).
< Vu

## Slide 40: Design and Detailing
Slab Design
Design the slab for flexure
Asmin = ρ b h= 0.0018 X 1000 X 200 = 360 mm2 (use 1 10/250mm)
ΦMn=19.01 kN.m /m
As = ρ b h= 0.00201 X 1000 X 160 = 322 mm2 (use 1 10/250mm)

## Slide 42: Design and Detailing
Slab Design
Design the slab for flexure
Asmin = ρ b h= 0.0018 X 1000 X 250 = 450 mm2 (use 1 10/160mm)
ΦMn=29.5 kN.m /m

## Slide 44: Design and Detailing
Beam Design

## Slide 45: Design and Detailing
Longitudinal bar for beam |  |  |  |  | 
1000*400 |  |  |  |  | 
Type | Al (mm2) | AL (torsion) | Main area steel | φ | NO. of bars
Top steel in right side | 1133 | 0 | 1332 | 16 | 6
Top steel in left side | 1133 | 0 | 1332 | 16 | 6
Bottom steel | 1064 | 0 | 1332 | 16 | 6

## Slide 46: Design and Detailing
Shear reinforcement for beam |  |  |  |  |  |  |  |  | 
1000*400 |  |  |  |  |  |  |  |  | 
Av/s | At/s | Av+t/s | (Av+t/s) min | adjusted (Av+t/s) | Ø , ( Av+t) | S | S max | adjusted S | final s
0 | 0 | 0 | 0.0 | 00 | 12,(2*78.5) | - | 180 | - | 2Ø10/200

## Slide 47: Design and Detailing
Beam Design

## Slide 48: Design and Detailing
Longitudinal bar for beam |  |  |  |  | 
1000*400 |  |  |  |  | 
Type | Al (mm2) | AL (torsion) | Main area steel | φ | NO. of bars
Top steel in right side | 330 | 0 | 1332 | 16 | 6
Top steel in left side | 190 | 0 | 1332 | 16 | 6
Bottom steel | 112 | 0 | 1332 | 16 | 6

## Slide 49: Design and Detailing
Shear reinforcement for beam |  |  |  |  |  |  |  |  | 
1000*400 |  |  |  |  |  |  |  |  | 
Av/s | At/s | Av+t/s | (Av+t/s) min | adjusted (Av+t/s) | Ø , ( Av+t) | S | S max | adjusted S | final s
0 | 0 | 0 | 0.0 | 00 | 12,(2*78.5) | - | 180 | - | 2Ø10/200

## Slide 50: Design and Detailing
Column
Check for Slenderness
Axial force in column=520.95kN
M22=2.7396kN.m
M33=14.1709kN.m
KL/r where :
L : length of column
R : radius of gyration =0.3*h for rectangular column
K : stiffness coefficient
R=0.3 X h = 0.3 X 0.4 = 0.12 m , L = 3.38 , K = 1
KL/r = 1 X 3.38/ 0.12 = 28 should be less than 34− 12 M11/M22
34− 12 M11= 31.68 > 28 , so is a short column
M22

## Slide 51: Design and Detailing
Column Reinforcement

## Slide 52
Checks
Bearing capaciy
Shear capacity
Deflection

## Slide 53: Design and Detailing
Check for Punching
Allowable displacement in the single foundation is10mm.
The maximum displacement of the footings joints is shown in figure and it is approximant equal 10mm… ok
Footings Design

## Slide 54: Design and Detailing
Check for soil pressure
Bearing capacity of the soil ( ) 340kN/m2
The maximum stress is shown in figure and it is less than 340 kN/m2
Footings Design

## Slide 55: Design and Detailing
Footings Design
F ID | Dimensions m*m | Depth mm | Thickness mm | Reinforcement X | Reinforcement y
F1 | 3.5*3.5 | 630 | 700 | 1 Ø16 mm/20cm | 1 Ø16 mm/20cm
F2 | 3*3 | 1070 | 1140 | 1 Ø16 mm/25cm | 1 Ø16 mm/25cm
F3 | 3*3 | 600 | 670 | 1 Ø16 mm/16cm | 1 Ø16 mm/20cm
F4 | 2*2 | 380 | 450 | 1 Ø16 mm/30cm | 1 Ø16 mm/30cm
F5 | 2*2 | 300 | 370 | 1 Ø16 mm/30cm | 1 Ø16 mm/30cm

## Slide 56: Design and Detailing
Check for soil pressure
Bearing capacity of the soil ( ) 340kN/m2
The maximum stress is shown in figure and it is less than 340 kN/m2
Footings Design

## Slide 57
Checks
Deflection
Shear Checks

## Slide 58: Design and Detailing
The thickness of stair slab is assumed based on ACI 318-11 ,which equal 150 mm (landing and flight)
Loads:
  The own weight of stairs = 3.75 KN/m2
  Live load (LL) = 5 KN/m2
  Superimposed dead live () =~ 3.5 KN/m2
Slab Thickness

## Slide 59: Design and Detailing
Check for Deflection
A𝑙𝑙𝑎𝑤𝑎𝑏𝑙𝑒 𝐿𝑜𝑛𝑔 𝑡𝑒𝑟𝑚 deflection, ∆𝐿/ 240≤ 12 mm
The long term deflection from SAP found approximately 0.23 mm
which means that is smaller than the allowable deflection
So, Its OK

## Slide 60: Design and Detailing
Check for shear
VC= 72.8 kN
Vu13 and Vu23=19& 23.2kN respectively.
So, The slab thickness is OK

## Slide 61: Design and Detailing
Design for flexural
TABLE Flexural |  |  |  |  | 
Slab Name | Mu max (KN.m) | As mm2 | mm2 | As mm2 | Reinforcement
For landing | 4.25 | 108.2 | 270 | 270 | 4ɸ12/m in two direction)
For Flight | 1.61 | 38.5 | 270 | 270 | 4ɸ12/m in two direction)
TABLE Flexural |  |  |  |  | 
Slab Name | Mu max (KN.m) | As mm2 |  | As mm2 | Reinforcement
For landing | 4.25 | 108.2 | 270 | 270 | 4ɸ12/m in two direction)
For Flight | 1.61 | 38.5 | 270 | 270 | 4ɸ12/m in two direction)

## Slide 62: Design and Detailing
The thickness of Dom slab is assumed to be equal 120 mm
  The own weight of Dom = 3 KN/m2
  Live load (LL) = 1.5 KN/m2
Slab Thickness
Loads

## Slide 63: Design and Detailing
Calculation
TABLE: Gravity Projection |  | 
∅ | N∅ | Nϴ
0 | -11.595 | -11.6
79.47 | -19.6 | -15.36

## Slide 64: Design and Detailing
Calculation
TABLE: Live Projection |  | 
R | N∅ | Nϴ
7.73 | -5.8 | -5.4

## Slide 65: Design and Detailing
Design
ØP n= Øλ (0.85 fc` (Ag-As) + fy × As)
Ø = 0.65
λ=0.85
Ag = 120*1000
ØP n = 1485 KN >>N∅ ,Nϴ
Use min steel
As = 0.003*1000*120 = 360 mm2 1Ø12/250 mm

## Slide 66: Design and Detailing
Special Shear Wall Design
TABLE: Reinforced shear wall |  |  |  |  |  | 
Model Name | Wall Thickness | L | Longitudinal |  | shear | 
 | 200 | 15 | 16419 | 1∅ 12 / 350 mm | 10950 | 1∅12 / 150 mm
 | 250 | 12 | 3676 | 1∅ 12 / 100 mm | 7500 | 1∅12 / 180 mm
 | 200 | 5 | 1896 | 1∅ 12 / 290 mm | 2500 | 1∅12 / 200 mm
 | 250 | 8 | 3325 | 1∅ 12 / 270 mm | 5000 | 1∅12 / 180 mm
 | 300 | 4 | 2488 | 1∅ 12 / 180 mm | 3000 | 1∅12 / 150 mm
Ibraheem AL-Khalil Inclined Mosque
Rawabi Municipality

## Slide 67: Recommendations
Based on the previous results which explained in presentation , which show the importance of separating this structure to reduce the irregularity of the building .
In general, we recommend to do the necessary analysis in the future projects which face like this challenge , and separating these structures depend on analysis studies .
For First Challenge

## Slide 68: Recommendations
For Second Challenge
we recommend designing inclined slabs with beams in structures
that contains parking floors ( Ramps) instead of horizontal – flat slabs structures , which reduce the internal forces of the structural elements such as beams.