## Slide 1: Structural Design of Al-Fidai Stadium
Prepared by: Bisan Khader
Yasmeen Abu Oun
Under Supervision of:
Dr. Ibrahim Arman

## Slide 2: OUTLINE
Introduction
Preliminary Design
Three-Dimensional Analysis and Design

## Slide 3: INTRUDUCTION

## Slide 4: INTRUDUCTION
Location: Eastern area from Nablus, Palestine
Nablus’s Height: 400m above mean sea level
Soil Type: Rock
Bearing Capacity = 350 KN/m2
Soil Site Class: C
Background Information …

## Slide 5: INTRUDUCTION
Field area of about 54000 m2
Capacity of about 50000
Architectural and Structural Design …
Four Stories
Total area of about 71420 m2
Divided into Eight Blocks
Part One: Concrete Structure
Part Two: Steel Structure
Total height of about 40.5 m
Length of about 50 m

## Slide 11: PART ONE : CONCRETE STRUCTURE

## Slide 12: INTRUDUCTION
Block
Architectural and Structural Design …
Height (m) | Area (m2) | 
5.5 | 3000 | Ground Floor
4 | 2430 | First Floor
4 | 1850 | Second Floor
8 | 1700 | Third Floor

## Slide 13: INTRUDUCTION
Codes and Standards …
American Society of Civil Engineers (ASCE 7-10)
American Concrete Institute (ACI 318-14)
Jordanian Code for Loads and Forces
American Society for Testing Materials (ASTM)
Israeli Code SI 413

## Slide 14: INTRUDUCTION
Materials …
Concrete
Structural Materials
Value | Property
40 MPa | Compressive Strength ()
29725.41 MPa | Modulus of Elasticity ()
23 | Unit Weight of Plain Concrete ()
25 | Unit Weight of Reinforced Concrete ()
0.2 | Poisons ratio
Value | Property
40 MPa | 
29725.41 MPa | 
0.2 | Poisons ratio
Steel
Value | Property
Grade 60 | Steel Grade
420 MPa | Yield Strength ()
600 MPa | Ultimate Strength ()
Value | Property
Grade 60 | Steel Grade
420 MPa | 
600 MPa | 

## Slide 15: INTRUDUCTION
Materials …
Nonstructural Materials
Unit Weight () | Material
23 | Plastering
27 | Tiles
18 | Fill Material
12 | Bricks
 | Material
23 | Plastering
27 | Tiles
18 | Fill Material
12 | Bricks

## Slide 16: INTRUDUCTION
Loads …
Loads
Gravity
Dead
Live
Temperature
Seismic
Lateral

## Slide 17: INTRUDUCTION
Gravity Loads …
Dead Loads: Own Weight
Super-imposed dead load
Live load: all rooms have 5 KN/m2 Except: Storage area has 6 KN/m2
Temperature Load …
From Jordanian Code: the expected value of the temperature changes is 20.

## Slide 18: INTRUDUCTION
Lateral Loads …
Seismic Loads
Seismic Parameters
Site Class is C
Risk Category III
Seismic Importance Factor = 1.25
Seismic Design Category is D
Value | Parameter
0.7 | Spectral response acceleration parameter at short periods ()
0.14 | Spectral response acceleration parameter at 1 second period ()
 | Design spectral response acceleration parameter at short periods ()
 | Design spectral response acceleration parameter at 1 second period ()
Value | Parameter
0.7 | 
0.14 | 

## Slide 19: INTRUDUCTION
Type of Lateral Forces Resisting System …
Block | 
Moment resisting frame system with special reinforced moment frames | Structural System
8 | Response Modification Coefficient (R)
3 | Overstrength Factor ()
5.5 | Amplification Factor ( )
Block | 
Moment resisting frame system with special reinforced moment frames | Structural System
8 | Response Modification Coefficient (R)
3 | 
5.5 | 
Type of lateral forces resisting system

## Slide 20: INTRUDUCTION
Approximate Fundamental Period …
Values of Approximate Period Parameters and

## Slide 21: INTRUDUCTION
Load Combinations …
Ultimate Load Combinations
1.4D T
1.2D + 1.6L + 0.5( or S or R) T
1.2D + 1.6(or S or R) + (L or 0.5W) T
1.2D + 1.0W + L + 0.5( or S or R) T
1.2D + 1.0E + L + 0.2S T
0.9D + 1.0W T
0.9D + 1.0E T
Service Load Combinations
D + L T
D + ( or S or R) T
D + 0.75L + 0.75( or S or R) T
D + (0.6W or 0.7E) T
D + 0.75L + 0.75(0.6W) + 0.75( or S or R) T
D + 0.75L + 0.75(0.7E) + 0.75S T
0.6D + 0.6W T
0.6D + 0.7E T
D T

## Slide 22: PRELIMINARY DESIGN

## Slide 23: PRELIMINARY DESIGN
Preliminary Dimensions for …
Beams
Slabs
Columns

## Slide 24: PRELIMINARY DESIGN
Preliminary Dimensions of Beams …
Width
Depth (h)
Block | 
300X400 | 1
400X600 | 2
500X700 | 3
600X850 | 4
Minimum depth of beams
Preliminary dimensions of beams

## Slide 25: PRELIMINARY DESIGN
Preliminary Thickness of Slabs …
Two Way Solid Slab
Minimum thickness of two-way solid slabs

## Slide 26: PRELIMINARY DESIGN
Ground Floor
Critical panel in ground floor

## Slide 27: PRELIMINARY DESIGN
First Floor
Critical panel in first floor

## Slide 28: PRELIMINARY DESIGN
Second Floor
Critical panel in second floor

## Slide 29: INTRUDUCTION
Preliminary Thickness of Slabs …
 | Block |  |  |  | 
Floor | Ground Floor | First Floor | Second Floor | Third Floor | Stands
Slab Thickness | 250mm | 250mm | 250mm | 250mm | 250mm
The final preliminary thickness of slabs
Preliminary Thickness of Columns …
Square Columns 800X800

## Slide 30: INTRUDUCTION
Slab Superimposed Dead Load …
Value that will be used (K) | Value | Floor Slab
6 | 5.24 | Ground Floor Slab
6 | 5.1 | First Floor Slab
6 | 5.4 | Second Floor Slab
6 | 3.3 | Third Floor Slab
6 | 5.93 | Stands
4.5 | 4.28 | Stairs
 | Value | Floor Slab
6 | 5.24 | Ground Floor Slab
6 | 5.1 | First Floor Slab
6 | 5.4 | Second Floor Slab
6 | 3.3 | Third Floor Slab
6 | 5.93 | Stands
4.5 | 4.28 | Stairs
Slab superimposed dead load

## Slide 31: THREE-DIMENSIONAL ANALYSIS

## Slide 32: THREE-DIMENTIONAL ANALYSIS
By using ETABS software

## Slide 34: THREE-DIMENTIONAL ANALYSIS
Section Properties …
No. | Section Name | Property Name | Material | Section Type | Dimensions (mm) | Flexural Modifier | Torsional Modifier
1 | Frame sections | B-400X400 | C-40MPa | Rectangular Beam | 400X400 | 0.35 | 0.001
2 |  | B-500X400 | C-40MPa | Rectangular Beam | 500X400 | 0.35 | 0.001
3 |  | B-400X700 | C-40MPa | Rectangular Beam | 400X700 | 0.35 | 0.001
4 |  | B-550X1300 | C-40MPa | Rectangular Beam | 550X1300 | 0.35 | 0.001
5 |  | B-550X1300 | C-40MPa | Rectangular Beam | 550X1300 | 0.001 | 0.001
6 |  | C-800X800 | C-40MPa | Rectangular Column | 800X800 | 0.7 | 0.001
7 |  | C-1200X1200 | C-40MPa | Rectangular Column | 1200X1200 | 0.7 | 0.001
8 | Shell sections | GF-S-300 | C-40MPa | Slab | t = 300 | 0.35 | 0.35
9 |  | F1-S-300 | C-40MPa | Slab | t = 300 | 0.35 | 0.35
10 |  | F2-S-300 | C-40MPa | Slab | t = 300 | 0.35 | 0.35
11 |  | F3-S-300 | C-40MPa | Slab | t = 300 | 0.35 | 0.35
12 |  | STANDS-300 | C-40MPa | Slab | t = 300 | 0.35 | 0.35
13 |  | STAIR-200 | C-40MPa | Slab | t = 200 | 0.001 | 0.001

## Slide 35: THREE-DIMENTIONAL ANALYSIS
Design Load Combinations …
Ultimate Load Combinations
Service Load Combination

## Slide 36: THREE-DIMENTIONAL ANALYSIS
Load Definitions …
Load Patterns
Seismic Load
Load Cases
Response Spectrum Function
Seismic Load Cases
EYD |  | EXD |  | Load Case
Y | X | Y | X | Direction
1532.81 | 459.84 | 459.84 | 1532.81 | Scale Factor
EXD is the dynamic seismic load in X-direction
EYD is the dynamic seismic load in Y-direction

## Slide 37: THREE-DIMENTIONAL ANALYSIS
Verification of Structural Analysis …
Compatibility Check
Equilibrium Check
Difference | ETABS Result | Manual Result | 
0.53 % | 124571.4808 | 125229.3749 | Own Weight
0 % | 65255.2771 | 65255.388 | Superimposed Dead Load
0% | 45663.0048 | 45662.79 | Live Load
Compatibility for the block
Equilibrium for the block

## Slide 38: THREE-DIMENTIONAL ANALYSIS
Check Equilibrium for Base Shear …
201242.5091 | Effective Weight ()
0.057 | Final (X-direction)
0.057 | Final (Y-direction)
11418.72 | 
11418.72 | 
10566.5449 | (ETABS)
10566.5449 | (ETABS)
7.5 % | Difference for
7.5 % | Difference for
201242.5091 | 
0.057 | 
0.057 | 
11418.72 | 
11418.72 | 
10566.5449 | 
10566.5449 | 
7.5 % | 
7.5 % | 
Effective Weight () = DL + SD + 0.25 LL
=

## Slide 39: THREE-DIMENTIONAL ANALYSIS
Checking for Dynamic Response Spectrum …
Model-2 | Model-1 | 
10566.5449 | 10566.5449 | 
9509.8985 | 9751.406 | 
0.90 | 0.92 | Ratio ()
1294.86 | - | Modified Scale Factor
 | 10566.5449 | 
8148.2303 | 8312.9177 | 
0.77 | 0.79 | Ratio ()
1788.96 | 1753.52 | Modified Scale Factor
Model-2 | Model-1 | 
10566.5449 | 10566.5449 | 
9509.8985 | 9751.406 | 
0.90 | 0.92 | 
1294.86 | - | Modified Scale Factor
 | 10566.5449 | 
8148.2303 | 8312.9177 | 
0.77 | 0.79 | 
1788.96 | 1753.52 | Modified Scale Factor

## Slide 40: THREE-DIMENTIONAL ANALYSIS
Structural Irregularities …
Horizontal Irregularities
Model-2 | Model-1 | 
Yes | Yes | Type 1
No | No | Type 2
No | No | Type 3
No | No | Type 4
No | No | Type 5
Horizontal Irregularities

## Slide 41: THREE-DIMENTIONAL ANALYSIS
Structural Irregularities …
Vertical Irregularities
Model-2 | Model-1 | 
Yes | Yes | Type 1
No | No | Type 2
No | No | Type 3
No | No | Type 4
No | No | Type 5
Vertical Irregularities

## Slide 42: THREE-DIMENTIONAL ANALYSIS
Torsional Irregularity …
Model-1
 | Direction | Max drift (mm) | Average drift (mm) | Ratio | Check
Story4 | X | 0.3 | 0.243 | 1.236 | Yes
Story3 | X | 4.362 | 3.572 | 1.221 | Yes
Story2 | X | 2.683 | 2.114 | 1.269 | Yes
Story1 | X | 5.33 | 4.35 | 1.225 | Yes
Story4 | Y | 0.125 | 0.113 | 1.11 | No
Story3 | Y | 1.935 | 1.538 | 1.258 | Yes
Story2 | Y | 1.178 | 0.72 | 1.637 | Yes
Story1 | Y | 6.557 | 4.933 | 1.329 | Yes
Torsional Irregularity
Model-2
 | Direction | Max drift (mm) | Average drift (mm) | Ratio | Check
Story4 | X | 0.2 | 0.164 | 1.216 | Yes
Story3 | X | 2.888 | 2.399 | 1.204 | Yes
Story2 | X | 0.921 | 0.702 | 1.311 | Yes
Story1 | X | 5 | 4.063 | 1.23 | Yes
Story4 | Y | 0.13 | 0.119 | 1.094 | No
Story3 | Y | 1.554 | 1.381 | 1.126 | No
Story2 | Y | 1.289 | 0.81 | 1.591 | Yes
Story1 | Y | 6.435 | 4.883 | 1.318 | Yes

## Slide 43: THREE-DIMENTIONAL ANALYSIS
Stiffness-Soft Story Irregularity…
Model-1
 | Load Case | Stiffness X (KN/m) | Stiffness Y (KN/m) | Ratio % | Check
Story4 | EXD | 10338782 | 14557255.01 | - | -
Story3 | EXD | 1583686.62 | 2445302.293 | 15.3 | Yes
Story2 | EXD | 3510399.98 | 5506136.54 | 221.6 | No
Story1 | EXD | 2222069.98 | 1777157.871 | 63.3 | Yes
Story4 | EYD | 3958362.46 | 17501453.36 | - | -
Story3 | EYD | 656041.952 | 2963182.391 | 16.9 | Yes
Story2 | EYD | 1316516.17 | 7852321.903 | 265.0 | No
Story1 | EYD | 935484.351 | 2181814.705 | 27.9 | Yes
Stiffness-soft story irregularity
Model-2
 | Load Case | Stiffness X (KN/m) | Stiffness Y (KN/m) | Ratio % | Check
Story4 | EXD | 13963507.96 | 15205577 | - | -
Story3 | EXD | 2167724.845 | 2823636 | 15.5 | Yes
Story2 | EXD | 10573830.9 | 8629178 | 487.8 | No
Story1 | EXD | 2379316.502 | 1611536 | 22.5 | Yes
Story4 | EYD | 5557591.047 | 16976553 | - | -
Story3 | EYD | 947317.861 | 3354133 | 19.7 | Yes
Story2 | EYD | 3807720.174 | 11344938 | 338.2 | No
Story1 | EYD | 973867.487 | 2006525 | 17.7 | Yes

## Slide 44: THREE-DIMENTIONAL ANALYSIS
Vertical Geometric Irregularity …
Vertical geometric irregularity is defined to exist where the horizontal dimension of the seismic force-resisting system in any story is more than 130% of that in an adjacent story.

## Slide 45: THREE-DIMENTIONAL ANALYSIS
Check Type of Diaphragm …
Story | Direction | Average displacement (mm) | Mid-Point displacement (mm) | 2*Avg. displacement | Rigid/Flexible
Story1 | X | 5.717 | 4.261 | 11.434 | Rigid
Story2 | X | 8.003 | 5.882 | 16.006 | Rigid
Story3 | X | 11.719 | 8.819 | 23.438 | Rigid
Story4 | X | 11.992 | 9.025 | 23.984 | Rigid
Story1 | Y | 6.067 | 5.189 | 12.134 | Rigid
Story2 | Y | 7.071 | 5.995 | 14.142 | Rigid
Story3 | Y | 9.032 | 7.604 | 18.064 | Rigid
Story4 | Y | 9.791 | 8.734 | 19.582 | Rigid
Type of diaphragm in Model-1
Story | Direction | Average displacement (mm) | Mid-Point displacement (mm) | 2*Avg. displacement | Rigid/Flexible
Story1 | X | 5.487 | 4.085 | 10.974 | Rigid
Story2 | X | 6.445 | 4.756 | 12.89 | Rigid
Story3 | X | 9.334 | 7.111 | 18.668 | Rigid
Story4 | X | 9.512 | 7.252 | 19.024 | Rigid
Story1 | Y | 6.406 | 5.466 | 12.812 | Rigid
Story2 | Y | 7.286 | 6.396 | 14.572 | Rigid
Story3 | Y | 9.131 | 8.005 | 18.262 | Rigid
Story4 | Y | 10.216 | 9.237 | 20.432 | Rigid
Type of diaphragm in Model-2

## Slide 46: THREE-DIMENTIONAL ANALYSIS
Check Amplification of Accidental Eccentricity …
 | Direction | Max displacement (mm) | Average displacement (mm) |  | Amplified Eccentricity =
Story4 | X | 12.26 | 9.923 | 1.0600649 | 0.053
Story3 | X | 11.979 | 9.697 | 1.059751 | 0.053
Story2 | X | 7.923 | 6.389 | 1.0679503 | 0.054
Story1 | X | 5.33 | 4.35 | 1.0425897 | 0.052
Story4 | Y | 7.757 | 6.854 | 0.8894814 | 0.050
Story3 | Y | 7.639 | 6.513 | 0.9553189 | 0.050
Story2 | Y | 6.28 | 5.121 | 1.0443528 | 0.052
Story1 | Y | 5.266 | 4.348 | 1.0186386 | 0.051
 | Direction | Max displacement (mm) | Average displacement (mm) |  | 
Story4 | X | 12.26 | 9.923 | 1.0600649 | 0.053
Story3 | X | 11.979 | 9.697 | 1.059751 | 0.053
Story2 | X | 7.923 | 6.389 | 1.0679503 | 0.054
Story1 | X | 5.33 | 4.35 | 1.0425897 | 0.052
Story4 | Y | 7.757 | 6.854 | 0.8894814 | 0.050
Story3 | Y | 7.639 | 6.513 | 0.9553189 | 0.050
Story2 | Y | 6.28 | 5.121 | 1.0443528 | 0.052
Story1 | Y | 5.266 | 4.348 | 1.0186386 | 0.051
Check amplification of accidental eccentricity (Model-1)
Check amplification of accidental eccentricity (Model-2)
 | Direction | Max displacement (mm) | Average displacement (mm) |  | Amplified Eccentricity =
Story4 | X | 8.722 | 7.111 | 1.04474 | 0.052
Story3 | X | 8.538 | 6.959 | 1.045337 | 0.052
Story2 | X | 5.856 | 4.729 | 1.064881 | 0.053
Story1 | X | 5 | 4.063 | 1.051681 | 0.053
Story4 | Y | 8.559 | 7.587 | 0.883778 | 0.050
Story3 | Y | 8.433 | 6.815 | 1.063335 | 0.053
Story2 | Y | 6.982 | 5.406 | 1.158364 | 0.058
Story1 | Y | 6.153 | 4.715 | 1.182627 | 0.060
 | Direction | Max displacement (mm) | Average displacement (mm) |  | 
Story4 | X | 8.722 | 7.111 | 1.04474 | 0.052
Story3 | X | 8.538 | 6.959 | 1.045337 | 0.052
Story2 | X | 5.856 | 4.729 | 1.064881 | 0.053
Story1 | X | 5 | 4.063 | 1.051681 | 0.053
Story4 | Y | 8.559 | 7.587 | 0.883778 | 0.050
Story3 | Y | 8.433 | 6.815 | 1.063335 | 0.053
Story2 | Y | 6.982 | 5.406 | 1.158364 | 0.058
Story1 | Y | 6.153 | 4.715 | 1.182627 | 0.060

## Slide 47: THREE-DIMENTIONAL ANALYSIS
Effect of P-delta …
 | P |  |  |  |  |  | 
Story4 | 9724.8816 | 3.80E-05 | 1.60E-05 | 830.8738 | 603.593 | 4.45E-04 | 2.58E-04
Story3 | 84947.5908 | 0.001105 | 0.000485 | 5702.0106 | 4568.023 | 1.65E-02 | 9.02E-03
Story2 | 132260.8704 | 0.000681 | 0.000329 | 7163.2859 | 6265.467 | 1.26E-02 | 6.95E-03
Story1 | 206337.5718 | 0.000983 | 0.000961 | 9373.5399 | 9104.205 | 2.16E-02 | 2.18E-02
 | P |  |  |  |  |  | 
Story4 | 9724.8816 | 3.80E-05 | 1.60E-05 | 830.8738 | 603.593 | 4.45E-04 | 2.58E-04
Story3 | 84947.5908 | 0.001105 | 0.000485 | 5702.0106 | 4568.023 | 1.65E-02 | 9.02E-03
Story2 | 132260.8704 | 0.000681 | 0.000329 | 7163.2859 | 6265.467 | 1.26E-02 | 6.95E-03
Story1 | 206337.5718 | 0.000983 | 0.000961 | 9373.5399 | 9104.205 | 2.16E-02 | 2.18E-02
Effect of P-delta (Model-1)
Effect of P-delta (Model-2)
 | P |  |  |  |  |  | 
Story4 | 9724.8816 | 2.50E-05 | 1.60E-05 | 759.5342 | 664.1562 | 3.20E-04 | 2.34E-04
Story3 | 84947.5908 | 0.000731 | 0.000391 | 5240.1378 | 4646.231 | 1.19E-02 | 7.15E-03
Story2 | 132260.8704 | 0.000234 | 0.000325 | 6859.9288 | 6395.609 | 4.51E-03 | 6.72E-03
Story1 | 206337.5718 | 0.000922 | 0.001126 | 9363.5189 | 9131.056 | 2.03E-02 | 2.54E-02
 | P |  |  |  |  |  | 
Story4 | 9724.8816 | 2.50E-05 | 1.60E-05 | 759.5342 | 664.1562 | 3.20E-04 | 2.34E-04
Story3 | 84947.5908 | 0.000731 | 0.000391 | 5240.1378 | 4646.231 | 1.19E-02 | 7.15E-03
Story2 | 132260.8704 | 0.000234 | 0.000325 | 6859.9288 | 6395.609 | 4.51E-03 | 6.72E-03
Story1 | 206337.5718 | 0.000922 | 0.001126 | 9363.5189 | 9131.056 | 2.03E-02 | 2.54E-02

## Slide 48: THREE-DIMENTIONAL ANALYSIS
Story Drift Check …
Allowable Drift /1.3
Story drift does not exceed the allowable drift
 | Direction |  | () | () | 
Story4 | X | 8000 | 0.304 | 1.34 | 92.3
Story3 | X | 4000 | 4.42 | 19.4 | 46.2
Story2 | X | 4000 | 2.72 | 12.0 | 46.2
Story1 | X | 5500 | 5.41 | 23.8 | 63.5
Story4 | Y | 8000 | 0.216 | 0.95 | 92.3
Story3 | Y | 4000 | 2.00 | 8.82 | 46.2
Story2 | Y | 4000 | 1.32 | 5.79 | 46.2
Story1 | Y | 5500 | 6.57 | 28.9 | 63.5
 | Direction |  |  |  | 
Story4 | X | 8000 | 0.304 | 1.34 | 92.3
Story3 | X | 4000 | 4.42 | 19.4 | 46.2
Story2 | X | 4000 | 2.72 | 12.0 | 46.2
Story1 | X | 5500 | 5.41 | 23.8 | 63.5
Story4 | Y | 8000 | 0.216 | 0.95 | 92.3
Story3 | Y | 4000 | 2.00 | 8.82 | 46.2
Story2 | Y | 4000 | 1.32 | 5.79 | 46.2
Story1 | Y | 5500 | 6.57 | 28.9 | 63.5
Story drift for Model-1
Story drift for Model-2
 | Direction |  | () | () | 
Story4 | X | 8000 | 0.232 | 1.02 | 92.3
Story3 | X | 4000 | 2.92 | 12.9 | 46.2
Story2 | X | 4000 | 0.936 | 4.12 | 46.2
Story1 | X | 5500 | 5.07 | 22.3 | 63.5
Story4 | Y | 8000 | 0.208 | 0.915 | 92.3
Story3 | Y | 4000 | 1.88 | 8.27 | 46.2
Story2 | Y | 4000 | 1.30 | 5.72 | 46.2
Story1 | Y | 5500 | 6.46 | 28.4 | 63.5
 | Direction |  |  |  | 
Story4 | X | 8000 | 0.232 | 1.02 | 92.3
Story3 | X | 4000 | 2.92 | 12.9 | 46.2
Story2 | X | 4000 | 0.936 | 4.12 | 46.2
Story1 | X | 5500 | 5.07 | 22.3 | 63.5
Story4 | Y | 8000 | 0.208 | 0.915 | 92.3
Story3 | Y | 4000 | 1.88 | 8.27 | 46.2
Story2 | Y | 4000 | 1.30 | 5.72 | 46.2
Story1 | Y | 5500 | 6.46 | 28.4 | 63.5

## Slide 49: THREE-DIMENTIONAL ANALYSIS
Deflection Check …
Long-term Deflection
Allowable Deflection
Long-term deflection

## Slide 50: THREE-DIMENTIONAL ANALYSIS
Width of Separation …
The width of separation is equal to 70 mm
Max elastic displacement

## Slide 51: CONCRETE STRUCTURAL DESIGN

## Slide 52: CONCRETE STRUCTURAL DESIGN
Design of Slabs …

## Slide 53: CONCRETE STRUCTURAL DESIGN
Design of Beams …
The first hoop shall be located not more than 50 mm from the face of a supporting column.
d/4. 6db. 150 mm.
Spacing of the transverse reinforcement enclosing the lap-spliced bars shall not exceed the lesser of d/4 and 100 mm.
The spacing of transversely supported flexural reinforcing bars shall not exceed 350 mm.

## Slide 54: CONCRETE STRUCTURAL DESIGN
Design of Columns …
The depth of the column at the face One-sixth of the clear span of the column 450 mm
S ≤ 1/4 minimum member dimension.
≤ 6 db.
≤
Lap splicing = 1.3 development length

## Slide 55: CONCRETE STRUCTURAL DESIGN

## Slide 56: PART TWO : STEEL STRUCTURE

## Slide 57: Steel Structure
Steel Structure plan
3D Modeling
Shape of single unit truss
1. Hight = 40.5 m
2. Length = 50m
3. 4 m away from concrete
structure

## Slide 58: Design of Steel
Loads…
Loads
Gravity
Dead
Live
Lateral
Snow
Wind

## Slide 59: Design of Steel
Loads…
Dead Loads: Own weight
Super-imposed dead load = 0.5 KN/m2
Live load = 0.5 KN/m2 (maintenance)
Snow load = 1.5 KN/m2
Wind load

## Slide 60: Wind Loads…
Horizontal part …
Joints and tributary area

## Slide 61: Wind Loads…
Horizontal part …
Wind Load calculation:
- The type of structure is open building.
- Basic Wind Speed,
- Wind directionality factor, .
- Topographic factor, .
- Gust-effect factor
- Mean roof height
- by interpolation
- Velocity pressure,:
- = 0.613 (N/); V in m/s
- = 851.22 N/m2

## Slide 62: Wind Loads…
Horizontal part …
For open structure:
: net pressure coefficient.
To calculate there is three cases for monoslope:

## Slide 63: Wind Loads…
Horizontal part …
Values of

## Slide 64: Wind Loads…
Horizontal part …
Values of pressure:

## Slide 65: Wind Loads…
Vertical part …
For vertical open truss (pressure at vertical joints):
Where:
Vertical Tributary area:

## Slide 66: Design of connections…
Types of members.
Check steel design using ETABS.
Tension and compression forces.
Welding.
Weld fracture
Weld fracture >= F

## Slide 67: THANK YOU