## Slide 1: Structural Analysis and Design of Bakeer Building in Nablus City
By:
Assim Hantoli.
Asem Mohaibish.
Raffat soliman.
Akram Hanoon.
Under supervision of: Dr. Ibrahim Arman.
Fall 2019

## Slide 2: PREFACE
This project aims to design a residential building, which is located in Beit-Wazan in Nablus.
The building consist of 12 similar stories.
The story area is 445 .
The design will consider seismic and gravity loads.

## Slide 3: OUTLINE
Introduction
  Project Description
  Codes & Standards
  Programs
  Materials
  Soil Properties
  Seismic definitions.
  Seismicity of the site & Structure
  Load & Load Combination
Preliminary Design
  Slabs
  Beams
  Columns
  Walls
  Modeling
    Section Modifier
    Response Spectrum Definition
    Model Checks
Design Checks
  Base Shear
  Irregularities checks
  Drift
  P-Delta
  Deflection
  Preliminary Design Check
  Element Design
    Shear Walls
    Columns
    Beams
    Slabs
    Foundation
    Stair
Element Detailing
  Slab
  Beams
  Columns
  Walls
  Foundation
  Stair

## Slide 4
INTRODUCTION

## Slide 5: Project Description
3D view of the building

## Slide 6: Project Description
Ground Floor Plan

## Slide 7: Project Description
Floor 1 to Floor 12 Typical Plan

## Slide 8: Project Description
North Elevation

## Slide 9: Project Description
South Elevation

## Slide 10: Project Description
East Elevation

## Slide 11: Project Description
Section 1-1

## Slide 12: Project Description
Section 2-2

## Slide 13: Codes & Standards
ACI 318-11
ASCE 7-10

## Slide 14: Programs
AutoCAD
ETABS
Revit

## Slide 15: Materials
Steel:
Concrete
Used for | Slabs, Beams, Columns and Shear Walls
Compressive strength | 28 (mpa)
Modules of elasticity | 24870 (mpa)
Unit weight of plain concrete | 23 kN/m3
Unit weight of reinforced concrete | 25 kN/m3
Materials used in structural elements:

## Slide 16: Materials
Materials used in non-structural elements:
Material | Unit Weight (kN/)
Tiles | 26
Blocks | 12
Masonry Stones | 26
Filling Materials | 18
Plastering | 23
Aggregate (gravel) | 17
Concrete Mortar | 23
Material | 
Tiles | 26
Blocks | 12
Masonry Stones | 26
Filling Materials | 18
Plastering | 23
Aggregate (gravel) | 17
Concrete Mortar | 23

## Slide 17: Soil Properties
Bearing Capacity: 380 kPa
Site Class: Soft Rock “Type C”

## Slide 18: Gravity Loads
Gravity loads:
Dead load
Live load:
Area | Floor | Balcony | Stairs
Live load | 2.5 kN/m2 | 3.75 kN/m2 | 5 kN/m2

## Slide 19: Gravity Loads
Super Dead Load
Location | Floor | Exterior beams | Balconies edges | Walls
Super Dead Load | 5 kN/m2 | 15.5 kN/m | 4.5 kN/m | 3.2 kN/m2

## Slide 20: Seismic load
Select risk category
Set the importance factor Ie
Determination of Ss and S1
Determination of seismic design category
Calculate the design spectral acceleration SDS & SD1
Determination of response accelerations Sms and Sm1
Design Coefficients and Factors for seismic Force - Resisting Systems
Determination of Seismic Design Parameters:

## Slide 21: Seismic definitions Selection of Risk Category
According ASCE 7-10
Use risk category III.

## Slide 22: Seismic definitions Set importance factor Ie
I=1.25

## Slide 23: Seismic definitions Determination of Ss and s1
Seismic zone factor (z):
Our project is located in Nablus so the
zone factor (z) =0.2g.

## Slide 24: Seismic definitions Determination of Ss and s1
Empirical formulas have been developed to calculate and based on Z factor:
=
To convert Ss, and S1 from 10% to 2% probability of exceedance the following formula used:

## Slide 25: Seismic definitions Determination of and
Fa = 1.1 , Fv = 1.425 determined from the below tables .
The amplified accelerations, Sms, and Sm1:

## Slide 26: Seismic definitions Calculation of and
Design earthquake spectral response acceleration parameter at short period 0.2s (, and at 1s ():
.

## Slide 27: Seismic definitions Seismic design category
Seismic design category:
According to the previous tables the seismic design category is D.

## Slide 28: Seismic definitions Method of analysis
In this project modal response spectrum method will be used

## Slide 29: Seismic definitions Seismic force resisting system
X-direction selected frames to take the seismic load.

## Slide 30: Seismic definitions Seismic force resisting system
In this project two systems will be used:
Y-direction system:
the system is special reinforced shear walls, with design coefficients as shown in the table below.
Response Modification coefficient Ra | Over strength factor Ω0g | Deflection amplification factor Cdb
6 | 2.5 | 5

## Slide 31: Seismic definitions Seismic force resisting system
In this project two systems will be used:
X-direction system:
the system is special reinforced moment resisting frames, with design coefficients as shown in the table below.
Response Modification coefficient Ra | Over strength factor Ω0g | Deflection amplification factor Cdb
8 | 3 | 5.5

## Slide 32: Load combinations
Ultimate load combinations:
Combination | D | L | Ex | Ey
ULT1 | 1.4 | - | - | -
ULT2 | 1.2 | 1.6 | - | -
ULT3a | 1.31 | 1 | 1.3 | 0.39
ULT3b | 1.31 | 1 | 0.39 | 1.3
ULT4a | 0.79 | - | 1.3 | 0.39
ULT4b | 0.79 | - | 0.39 | 1.39

## Slide 33: Load combinations
Service load combinations:
Combination | D | L | Ex | Ey
Serv1 | 1 | - | - | -
Serv2 | 1 | 1 | - | -
Serv3a | 1.077 | - | 0.91 | 0.273
Serv3b | 1.077 | - | 0.273 | 0.91
Serv4a | 1.0577 | 0.75 | 0.6825 | 0.2047
Serv4b | 1.0577 | 0.75 | 0.2047 | 0.6825
Serv 5a | 0.523 | - | 0.91 | 0.273
Serv 5b | 0.523 | - | 0.273 | 0.91

## Slide 34
Preliminary design

## Slide 35: Preliminary design
Beams:

## Slide 36: Preliminary design
Beams:
Slab: The slab will be Two way U-boot slab.
Group number | Dimensions
1 | 400 x 600 mm
2 | 400 x 500 mm
3 | 400 x 350 mm

## Slide 37: Preliminary design
Columns:
Shear walls:
Shear wall thickness=20cm
Group number | Dimensions
1 | 400 x 400 mm
2 | 400 x 600 mm
3 | 400 x 800 mm
4 | 400 x 1000 mm
5 | 900 x 600 mm

## Slide 38: Modeling
U-Boot slab Modifiers:
M11 | 0.2993
M22 | 0.2993
M13 | 0.5565
V13 | 0.2238806
V23 | 0.2238806
F11 | 0.5565032
F22 | 0.5565032
weight | 0.6546
mass | 0.6546

## Slide 39: Modeling
Beams modifiers:
Section Properties | Modifier
Torsional Constant | 0.01
Moment of inertia about 2 axis | 0.35
Moment of inertia about 3 axis | 0.35
Mass | 1
Weight | 1

## Slide 40: Modeling
Columns modifiers:

## Slide 41: Modeling Response spectrum definition

## Slide 42: Modeling Load cases
Load cases definition:
Load case in X direction:

## Slide 43: Modeling Load cases
Load cases definition:
Load case in Y direction:

## Slide 44: Modeling Equivalent static load
X-direction

## Slide 45: Modeling Equivalent static load
Y-direction

## Slide 46: Modeling Mass source

## Slide 47: Modeling Diaphragm definition

## Slide 48: Model checks Compatibility check

## Slide 49: Model checks Equilibrium check
ETABS base reactions.

## Slide 50: Model checks Equilibrium check
Difference between manual calculations and ETABS results:
Load Pattern | Manual (kN) | ETABS (kN) | Difference (%)
Dead Load | 53991 | 53464 | 0.9
Live Load | 14403 | 14495 | 0.6
Super Dead | 41843 | 42215 | 0.8

## Slide 51: Model checks Stress strain check
Slab:
Moment from ETABS = 32.65 kN.m

## Slide 52: Model checks Stress strain check
Column:
Axial load manually = 1248 kN
Axial load from ETABS = 1298 kN

## Slide 53: Design checks
Minimum number of modes.
Base shear check.
Irregularities check.
Drift check.
P-delta check.
Deflection check.

## Slide 54: Design checks Minimum number of modes
ASCE 7-10 require cumulative modal participating mass ratio (Sum UX and Sum UY) of at least 90% for response spectrum analysis. The required number of modes to get this percent is 12 mode.

## Slide 55: Design checks Base shear check
Base shear manually:
is computed according to the following equations:

## Slide 56: Design checks Base shear check Y-direction
Base shear manually:
ASCE 7-10 requires that the calculated fundamental period of the structure not to be greater than the product of approximate period () and upper limit coefficient .
Ct=0.0488, hn=40.56, x=0.75, Cu=1.4
T from the fundamental mode=0.941

## Slide 57: Design checks Base shear check Y-direction
Base shear manually:
and
Cs=0.0788
W= KN

## Slide 58: Design checks Base shear check
Base shear From ETABS:
 | FX (kN) | FY(kN)
Response Spectrum |  | 
EQx | 2749.7545 | 451.8108
EQy | 602.4151 | 5820.5974
Equivalent Static Force |  | 
Ex | -3269.5551 | 1.83E-06
Ey | 7.552E-07 | 7772.0024

## Slide 59: Design checks Base shear check ETABS results
 | FX (kN) | FY(kN)
Response Spectrum |  | 
EQx | 2749.7545 | 451.8108
EQy | 602.4151 | 5820.5974
Equivalent Static Force |  | 
Ex | -3269.5551 | 1.83E-06
Ey | 7.552E-07 | 7772.0024

## Slide 60: Design checks Base shear check
direction | Base shear manually | Base shear from ETABS (Equivalent static) | Base shear from ETABS (Response Spectrum) | (v/vt) | Difference
X | 3277 | 3269 | 2749 | 1.189159694 | 0.24%
Y | 7792 | 7770 | 5820 | 1.335051546 | 0.28%

## Slide 61: Design checks Modification of RS

## Slide 62: Design checks torsional irregularity check
According to ASCE 7-10, there is no torsional irregularity if (max drift/average drift)<1.2 or Ax<1.
To check the torsional irregularity the following combination used:
D+L+SD+Eqx+Eqy

## Slide 63: Design checks torsional irregularity check X
Story | Combination | Direction | Max Displacement | Avg Displacement | (Max/avg) DISP | Ax
Story12 | Dx Max | X | 39.862 | 39.12 | 1.019 | 0.721084
Story11 | Dx Max | X | 37.143 | 36.56 | 1.016 | 0.716844
Story10 | Dx Max | X | 34.395 | 33.794 | 1.018 | 0.719669
Story9 | Dx Max | X | 31.38 | 30.747 | 1.021 | 0.723917
Story8 | Dx Max | X | 28.07 | 27.41 | 1.024 | 0.728178
Story7 | Dx Max | X | 24.497 | 23.834 | 1.028 | 0.733878
Story6 | Dx Max | X | 20.708 | 20.064 | 1.032 | 0.7396
Story5 | Dx Max | X | 16.768 | 16.124 | 1.04 | 0.751111
Story4 | Dx Max | X | 12.761 | 12.166 | 1.049 | 0.764167
Story3 | Dx Max | X | 8.817 | 8.319 | 1.06 | 0.780278
Story2 | Dx Max | X | 5.141 | 4.793 | 1.073 | 0.799534
Story1 | Dx Max | X | 1.931 | 1.77 | 1.091 | 0.826584

## Slide 64: Design checks torsional irregularity check Y
Story | Combination | Direction | Max displacement | Avg displacement | (Max/avg) DISP | Ax
Story12 | Dy Max | Y | 52.748 | 45.226 | 1.166 | 0.944136
Story11 | Dy Max | Y | 47.607 | 40.892 | 1.164 | 0.9409
Story10 | Dy Max | Y | 42.38 | 36.449 | 1.163 | 0.939284
Story9 | Dy Max | Y | 37.064 | 31.915 | 1.161 | 0.936056
Story8 | Dy Max | Y | 31.705 | 27.328 | 1.16 | 0.934444
Story7 | Dy Max | Y | 26.364 | 22.747 | 1.159 | 0.932834
Story6 | Dy Max | Y | 21.134 | 18.253 | 1.158 | 0.931225
Story5 | Dy Max | Y | 16.128 | 13.944 | 1.157 | 0.929617
Story4 | Dy Max | Y | 11.485 | 9.937 | 1.156 | 0.928011
Story3 | Dy Max | Y | 7.365 | 6.368 | 1.157 | 0.929617
Story2 | Dy Max | Y | 3.948 | 3.394 | 1.163 | 0.939284
Story1 | Dy Max | Y | 1.42 | 1.162 | 1.222 | 1.037003

## Slide 65: Design checks Drift check
Allowable story drift according to ASCE7-10:

## Slide 66: Design checks Drift check X
Story | Combination | Direction | Elastic drift(mm) | Cd/I | Design drift(mm) | Limit(mm) | OK or NOT
Story12 | Dx Max | X | 0.00293384 | 4.4 | 0.012909 | 0.0507 | OK
Story11 | Dx Max | X | 0.0033462 | 4.4 | 0.014723 | 0.0507 | OK
Story10 | Dx Max | X | 0.00361998 | 4.4 | 0.015928 | 0.0507 | OK
Story9 | Dx Max | X | 0.00383292 | 4.4 | 0.016865 | 0.0507 | OK
Story8 | Dx Max | X | 0.00398502 | 4.4 | 0.017534 | 0.0507 | OK
Story7 | Dx Max | X | 0.00406952 | 4.4 | 0.017906 | 0.0507 | OK
Story6 | Dx Max | X | 0.00410332 | 4.4 | 0.018055 | 0.0507 | OK
Story5 | Dx Max | X | 0.0041236 | 4.4 | 0.018144 | 0.0507 | OK
Story4 | Dx Max | X | 0.00402558 | 4.4 | 0.017713 | 0.0507 | OK
Story3 | Dx Max | X | 0.0037349 | 4.4 | 0.016434 | 0.0507 | OK
Story2 | Dx Max | X | 0.00325832 | 4.4 | 0.014337 | 0.0507 | OK
Story1 | Dx Max | X | 0.00192998 | 4.4 | 0.008492 | 0.0507 | OK

## Slide 67: Design checks Drift check Y
Story | Combination | Direction | Elastic drift(mm) | Cd/I | Design drift(mm) | Limit (mm) | OK or NOT
Story12 | Dy Max | Y | 0.00517478 | 4 | 0.0206991 | 0.0507 | OK
Story11 | Dy Max | Y | 0.0052728 | 4 | 0.0210912 | 0.0507 | OK
Story10 | Dy Max | Y | 0.00536406 | 4 | 0.0214562 | 0.0507 | OK
Story9 | Dy Max | Y | 0.005408 | 4 | 0.021632 | 0.0507 | OK
Story8 | Dy Max | Y | 0.00537758 | 4 | 0.0215103 | 0.0507 | OK
Story7 | Dy Max | Y | 0.00525928 | 4 | 0.0210371 | 0.0507 | OK
Story6 | Dy Max | Y | 0.00502606 | 4 | 0.0201042 | 0.0507 | OK
Story5 | Dy Max | Y | 0.00465426 | 4 | 0.018617 | 0.0507 | OK
Story4 | Dy Max | Y | 0.00412698 | 4 | 0.0165079 | 0.0507 | OK
Story3 | Dy Max | Y | 0.00342056 | 4 | 0.0136822 | 0.0507 | OK
Story2 | Dy Max | Y | 0.00253162 | 4 | 0.0101265 | 0.0507 | OK
Story1 | Dy Max | Y | 0.0014196 | 4 | 0.0056784 | 0.0507 | OK

## Slide 68: Design checks P-delta check
P-Delta is concerned with stability of the structure, P-Delta effect may be ignored if the stability index () is less than 0.1 as defined in ASCE 7-10.
Where:
 = The Stability Index
P = Total Unfactored vertical design load.
= Design Story Drift.
= Seismic Shear Force.
H = Story height
= deflection amplification factor.

## Slide 69: Design checks P-delta check X
Story | P | Drift | Shear | H | ɵ | Allowable limit
 | kN | m | kN | m |  | 
Story12 | 10309.9318 | 0.0129089 | 664.9687 | 40.56 | 0.00112 | 0.1
Story11 | 19392.3555 | 0.01472328 | 1197.3252 | 37.18 | 0.00146 | 0.1
Story10 | 28474.7789 | 0.01592791 | 1576.2675 | 33.8 | 0.00193 | 0.1
Story9 | 37568.5758 | 0.01686485 | 1851.4846 | 30.42 | 0.00256 | 0.1
Story8 | 46662.2552 | 0.01753409 | 2063.7157 | 27.04 | 0.00333 | 0.1
Story7 | 55755.9347 | 0.01790589 | 2248.0451 | 23.66 | 0.00427 | 0.1
Story6 | 64849.7318 | 0.01805461 | 2432.797 | 20.28 | 0.00539 | 0.1
Story5 | 73943.4115 | 0.01814384 | 2630.2819 | 16.9 | 0.00686 | 0.1
Story4 | 83037.0912 | 0.01771255 | 2836.5143 | 13.52 | 0.00872 | 0.1
Story3 | 92144.3962 | 0.01643356 | 3030.6123 | 10.14 | 0.0112 | 0.1
Story2 | 101238.0759 | 0.01433661 | 3187.8897 | 6.76 | 0.01531 | 0.1
Story1 | 110332.7478 | 0.00849191 | 3271.3593 | 3.38 | 0.01926 | 0.1

## Slide 70: Design checks P-delta check Y
Story | P | Drift | Shear | H | ɵ | Allowable limit
 | kN | m | kN | m |  | 
Story12 | 10309.9318 | 0.02069912 | 1405.5207 | 40.56 | 0.00094 | 0.1
Story11 | 19392.3555 | 0.0210912 | 2669.2404 | 37.18 | 0.00103 | 0.1
Story10 | 28474.7789 | 0.02145624 | 3669.549 | 33.8 | 0.00123 | 0.1
Story9 | 37568.5758 | 0.021632 | 4473.544 | 30.42 | 0.00149 | 0.1
Story8 | 46662.2552 | 0.02151032 | 5151.5316 | 27.04 | 0.0018 | 0.1
Story7 | 55755.9347 | 0.02103712 | 5745.1959 | 23.66 | 0.00216 | 0.1
Story6 | 64849.7318 | 0.02010424 | 6271.497 | 20.28 | 0.00256 | 0.1
Story5 | 73943.4115 | 0.01861704 | 6737.3889 | 16.9 | 0.00302 | 0.1
Story4 | 83037.0912 | 0.01650792 | 7143.4311 | 13.52 | 0.00355 | 0.1
Story3 | 92144.3962 | 0.01368224 | 7474.182 | 10.14 | 0.00416 | 0.1
Story2 | 101238.0759 | 0.01012648 | 7699.4617 | 6.76 | 0.00492 | 0.1
Story1 | 110332.7478 | 0.0056784 | 7798.7015 | 3.38 | 0.00594 | 0.1

## Slide 71: Design checks Deflection check
The deflection check will consider:
Immediate deflection.
Long term deflection.
Allowable deflection according to ACI code:

## Slide 72: Design checks Deflection check
Immediate deflection:
Allowable values:
Allowable value on balconies
The figure shows the deflection from live load, and the deflection is less than allowable deflection.

## Slide 73: Design checks Deflection check
Long term deflection:
Long term deflection:
Where:
Immediate live load deflection
Immediate dead load deflection
= Immediate sustained live load deflection
Multiplier for additional deflection due to long-term effects
Using ,
Allowable value on balconies

## Slide 74: Design checks Deflection check
Long term deflection:
The long term defection on the slab is 24.
Long term deflection on balconies is 25.
So the deflection is less than the allowable limits.

## Slide 75
Design

## Slide 76: Design
In order to design this project several models used:
The first: is the model with out any changes.
The second: is the model with the shear modifiers of hidden beams columns, and shear walls set to zero.
The third: is the model with the shear modifiers of all the columns set to zero.
The fourth: is the model without the shear walls.

## Slide 77: Changes on preliminary design
Beams:
Group number | Dimensions
1 | 600 x 600 mm
2 | 600 x 650 mm
3 | 600 x 350 mm

## Slide 78: Changes on preliminary design
Columns:
Group number | Dimensions
1 | 600 x 600 mm
2 | 600 x 600 mm
3 | 600 x 800 mm
4 | 600 x 1000 mm
5 | 900 x 600 mm

## Slide 79: Changes on preliminary design
Walls:
Wall A: 20 cm.
Wall B: 25 cm.
Wall C: 30 cm.

## Slide 80: Elements design
Beams design.
Columns design.
Shear walls design.
Slab design.
Stairs design.
Matt foundation design.

## Slide 81: Beams design
First step to check if the beam will behave as a flexural member:
The factored axial load should be less than 0.1 Ag f′c.
25<1092 so design as beam.

## Slide 82: Beams design
Dimensions limit:
Clear span ℓn shall be at least 4d
Lu = 3.71 – 0.6 = 3.11 4(0.59) = 2.36 m
Width bw shall be at least the lesser of 0.3h and 250 mm.
bw = 600 mm 0.3(650) = 195 mm 250 mm
Projection of the beam width beyond the width of the supporting column on each side shall not exceed the lesser of c2 and 0.75c1.
Transverse projection in column = 0 .

## Slide 83: Beams design
Design for flexure:
Maximum negative moment on the beam:
ρ =
As = 0.005751*600*590 = 2036 mm2

## Slide 84: Beams design
Design for flexure:
Check if compression steel is needed:
The compression reinforcements are required if a > amax.
𝞮cmax=0.003
𝞮smin=0.005
So a = 59 mm.
Cmax = 221mm
A max = 188mm
A < a max  no need for compression reinforcements.

## Slide 85: Beams design
The ETABS results:
%Difference = (2036-2069)/2036 *100% =-1.6% < 10% →Ok.

## Slide 86: Beams design
Shear design:
Design shear force shall be the max of:
Ve = +
Vu.
Mpr = Md = As fy (d-a/2)
where:
= 1 and 1.25 fy shall be used.

## Slide 87: Beams design
Shear design:
Vg= 152.5 kN

## Slide 88: Beams design
Shear design:
Ve = +
Vu =630 kN.
Design shear= 630 kN.

## Slide 89: Beams design
Shear design:
ETABS results:

## Slide 90: Columns design
Column slenderness:
The column selected for the check is 600*600mm:
In non-sway (braced) frames, slenderness effects can be ignored if:
k will assumed to be 1.0.
lu: length of the column from the faces of the beams = 3.38 – 0.65 = 2.73 m.
r: radius of gyration = I/A, approximately = 0.3h = 0.30 x 6.0 = 0.18 m.

## Slide 91: Columns design
Column slenderness:
The check will done with gravity loads:
M1= -27 kN.m
M2= 21 kN.m
Slenderness ratio = = 9.1 ,
Slenderness may be ignored.

## Slide 92: Columns design
Column slenderness:
In sway (unbraced) frames, slenderness effects can be ignored if:
ΨA =0 (fixed end).
ΨB=1.1
K=1.3
Slenderness ratio = = = 19.7,
which is less than 22,
so the column is considered to be short.

## Slide 93: Columns design
Dimensions limits:
The shortest cross sectional dimension is at least 300 mm.
The ratio of the shortest cross-sectional dimension to the perpendicular dimension shall be at least 0.4.

## Slide 94: Columns design
Longitudinal reinforcements check:
Pu= 3881 kN.
M3=373 kN.m
M2=165 kN.m
The column will be reinforced with 1%.
To check the adequacy of the reinforcements,
Breslar method will be used:

## Slide 95: Columns design
𝞍Pn=5035 kN.
3881 < 5035 Ok.

## Slide 96: Columns design
Strong column weak beam check:
A requirement for special columns that specify a minimum flexural strength for columns is:
ΣMnc ≥ (6/5)ΣMnb
ΣMnb = 674.4 kN.m
ΣMnc = 1199.7 kN.m
1.2 ΣMnb = 1.2 x 674.4 kN.m = 809.3 kN.m < ΣMnc = 1199.7 kN.m →Ok.

## Slide 97: Columns design
Shear design check:
Design shear= max(Ve, Vu)
Mpr3 = Mpr4 =281.25 kN.
VE =(281.25*2)/2.73=206 kN.
Vu =226 kN
Design shear = 226 kN.

## Slide 98: Columns design
Shear design check:
Shear reinforcement calculation:
Vs = Vn – Vc
Vs = – 0 = 301 kN.
Av/S = = = 1.52 mm2/mm
ETABS result for Av/S = 1.538 mm2/mm
Difference percentage = 1.18% <10%, acceptable.

## Slide 99: Walls design
Spandrel design:
The figure shows the wall that will be checked
H=2.08m
Ln=1.8m

## Slide 100: Walls design
Spandrel design:
Flexural design:
Mu = 1119 kN.m.
ρ =
As = ρL Ag = 0.0029(2080)(300) =1809 mm2
%Difference = (1809-1872)/1809*100 = 3.4%
3.4%<10%  ok.

## Slide 101: Walls design
Spandrel design:
Shear design:
For Vu = 1253 kN.
ØVc = *0.6*1872*300 /1000 =303 kN.
ØVs = 1253 - 303 =950 kN.
Av/s =ØVs/ Ø d fy =950/(0.6*1.8*420)*1000 = 2013 mm2/m.
%Difference = (2013-2044)/2013*100 = 1.5%
Less than 10% Ok for shear reinforcement.

## Slide 102: Walls design
Spandrel design:
Spandrel diagonal reinforcements:
Coupling beams with (ℓn/h) < 2 and with Vu ≥ 0.33 λ Acw shall be reinforced diagonally.
So the spandrel reinforcements required.

## Slide 103: Walls design
Spandrel design:
Spandrel diagonal reinforcements:
%difference = 0.2% ok.

## Slide 104: Walls design
Pier design:

## Slide 105: Walls design
Pier design:
Flexural design:
Length of pier = 4053 mm.
Thickness =250 mm.
1/Pn = 1/Pnx + 1/Pny – 1/P0
P0 = 13115 kN.
Pnx and Pny from interaction diagrams.

## Slide 106: Walls design
Pier design:
Flexural design:
ETABS results:

## Slide 107: Walls design
Pier design:
Flexural design:
For Mu3 = 2927kN.m, Pn = 13177 kN.
For Mu2 = 0.1617 kN.m, Pn = 13177 kN.
𝞍Pn=13239 kN>4047  ok.
Chart: 
| -2.9841000000000002 | 215.08940000000001 | 363.24869999999999 | 470.40649999999999 | 537.21360000000004 | 566.01779999999997 | 631.27239999999995 | 658.46870000000001 | 508.79039999999998 | 285.1728 | 4.3840000000000003
Interaction M2 | 13177.2058 | 13177.2058 | 12771.544 | 11020.9141 | 9236.2981 | 7394.8095 | 6863.127 | 6060.8411 | 3863.1101 | 1394.3028 | -1169.0751
Chart: 
| 0 | 3159.2064 | 5433.7876999999999 | 7094.4579000000003 | 8148.2218000000003 | 8608.6702999999998 | 9782.7245000000003 | 10282.442499999999 | 7921.3176999999996 | 4533.3653000000004 | 0
Interaction M3 | 13177.2058 | 13177.2058 | 13023.3761 | 11379.2063 | 9704.0911 | 7979.8992 | 7259.0144 | 6186.7444 | 3753.6482 | 1320.552 | -1169.0751

## Slide 108: Walls design
Pier design:
Shear design:
V2=1195 kN.
V3=0.6 kN.
ØVc = *0.75*4053.2*190 /1000 = 509 kN
Ok for minor shear.

## Slide 109: Walls design
Pier design:
Shear design:
For major shear
= 804 kN.
Vu= 1195 kN.
The computed Av/s less than the minimum reinforcement ration=0.0025.

## Slide 110: Walls design
Pier design:
Boundary element check:
The stress method will be used for this check:
If compressive stresses exceeds a nominal critical value equal to 0.2fc. Then the boundary element is required.

## Slide 111: Walls design
Pier design:
Boundary element check:
Stress =10.38 > 5.6 mpa.
So the boundary element required.

## Slide 112: Walls design
Pier design:
Boundary element check:
Length of boundary element is the greater of {C – 0.1Lw} and {C/2 }:
C – 0.1Lw = 1605.3 – 0.1 (4030) = 660 mm
C/2 = 1605.3/2 =802 mm
Use 14 ø16 for each end.

## Slide 113: Slab design
Shear check:

## Slide 114: Slab design
Shear check:
V13
V23

## Slide 115: Slab design
Shear check:
Vu=114 kN>
So shear reinforcements required:
Vs = Vn – Vc
Vs = – 30.75 = 121.25 kN.
Av/S = = = 931 mm2/m
Use 1 ø 10 / 8cm.

## Slide 116: Slab design
Flexural design:
AS min = 630 mm2
5 ø 14 /m.
M min = 88.2 kN.m
All the moment less than minimum

## Slide 117: Design of foundation
Type of foundation:
Percent of the foundation to the floor area = 320/445 = 71%.
So mat foundation will be used.

## Slide 118: Design of foundation
Soil pressure:
The pressure is less than the bearing capacity.

## Slide 119: Design of foundation
Punching check:
The foundation thickness will be used is 1.3m.

## Slide 120: Design of foundation
Wide beam shear

## Slide 121: Design of foundation
Flexural design:
Thus, one can use 525mm/m (2453.12 mm2)
M min = 1120 kN.m
All the moment is less than minimum.

## Slide 122: Stairs design
Check for shear:

## Slide 123: Stairs design
Check for shear:

## Slide 124: Stairs design
Flexural design:
M min = 14 kN.m

## Slide 125
ELEMENT DETAILS

## Slide 126: Slab Details

## Slide 127: Beam Details

## Slide 128: Column Details

## Slide 129: Column Details

## Slide 130: Wall Details

## Slide 131: Wall Details

## Slide 132: Mat Details

## Slide 133: Mat Details

## Slide 134: Stair Details

## Slide 135: Stair Details

## Slide 136: References
ACI Committee 318, “Building Code Requirements for Structural Concrete (ACI 318M-11)”, American Concrete Institute, Michigan, 2011.
ASCE Committee, “American Society of Civil Engineers, Minimum Design Loads for Buildings and Other Structures” Edition 7-10.
ETABS 2016 design documentations.