## Slide 1
Structural Analysis and Design of Palestine Red Crescent Society School For Deaf
An-Najah National University
Faculty of Engineering
Civil Engineering Department
Graduation Project II

## Slide 2
Supervisor Name: Dr. Munther Diab
AcademicYear: 2020-2021
Prepared by: Ahmad yahya 11714678
Madleen Bzoor 11612158
Mohammad Ibrahim 11714763
Obaida Zaben 11440709
Rasha Yameen 11715486

## Slide 3: Outline
General Description.
Structural System Design and Analysis.
Three Dimensional Modeling & Analysis.
Final Design of Structural Elements.

## Slide 4
General Description.

## Slide 5
Project Description :
This project is analysis and design The Palestine Red Crescent Society School for the Deaf in Ramallah.
This building has seven floors, two of them Underground (basement) and five above ground . This building includes: classrooms, halls, mechanical rooms, various laboratories, Elevators and water tanks

## Slide 6
Floor Name | Floor Height (m) | Floor Area (m2)
The second Basement | 3.9 | 813.95
The first Basement | 3.9 | 711
The ground floor | 3.9 | 629.69
The first floor | 3.9 | 675.02
The second floor | 3.9 | 675.02
The third floor | 3.9 | 675.02
The fourth floor | 3.9 | 675.02
Roof | 2.5 | 22.4
  General Information:

## Slide 7
Architectural Plans:
For Basement 1
For Basement 2

## Slide 8
For first floor
For Ground floor

## Slide 9
3D Model

## Slide 10
  Codes and standards:
  American Society for Civil Engineering (ASCE 7-16).
  American Society for Materials (ASTM).
  American Concrete Institute (ACI 318- 14)
  International Building Code (IBC- 2018).

## Slide 11
There are two types of materials which used in the building, such as :
Structural element materials : concrete and steel.
For concrete :
For Steel :
Materials
Property | Value
Cylindrical Compressive strength ( fc ) | 28 MPa
Modulus of elasticity ( Ec) | 24.8 GPa
Unit weight (Ɣ) | 25 KN/m3
Property | Value
Yielding strength (fy) | 420 MPa
Modulus of elasticity ( Es) | 200 GPa

## Slide 12
2. Nonstructural element materials : blocks , tiles , masonry stone and wood.
Material | Unit Weight Ɣ(kN/m3)
Tiles | 27
Blocks | 15
Masonry Stones | 27
Filling Materials | 18
Plaster | 23
Concrete Mortar | 23
Aggregate | 15
Sand | 18

## Slide 13
The common types of loads on the structures are as follow:
Gravitational loads such as: Live, Dead and Superimposed Dead loads.
Dead Load :
It is mainly the own weight of the structural elements and any permanent equipment, which can be defined as the load that does not change with time progressing.
Loads :

## Slide 14
Live Load :
It can be defined as the loads that are variable by time progressing. However, it is mainly caused by people, furniture, or any other movable objects
Occupancy or use | Live Load (kN/m2)
Laboratories | 4.79
Class room | 1.92
Corridors in first floor | 4.79
Corridors above first floor | 3.83
Bathrooms | 1.92
Dining rooms and restaurants | 4.79
stairs | 4.79
Use Live Load for all floors = 5 KN/m2

## Slide 15
Superimposed Dead Load :
This load is mainly caused by the nonstructural elements of the building, it
consists of the weight of walls, floors, ceilings, partitions, finishes, cladding
and fixed service equipment, such as mechanical ducts and electrical wires.

## Slide 16
Superimposed Dead Load :
Calculation far Superimposed dead load :
Floor Layers :
Total weight of layers = 0.03*27+0.02*23+0.1*18=3.07 KN/m2

## Slide 17
Internal partitions :
Total superimposed dead load from internal partitions = 1.3m2
Total super dead load on floor = 1.3+ 3.07= 4.37 KN/m2 from partitions and flooring.
Use 5 KN/m2 has been taken as conservative value.

## Slide 18
2. Lateral loads such as: wind, soil pressure and earthquakes .
Lateral Soil Pressure:
In the design of structures below grade, provision shall be made for the lateral pressure of adjacent soil.

## Slide 19
ASCE7-16 code will be used for seismic analysis to evaluate the building under
Lateral forces.
Earthquake Load :

## Slide 20
Load Combinations :
Ultimate Load Combination
1.4D
1.2 D + 1.6 L+0.5S
1.2 D + L+1.6S
1.2 D + 1.0W + L+0.5S
1.2 D + 1.0E + L+0.2S
0.9D+1.0W
0.9D+1.0E
Service Load Combination
D
D+L
D+S
D+0.75(0.6W)+0.75L+0.75S
D+0.75(0.7E)+0.75L+0.75S
0.6D+0.6W
0.6D+0.7E

## Slide 21
ETABS 2018 to Build a 3D model for the structure, and to take reinforcing steel results for structural elements.
AutoCAD 2017 to draw plans, and reinforcing details.
SAFE 2016 to design the footing .
Computer Programs :

## Slide 22
Structural System Design and Analysis.

## Slide 23
Structural System:
Wall bearing structure
Moment Resisting Frame
Building System
The Dual system

## Slide 24
Structural Element:
Slab System
Beams System
Columns System

## Slide 25
Preliminary Design :
Slab Thickness :
The ratio of the longer to the shorter side (L/B) of the slab less than 2 so it’s preferable to design the slab as two way slab.
To find an initial thickness of slabs, take the critical panel as seen in figure below :

## Slide 26
ACI Code for minimum slab thickness in two way slabs with beams between all supports .
Use

## Slide 27
Beams Dimensions :
Beams have been designed according to the ACI code :

## Slide 28
Beam Direction | Width (mm) | Depth (mm)
X-Direction | 500 | 650
Y-Direction | 300 | 400

## Slide 29
Column Dimensions :
Column | Width (mm) | Depth (mm)
C1 | 400 | 550
C2 | 800 | 600
C3 | 550 | 250

## Slide 30
Wall Thickness :
Wall | Depth (mm)
W1 | 300
W2 | 200
W3 | 250

## Slide 31
Modifiers for structural elements:
structural elements | Modifiers
Slab | 0.25
Beams | 0.35
Columns | 0.7
Wall | 0.7

## Slide 32
Structural Model Verification :
Compatibility Check :

## Slide 33
Equilibrium Check :
Load Type | Hand Result | ETABS Result | %Difference
Dead | 58223.9 | 58186.25 | 0.06%
SD | 29997.75 | 29997.76 | 0.00%
Live | 23327.56 | 23327.56 | 0.00%

## Slide 34
Internal Forces Check :
Results from ETABS :
M1 =111.1 KN.m
M2 =124KN.m
M3 =118 KN.m
(M1+M3 )/ 2 +M2 = (111.1+118)/ 2 +124 = 238.5 KN.m
Result Manually :
Mu = ( ) / 8 =5*5*(8.6)2 /8 = 231 KN.m
%Error =(238.5 – 231 / 231)*100% = 3%> 10% OK
Fream Check :

## Slide 35
Deflection Check :
- The check is done on the fourth slab.
Using the following equation:
Long term Deflection = 2D+2SD+1.25L
Long term Deflection =
45.5 - = 34.6 mm
Deflection = L/240=9400/240=39.1> 34.6mm OK

## Slide 36
In this section, check if the capacity of slab to resist shear force by reading Vu from ETABS and compare with Vc of slab:
Results from ETABS in B1 based on ultimate loads as shown in the following figures:
Slab shear Check :

## Slide 37
Based on results Vu <  OK

## Slide 38
Three Dimensional Dynamic Evaluation

## Slide 39
Determine the Risk Category:
The building is used for educational purposes. Therefore, the risk category was determined as shown in Table 1.5-1:

## Slide 41
Determine the Importance Factor Ie:
The importance factor is a function from the risk category and it is determined from Table 1.5-2 :

## Slide 42
Determine Site Soil Classification:
The selecting of site class is based on soil stiffness. According to Table 20.3-1, the type of soil is rock with allowable bearing capacity = 450 KN/m2.
So the site class is (B).

## Slide 43
  Mapped acceleration parameters:
    Ss = 0.625
    S1 = 0.352
 | 2% Exceedance | 
 | Ss | S1
Using zones |  | 
Ramallah Z=0.15 |  | 
 | 2% Exceedance | 
 | Ss | S1
Using zones |  | 
Ramallah Z=0.15 |  | 

## Slide 44
Define the Site Coefficients, Fa and Fv:
These coefficients are based on site class and mapped spectral accelerations, Ss & S1.

## Slide 45
Spectral Response Acceleration Parameters :
SMS = Fa·SS = 0.9 X 0.625= 0.5625
SM1 = Fv·S1 = 0.8 X 0.352 = 0.2816
Design Spectral Acceleration Parameters :
SDS = 2/3.SMS = 0.375
SD1 = 2/3.SM1 = 0.188

## Slide 46
Seismic design category (SDC): C

## Slide 47
The Fundamental Natural Period:
According to ASCE7-16 Code, the fundamental period in each direction calculated as follows:
T = Cu Ta
By Using the Interpolation Cu =1.524

## Slide 48
Section 12.8.2.1 of the ASCE7-16 provides an empirical formula to calculate the approximate period , Ta as follows:
Ta = Ct (ℎn)x
T = 1.524X 0.622 = 0.95 sec.

## Slide 49
The Seismic Analysis Methods :
Equivalent Lateral Force Method (ELF)
Modal Response Spectrum Method (MRS):
Time History

## Slide 50
These factors will be determined according to the types of lateral force resisting system listed in Table 12.2-1 of ASCE7-16 code.
Determine Design Coefficients and Factors for LFRS:
According to the Table 12.2-1 in ASCE7-16, the LFRS will be Building Frame System with Ordinary reinforced concrete shear walls and check using equivalent lateral force procedure to make sure that shear walls take the lateral forces.

## Slide 52
Response modification coefficient (R) = 5
Overstrength factor (Ω0 ) = 2.5
Deflection amplification factor (Cd) = 4.5
Direction | Shear wall reactions (KN) | Total Base shear(KN) | % of load
X-direction | 6493.2 | 6494.4 | 99.98%
Y-direction | 4573.4 | 4576.7 | 99.99%

## Slide 53
Equivalent Lateral Force Method (ELF) :

## Slide 54
Hand calculations for ELF:

## Slide 55
Direction | Hand (KN) | ETABS (KN) | Difference %
X | 6581.1 | 6502.2 | 1.2%
Y | 4635 | 4597.8 | 0.8 %
The difference between hand results and ETABS results less than the allowable (10%) so it is Ok.

## Slide 56
  Structural Irregularities Checks:
    Horizontal Irregularity:

## Slide 57
  1a-Torsional irregularity:
Accidental eccentricity, e = Ax * 0.05

## Slide 58
Story | DX | Ex3 |  |  |  |  |  | 
 |  | Displacement |  | Ratio | Check | Ax1 | Eccentricity | 
 |  | δmax | δavg |  |  |  |  | 
4 | 27.5 | 16.64 | 16.497 | 1.009 | OK | - | 0.05 | -
3 | 27.5 | 13.528 | 13.205 | 1.024 | OK | - | 0.05 | -
2 | 27.5 | 10.39 | 9.889 | 1.051 | OK | - | 0.05 | -
1 | 27.5 | 7.378 | 6.69 | 1.103 | OK | - | 0.05 | -
G | 27.5 | 4.314 | 3.713 | 1.162 | OK | - | 0.05 | -
  Torsional irregularity in X-direction:
    Irregularity does not exist

## Slide 59
Story | DY | Ey3 |  |  |  |  |  | 
 |  | Displacement |  | Ratio | Check | Ay1 | Eccentricity | 
 |  | δmax | δavg |  |  |  |  | 
4 | 27 | 30.885 | 30.008 | 1.029 | Not OK | 1.032 | 0.052 | 1.4
3 | 27 | 25.325 | 24.554 | 1.031 | Not OK | 1.035 | 0.052 | 1.4
2 | 27 | 19.657 | 19.026 | 1.033 | Not OK | 1.034 | 0.052 | 1.4
1 | 27 | 14.14 | 13.65 | 1.036 | Not OK | 1.025 | 0.051 | 1.4
G | 27 | 9.105 | 8.728 | 1.043 | Not OK | 1.007 | 0.050 | 1.4
  Torsional irregularity in Y-direction:
    Irregularity exist

## Slide 60
  Reentrant corner irregularity:
  diaphragm discontinuity irregularity:
  Does not exist
  Does not exist

## Slide 61
  Out of plane offset irregularity:
  Non parallel system irregularity:
  Does not exist
  Does not exist

## Slide 62
    Vertical Irregularity:

## Slide 63
Stiffness Irregularities:
  Does not exist
  Mass (weight) irregularity:
  Does not exist

## Slide 64
Vertical geometric irregularity
  Does not exist
In-Plane Discontinuity in Vertical Lateral Force Resisting Elements:
  Does not exist

## Slide 65
Discontinuity in Lateral Strength:
a- Weak Story Irregularity.
b- Extreme Weak Story Irregularity.
  Does not exist

## Slide 66
Response Spectrum Method :
Minimum Number of Modes:

## Slide 68
Response Spectrum Curve:
SDS =0.375
SD1 =0.188
T = the fundamental period of the structure.
To = 0.2 SD1/SDS = 0.1 sec
TS = SD1/SDS = 0.5 sec
TL = 4sec (Israeli code).
Sa = the design spectral response acceleration.

## Slide 69
Response Spectrum Definition:

## Slide 70
Checking for Dynamic Response Spectrum Analysis:
Scaling in X–direction:

## Slide 71
3608.9

## Slide 72
Scaling in Y–direction:

## Slide 73
3421.9

## Slide 74
  Check for Story Drift.

## Slide 75
Story | Load Case/Combo | Direction | Drift |  | Check
Roof | Envelop Service | X | 0.000191 | 0.000688 | OK
4 | Envelop Service | X | 0.00028 | 0.001008 | OK
3 | Envelop Service | X | 0.000279 | 0.001004 | OK
2 | Envelop Service | X | 0.000269 | 0.000968 | OK
1 | Envelop Service | X | 0.000267 | 0.000961 | OK
G | Envelop Service | X | 0.000265 | 0.000954 | OK
B1 | Envelop Service | X | 0.000128 | 0.000461 | OK
B2 | Envelop Service | X | 0.000054 | 0.000194 | OK

## Slide 76
  Check for P-Delta.
( P-Delta ) -RSx |  |  |  |  |  |  | 
Story | Height | P | VX | UX | ∆X | ƟX | Check
 | mm | kN | kN | mm | mm | 0.077 | 
Roof | 2500 | 420.0938 | 23.3763 | 5.83 | 0.84 | 0.0060 | Neglect P-Delta
4 | 3900 | 14152.3 | 727.9088 | 4.994 | 0.99 | 0.0049 | Neglect P-Delta
3 | 3900 | 27747.48 | 1100.584 | 4.003 | 0.97 | 0.0063 | Neglect P-Delta
2 | 3900 | 41389.94 | 1316.521 | 3.035 | 0.93 | 0.0075 | Neglect P-Delta
1 | 3900 | 55099.7 | 1540.417 | 2.106 | 0.84 | 0.0077 | Neglect P-Delta
G | 3900 | 68196.44 | 1779.966 | 1.27 | 0.73 | 0.0072 | Neglect P-Delta

## Slide 77
  Load Combinations:
Seismic Load Effect:
Use E = Eh + Ev
Where:
Eh = QE
QE = effects of horizontal seismic forces.
QEx = Ex + 0.3Ey
QEy = Ey + 0.3Ex
Ev = the load effect resulting from the vertical component of the earthquake ground motion and it is equal to an addition of (0.2SDS)D to the dead load effect.
Ev = 0.2SDSD = 0.2*0.375D = 0.075D

## Slide 80
  Diaphragm Rigidity:
There are two types of diaphragms are flexible and rigid

## Slide 81
Final Design of Structural Elements.

## Slide 82
  Slab Design:
Design for flexure:
For Moment in direction x:
For Moment in direction Y :

## Slide 83
For Top reinforcement in x-direction :
For Bottom reinforcement in X-direction
So for Mu ≤ 38.4 KN.m/m use minimum reinforcement of 1Ø10/200 mm for top reinforcement and 1Ø10/150 mm for bottom reinforcement.
This figures show the As is enough or not , when we need more As use 1Ø10/100 mm .

## Slide 84
For Top reinforcement in Y-direction :
For Bottom reinforcement in Y-direction
So for Mu ≤ 38.4 KN.m/m use minimum reinforcement of 1Ø10/200 mm for top reinforcement and 1Ø10/150 mm for bottom reinforcement.
This figures show the As is enough or not , when we need more As use 1Ø10/100 mm .

## Slide 85
  Beam Design:
Design for flexure:

## Slide 86
Beam Number | Span | Location | As(mm2) ETABS |  | As Used mm2 | Number of Bars
 |  |  | Moment | Torsion |  | 
Beam 1 | A-D | Negative-Left | 1349 | 644 | 2198 | 7 Ø20
 |  | Positive | 762 | 644 | 1570 | 5 Ø20
 |  | Negative-Right | 885 | 644 | 1570 | 5 Ø20
 | F-I | Negative-Left | 834 | 763 | 1884 | 6 Ø20
 |  | Positive | 819 | 763 | 1570 | 5 Ø20
 |  | Negative-Right | 1482 | 763 | 2512 | 8 Ø20
Beam 2 | A-D | Negative-Left | 983 | 570 | 1570 | 5 Ø20
 |  | Positive | 655 | 570 | 1256 | 4 Ø20
 |  | Negative-Right | 1306 | 570 | 1884 | 6 Ø20
 | D-F | Negative-Left | 2125 | 0 | 2198 | 7 Ø20
 |  | Positive | 1752 | 0 | 1884 | 6 Ø20
 |  | Negative-Right | 2296 | 0 | 2512 | 8 Ø20
 | F-I | Negative-Left | 1772 | 0 | 1884 | 6 Ø20
 |  | Positive | 1216 | 0 | 1256 | 4 Ø20
 |  | Negative-Right | 1480 | 0 | 1570 | 5 Ø20

## Slide 87
Example for Calculation :
For Negative moment M=229.4 KN.m
= = 0.00386
= ρbd = 0.00386*500*590=1139 mm2
= ρminbd = 0.00333*500*590=982.5mm2
%Error = (1141 – 1139 / 1139)*100% =0.1 %> 10% OK

## Slide 88
Design for Shear:
Beam Number | Span | Location | Av/s + 2At/s |  | Spacing | Number of stirrups
 |  |  | Av/s | 2At/s |  | 
Beam 1 | A-D | Left | 416 | 662 | 100 | 1Ø12/100mm
 |  | Medill | 416 | 662 | 100 | 1Ø12/100mm
 |  | Right | 416 | 662 | 100 | 1Ø12/100mm
 | F-I | Left | 416 | 784 | 90 | 1Ø12/90mm
 |  | Medill | 416 | 784 | 90 | 1Ø12/90mm
 |  | Right | 416 | 784 | 90 | 1Ø12/90mm
Beam 2 | A-D | Left | 416 | 586 | 110 | 1Ø12/110mm
 |  | Medill | 416 | 586 | 110 | 1Ø12/110mm
 |  | Right | 416 | 586 | 110 | 1Ø12/110mm
 | D-F | Left | 710 | 0 | 160 | 1Ø12/160mm
 |  | Medill | 416 | 0 | 200 | 1Ø12/200mm
 |  | Right | 743 | 0 | 150 | 1Ø12/150mm
 | F-I | Left | 624 | 0 | 180 | 1Ø12/180mm
 |  | Medill | 416 | 0 | 200 | 1Ø12/200mm
 |  | Right | 416 | 0 | 200 | 1Ø12/200mm

## Slide 90
  Column Design:
Column Section | As (mm2) | Number of Bars
400*550 | 2200 | 10Ø18
800*600 | 4800 | 16Ø20
550*250 | 1375 | 8Ø16

## Slide 91
For Column (400*550)
Check Distance Between bars if < 150 :
In X-Direction = =140 < 150 OK
In Y-Direction = =143 < 150 OK
Strips 24 = 10*24 = 240
8 = 8*18 = 144 take s= 140 mm
Least Dimensions /2 =200

## Slide 92
For Column (600*800)
Check Distance Between bars if < 150 :
In X-Direction = =160 > 150 NOT OK
In Y-Direction = =136 < 150 OK
𝑆0 = 𝑀𝑖𝑛 (𝑙𝑒𝑎𝑠𝑡 𝑐𝑜𝑙𝑢𝑚𝑛 𝑑𝑖𝑚, 8𝑑𝑏, 24𝑑𝑠, 300) = 𝑀𝑖𝑛 (600, 160, 240, 300)
Use 𝑆0 = 150 mm.
L

## Slide 94
  Shear Wall Design:
Shear Wall Name | Thickness(mm) | Longitudinal Reinforcement for Each face | Transverse Reinforcement for Each face
P1 | 250 | 1Ø 10 /250mm | 1Ø 10 /250mm
P 2 | 300 | 1Ø 10 /200mm | 1Ø 10 /200mm
P 3 | 250 | 1Ø 10 /250mm | 1Ø 10 /250mm
P 4 | 250 | 1Ø 10 /250mm | 1Ø 10 /250mm
P 5 | 300 | 1Ø 10 /200mm | 1Ø 10 /200mm
P 7 | 300 | 1Ø 10 /200mm | 1Ø 10 /200mm
P 9 | 200 | 1Ø 10 /300mm | 1Ø 10 /300mm
P 10 | 200 | 1Ø 10 /250mm | 1Ø 10 /300mm
P 11 | 200 | 1Ø 10 /300mm | 1Ø 10 /300mm
P 12 | 300 | 1Ø 10 /200mm | 1Ø 10 /200mm
P 13 | 200 | 1Ø 10 /250mm | 1Ø 10 /300mm

## Slide 95
= ρminbh = 0.0025*1000*250=625mm2/m
1Ø 10 /250mm
As from ETABS = 4000 mm2
Length = 6.4 m
As = 4000/6.4 =625 mm2 /m
%Error = (625 – 625 / 625)*100% = 0 %> 10% OK

## Slide 96
  Design of Foundations :
The Percentage of area of footing = 30 % on the area of building .
Area of footings < 50% Area of building, Use single footing , combined footing , mat footing and Wall footing .
Area of footing = = = 247.8 m2
Area of building = 813.95 m2.

## Slide 98
For Single footing :
use depth 40 cm , 60 cm , 70 cm , 80 cm according to Punching shear check .
For combined footing :
use depth 60 cm , 70 cm , 80 cm according to Punching shear check .
For mat footing :
use depth 60 cm , 90 cm according to Punching shear check .
For stiff is the area that moment of inertia is more large and it is use for column and wall location .
  Sections of footing :

## Slide 99
  Soil Property:

## Slide 100
  Checks Using ETABS :
Bearing capacity Check :

## Slide 101
2. Punching Shear capacity check :
As we can see all ratios <1, so it is OK.

## Slide 102
Number | Length (m) | Width (m) | Depth (m) | Bottom Reinforcement in X-Direction | Bottom Reinforcement in Y-Direction | Top Reinforcement in X-Direction | Top Reinforcement in Y-Direction
F1 | 1.5 | 1.5 | 0.4 | 1Ø 14 /200mm | 1Ø 14 /200mm | 1Ø 14 /200mm | 1Ø 14 /200mm
F2 | 1.5 | 1.5 | 0.4 | 1Ø 14 /200mm | 1Ø 14 /200mm | 1Ø 14 /200mm | 1Ø 14 /200mm
F3 | 1.5 | 1.5 | 0.4 | 1Ø 14 /200mm | 1Ø 14 /200mm | 1Ø 14 /200mm | 1Ø 14 /200mm
F4 | 1.5 | 1.5 | 0.4 | 1Ø 14 /200mm | 1Ø 14 /200mm | 1Ø 14 /200mm | 1Ø 14 /200mm
F5 | 1.5 | 1.5 | 0.4 | 1Ø 14 /200mm | 1Ø 14 /200mm | 1Ø 14 /200mm | 1Ø 14 /200mm
F6 | 11.7 | 7 | 0.6 | 1Ø 22 /150mm | 1Ø 22 /150mm | 1Ø 22 /150mm | 1Ø 22 /150mm
F7 | 5 | 2.2 | 0.6 | 1Ø 22 /200mm | 1Ø 22 /200mm | 1Ø 20/200mm | 1Ø 20/200mm
F8 | 11.5 | 7.2 | 0.6 | 1Ø 22 /150mm | 1Ø 22 /150mm | 1Ø 22 /150mm | 1Ø 22 /150mm
F9 | 2.5 | 2.5 | 0.6 | 1Ø 20 /200mm | 1Ø 20 /200mm | 1Ø 18/200mm | 1Ø 18/200mm
F10 | 6.7 | 3.4 | 0.8 | 1Ø 22 /200mm | 1Ø 22 /200mm | 1Ø 20/200mm | 1Ø 20/200mm
F11 | 7.4 | 3.4 | 0.8 | 1Ø 25 /150mm | 1Ø 25 /150mm | 1Ø 20/200mm | 1Ø20/200mm
F12 | 2.5 | 2.5 | 0.6 | 1Ø 22 /150mm | 1Ø 22 /150mm | 1Ø 18/200mm | 1Ø 18/200mm
F13 | 11.1 | 9.65 | 0.9 | 1Ø 22 /150mm | 1Ø 22 /150mm | 1Ø 22 /150mm | 1Ø 22 /150mm
F14 | 6.9 | 2.9 | 0.7 | 1Ø 25 /150mm | 1Ø 25 /150mm | 1Ø 20/200mm | 1Ø 20/200mm
F15 | 2.5 | 2.5 | 0.6 | 1Ø 20 /200mm | 1Ø 20 /200mm | 1Ø 18/200mm | 1Ø 18/200mm
F16 | 5.9 | 2.5 | 0.7 | 1Ø 25 /150mm | 1Ø 25 /150mm | 1Ø 20/200mm | 1Ø 20/200mm
F17 | 2.5 | 2.5 | 0.6 | 1Ø 20 /200mm | 1Ø 20 /200mm | 1Ø 18/200mm | 1Ø 18/200mm
F18 | 4 | 3 | 0.8 | 1Ø 22 /200mm | 1Ø 22 /200mm | 1Ø 18/200mm | 1Ø 18/200mm
F19 | 29.7 | 6.95 | 0.5 | 1Ø 20 /200mm | 1Ø 20 /200mm | 1Ø 16/200mm | 1Ø 16/200mm

## Slide 103
Design for flexure:
Mu = = 599 KN.m
= = 0.00297
In x-direction & Y-direction :
As = *B*d = 0.00297*1000*740 = 2200 mm2
Asmin =*B*h = 0.0018*1000*800 = 1440 mm2
Asmin < As use As=2200 mm2
For bottom reinforcement 1Ø 20 /200mm
For Top reinforcement put Asmin = 1Ø16 /200mm
Use 1Ø18 /200 mm and it is ok.

## Slide 104
  Design of Tie Beams :
This section of tie beam (Depth =600 and Width =300 mm) is commonly used
Ag = 300*600

## Slide 105
  Design of Stairs :
Dimensions of stair:
The following dimensions of stair as in architectural drawings.
Landing width = 3.1m
Landing length = 1.2m
Span length of flight = 4.5 m
Rise=0.17 m
Going = 0.3m

## Slide 106
Loads on the stair:
For flight:
h = = = 0.16 try h = 0.2 m
Dead load = 0.2 *25 = 5 KN\m2
For SD load = Tiles weight + Mortar weight + Sand weight
= KN\m2
Live load =5 KN\m2
Wu = 1.2D+1.6L = 1.2(5+2.1) +1.6(5) = 16.52 KN\m2

## Slide 107
For Landing :
Take h = thickness of slab = 0.25 m
Dead load = 0.25 *25 = 6.25 KN\m2
For SD load = 5 KN\m2
Live load =5 KN\m2
Wu = 1.2D+1.6L
= 1.2(6.25+5) +1.6(5) = 21.5 KN\m2