## Slide 1: An-Najah National University Engineering Collage Civil Engineering Department
Graduation project:
Prestressed Design Of Blue Sparkler Hotel
Supervised by: Dr. Wael Abu Assab
By : Ahmad Abu Farha Ahmad Marei

## Slide 3: Titles to be covered
Introduction
Building Loads
Preliminary Design
Prestressed Design & Three Dimensional Analysis
Columns & Footings Design
Special Design

## Slide 4: Introduction

## Slide 5: Project Description
Blue Sparkler Hotel is Proposed to be in Palestine , Nablus city.
Consists of 10 stories and roof
average height of 3.8 meters except the ground and basement floor which has 4.5, 3 meters height respectively.
The overall area (5703)meter square.
The basement floor includes parking with 31 car parks.

## Slide 6: Project Description
The ground floor includes 9 car park, 2 water tank, offices , ladies saloon.
The mezzanine floor include a restaurant.
The remaining floors include residential apartments.
Type of soil is assumed to be as soft rock with a bearing
capacity of 350 KN/m2.
ACI -2008 (American Concrete Institute Code 2008 will be used.

## Slide 7: Design Determinants
Structural Materials:
- Concrete:
f’c = 21- 40 Mpa (slab-on-grade, footings)
= 24-35 Mpa (beams, framed slabs)
= 21- 45 Mpa (columns and shear walls)
-Reinforcing Steel:
Es = 200,000 Mpa
fy = 420 MPa.
Grade 60

## Slide 8: Design Determinants
Nonstructural Materials:
The following table shows the densities for materials used in construction:
Material | unit weight(KN/m3 )
Reinforced concrete | 25
Plain concrete | 23
Filler | 18
Blocks | 12
Polystyrene | 0.3
Masonry stone | 27
Light weight block | 6

## Slide 9: Building Loads

## Slide 10: Loads
The structural elements are subjected to different stresses and deformations due to the following loads:
Vertical loads : consist of dead and live loads.
Lateral loads: consist of wind and earthquake loads .
- Note : earthquake load will not be designed.

## Slide 11: Dead load
Consist of weight of all permanent constructions such as:
- Slab own weight.
:- Super imposed dead load = 5.4kN/m2 (as shown below)

## Slide 12: Live load
we specify the live load from table 4-1 in ASCE/SEI 7-05 code :

## Slide 13: Wind load
The wind pressure is mainly affect all structures and has small effect in low structures.
This building is consisting of 10 floors + roof with average height of 3.8m and average area of floor of 575m2 (for residential floors) and it is expected that the wind loads will not be critical, Jordanian code will be used to check that.
The design wind speed in this region can be taken as 120 km/hr as reasonable value for the country weather.

## Slide 14
- بعد اجراء عمليات حسابية لأحمال الرياح تبعا للكود الاردني ,
- تم تقسيم واجهات المبنى وذلك حسب الجدول التالي:
*هنا تم استخدام الطريقة (أ)
والطريقة (ب) حيث تم تقسيم
المبنى الى ثلاث واجهات.

## Slide 15
اكبر قيمة للحمل على الواجهة 2 : P = p*A
=237.15* (30.65*30.65)
=222.78 KN
For meter square =
LOAD/ (NUMBER OF STORIES * STORY AREA)= 222.78/(8*581.43)=
0.05 KN/m2 in Y direction ,
and 0.03 KN/m2 in X direction.
- These values will be used in 3dimensional analysis.

## Slide 16: Load Combination
The Code gives load factors for specific combinations of loads.
U = 1.4D (9-1)
U = 1.2D + 1.6L + 0.5(Lr or S or R) (9-2)
U = 1.2D + 1.6(Lr or S or R) + (1.0L or 0.5W) (9-3)
U = 1.2D + 1.0W + 1.0L + 0.5(Lr or S or R) (9-4)
U = 1.2D + 1.0E + 1.0L + 0.2S
U = 0.9D + 1.2W (9-6)
U = 0.9D + 1.0E (9-7)

## Slide 17: Preliminary Design

## Slide 18: Design of reinforced concrete floor manually
The floor system as one way solid slab with drop beam
The ACI-code coefficient used in analysis
The design for second floor.
one way solid slab specification is ok as
(L/B ≥2.0)
Loads transfer in x-direction ,beams in y- direction

## Slide 19: One way solid slab

## Slide 20: Loads
Minimum slab thickness =(0.3) meter.
Own weight of slab =(7.5) KN/m2
S.I.D = (5.4) KN/m2
Wu1 = 1.4 D.L = 18 KN/m2
Wu2=1.2 D.L + 1.6 L.L = 23 KN/m2
So, use Wu = 23 KN/m2

## Slide 21: Check slab for shear

## Slide 22
Vu= 92.8 KN
ØVc = 159 KN
Vu < ØVc ====>ok

## Slide 23: Design slab for flexure

## Slide 26: Design for flexure
For max. Mu+ int. = Wu Ln 2/ 16 = 85.2KN.m
(Use1Ø16 / 200mm)
For max. Mu- int. = Wu Ln 2/ 10 = 124KN.m
( Use1Ø16 / 150mm )
For max. Mu- ext. = Wu Ln 2/ 24 = 122.5KN.m
( Use1Ø16 / 150mm )

## Slide 27
Transverse reinforcement

## Slide 55: Prestressed Design

## Slide 56: Prestressed background
A prestressed concrete member can be defined as one in which there have been introduced internal stresses of such magnitude and distribution that the stresses
resulting from the given external loading are counter forted to a desired value .
Concrete is strong in compression but weak in tension. Due to such a low tensile capacity, flexural cracks developed at early ages of loading .
in order to prevent or reduce such cracks from developing , a concentric or eccentric force is imposed in the longitudinal direction of the structural element.
This force prevents the cracks from developing by eliminating or considerably reducing the tensile stresses at the critical mid span or support sections at service load , thereby raising the binding, shear, and torsion capacities of the sections .
The sections are then able to behave elastically, and almost the full capacity of the concrete in compression can be efficiently utilized across the entire depth of the concrete sections when all loads act on the structure, such an imposed longitudinal force is called prestressing force.

## Slide 57: Prestressed concrete properties
Most prestressed concrete elements are designed for a compressive strength above 35 MPa, the reason for this the high strength concrete normally has a higher modulus of elasticity. This means a reduction in initial elastic strain under application of prestress force and reduction in creep strain results in a reduction in loss of prestress.
In post-tensioned construction, high bearing stresses results at the ends of beams where the prestressing force is transferred from the tendons to anchorage fittings which bear directly against the concrete.
In pre-tensioned concrete construction, where transfer by bond is customary, the use of high strength concrete will permit the development of higher bond stresses.

## Slide 58: Prestressing Reinforcement
Because of the high creep and shrinkage losses in concrete, effective prestressing can be achieved by using very high – strength steels, such high – stressed steels are able to counterbalance these losses in the surrounding concrete and have adequate leftover stress levels to sustain the required prestressing force.
Prestressing reinforcement can be in the form of single wires, strands composed of several wires twisted to form a single element, and high – strength bars. Three types of wires are commonly used are:
- Uncoated stress-relieved wires.
- Uncoated stress- relieved strands and low-relaxation strands.
- Uncoated high-strength steel bars.

## Slide 59: Prestressing system
The design will deal with indeterminate post-tensioning two way flat slab with edge beams system. In post-tensioning, the strands, wires, or bars are tensioned after hardening of the concrete. The strands are placed in the longitudinal ducts within the precast concrete element. The prestressing force is transferred through end anchorages and the tendons of strands should not be bonded or grouted prior to full prestressing .
In order to provide permanent protection for the post-tensioned steel and to develop a bond between the prestressing steel and the surrounding concrete, the prestressing ducts have to be filled under pressure with the appropriate cement grout in an injection process.

## Slide 60: Slab Design Of Two Way Flat Plate(Manual)
Second floor plan

## Slide 61
Material properties :
f'c = 30 MPa f'c i = 21 MPa
f pu = 1862 MPa fy = 414 MPa
f pe = 1096 MPa f py = 1675 MPa
Eps=200 000 MPa
Use strands diameter ɸ 12.7 mm

## Slide 62
Loads :
Live Load (LL) = 4.79 KN/m2
Super Imposed Load (SID) = 5.4 KN/m2
Slab thickness = L/40 = 9.44 /40 = 0.236 ……..use = 25 cm slab
Total dead load = 0.25m * 25 KN/m3 = 6.25 KN/m2
Ultimate load (Wu) = 1.2(6.25+5.4) + 1.6(4.79) =21.644 KN/m2
Service load = 6.25 + 5.4 + 4.79 =16 .44 KN/m2
Frame width = 7.154 m

## Slide 63
Load balancing:
- Assume an average intensity of compressive stress on the concrete due to load balancing of fc =1.2 MPa
Unit force = (1.2*1000*250)/ 1000 = 300 KN
Pe (effective prestressing force after losses) per strand = 99*1096 /1000
= 108.5 KN
Fe ( force in unit width of section) on concrete = unit force* frame width
= 300 * 7.154 =2146.2 KN
Number of strands = 2146.2/108.5 = 19.7……..Use 18 strands
Area of prestressing steel = 18 * 99 mm2 = 1782 mm2
Pe = 18 * 108.5 = 1953 KN
fc = 1953*1000/(7154*250) = 1.092 MPa

## Slide 64
Exterior span:
a = (169+187)/2 – 67= 111 mm
W balance = 8 Fe a / L2 = 8(2146.2)(.111/ 7.154) / (7.89)2 = 4.28 KN/m2
W unbalance = W ser. – W bal. = 16.44 – 4.28 = 12.16 KN/m2
Interior span:
a = (225 + 188) / 2 - 99 = 108 mm
W balance = 8(2146.2)(.108 / 7.154) / (7.99)2 = 4.06 KN/m2
W unbalance = 16.44 – 4.06 = 12.38 KN/m2

## Slide 65
Here Wunbalanced is not the same for the two spans. These values can be used or adjustment to eccentricities can be made to have equal Wunbalanced for all spans .

## Slide 68
At support :
Ftop= = 1.9 < 5.48……ok
Fbot= = -1.9 < 13.5 ……ok
At mid span:
Ftop== -2.7< 13.5 ……..ok
Fbot== 2.6 < 5.48…..…ok
- Stresses at service loads ( compare with fc and ft )
Fc =.45*= (0.45* 30)= 13.5 MPa
Ft=

## Slide 69
- Stresses at transfere(compare with fci and fti)
Fci =0.6*=18 MPa
Fti =
=
Pi = Aps * fpi = 1548 KN

## Slide 70
- Stresses at transfere(compare with fci and fti)
At support:
Ftop= = -1.3 < 18 …....ok
Fbottom= = -2.44 < 18 …..ok
At mid span:
Ftop= = 1.13 < 2.7…..ok
Fbot= = -1.3 < 18…...ok

## Slide 71
Minimum top nonprestressed (bonded)steel is equal to:
As = .00075 h L
- Where L is length of half spans at the support along the frame
L= 7.99/2 + 7.45/2 =7.72 m
As= .00075*7720*250 = 1447.5 mm2
Use… 8 ɸ16 at supports
As min= .004*250*1000=1000 mm2/m
Use….1 ɸ12/110 mm.

## Slide 72: Design Of Two Way Post tensioned Flat Slab With Edge Beams (By Using SAP Program)
here the design will deal with the second floor slab as shown in the plan below:

## Slide 73: Design of Slab
Given:-
, E = 4700 =814.0638 Mpa.
.
.
Floor height = 3 m.
Superimposed dead load = 5.4 KN/.
Live load for residential public rooms = 5 KN/.
External wall load = 5 KN/m.
Wind load in X direction = 0.03 KN/m.
Wind load in Y direction = 0.05 KN/m.
12 Column

## Slide 74: Design of Slab
.{
.{=
.{assumed [loss=254 MPa from AASHTO the avg. loss around 300Mpa]}
Slab Thickness : hmin = max. span length/40 = 0.236 m (take it 25 cm)

## Slide 75: Design of Slab
Calculate the Max. Moments :
- Here we take two frames in X
and Y directions and take
the max. and min. envelope moments from SAP ,
to use it in drawing the tendon layout.

## Slide 76
Frame 1 in X-direction :

## Slide 77
Frame 2 in Y-direction :

## Slide 78
Drawings of Tendon Layout :
For Frame 1in X direction
- from the Max. moment = 170.84 take the cover = 25 mm so the table below show the eccentricities of the tendon in X frame:

## Slide 79
For Frame 2 in Y direction
from the Max. moment = 291.24 take the cover = 25 mm so the table below show the eccentricities of the tendon in Y frame:

## Slide 80
For Frame 1 in X direction :
Assume an average intensity of compressive stress on the concrete due to load balancing of fc =1.2 MPa
Unit force = (1.2*1000*250)/ 1000 = 300 KN
Pe (effective prestressing force after losses) per strand = 99*1096 /1000 = 108.5 KN
Total Fe ( force in unit width of section) on concrete = unit force* frame avg. width
= 300 * 7.154 = 2146.2 KN
Number of strands = 2146.2/108.5 = 19.7 >>>>>> Use 18 strands
Area of prestressing steel = 18 * 99 mm2 = 1782 mm2
Pe = 18 * 108.5 = 1953 KN
fc = 1953*1000/(7154*250) = 1.092 MPa

## Slide 81
Tendon Section Data for the frame X :
18 strands will be distributed as (1/3) for the middle strip and (2\3) for the column strip.
So, here C.S= 12 strands * area of strand
= 12*99= 1188 mm2
And M.S = 6 strands * area of strand
= 6*99= 594 mm2/2= 297 mm2

## Slide 82
Drawing the tendon on SAP:
- Selecting the Parabolic Tendon 1
(as the moment diagram )

## Slide 83
Define the eccentricities of tendon
that was calculated manually :

## Slide 84
After defining the load pattern
(hyperstatic) on SAP, define the load
of tendon as a stress :

## Slide 85
For Frame 2 in Y direction :
fc =1.2 MPa
Unit force = (1.2*1000*250)/ 1000 = 300 KN
Pe (effective prestressing force after losses) per strand = 99*1096 /1000 = 108.5 KN
1.2 = (Ape *1096)/(250*7495) >>> Ape = 2051.55 mm2
Number of strands = 2051.55/108.5 = 18.9 >>>>>> Use 17 strands
Area of prestressing steel = 18 * 99 mm2 = 1782 mm2
Tendon Section Data for the frame X :
- 17 strands will be distributed as (1/3) for the middle strip and (2\3) for the column strip.
So, here C.S= 11 strands * area of strand = 11*99= 1089 mm2
And M.S= 6 strands * area of strand = 6*99= 594 mm2/2= 297 mm2

## Slide 86
- Divided the plan into 3 frames in X direction and 5 frames in Y direction and distribute the tendons in the column and middle strips in the frames as shown in figure below :

## Slide 88
Quick check on the deformation shape of the slab after distribution of tendons (the slab should deformed upward due to tendons)

## Slide 89
* Check Stresses :
--we must check stress at transfer stage and at final stage for service and ultimate loads
The allowable stresses are shown below:
At transfer stage:
Fci=0.6*= 0.6*21= 12.6 MPa.
Fti=
At final stage:
Fc =.45*= 0.45 * 30= 13.5 MPa.
Ft=

## Slide 90
By using direct design method to calculate interior stresses:
-At transfer stage:
Ftop =
Fbottom =
-At final stage :
Ftop =
Fbottom =
* Check Stresses :

## Slide 91
- The tables below show the calculations of interior stresses :

## Slide 94
- Compare the results from table (4.4.9) with the allowable stresses (OK) for example Ftop= 0.688 < Fci= 12.6 MPa…………..ok
And it's OK for all stresses.

## Slide 95
Bonded reinforcement:
- Because the member resists flexure; minimum bonded reinforcement must be put in the tensile zone (at the tendon zone) as a factor of safety and to bond the concrete with steel cause the tendon is non-bonded material (post tension).
As for bonding =0.004*Act

## Slide 96
The table below show the calculations of the frames bonded reinforcement:

## Slide 97
Check Deflection for slab :
The max deflection obtained in the Second floor and the results were as follow:
Deflection from dead, live, super imposed and hyperstatic loads are taken from SAP , as shown in figures

## Slide 102
The long term deflection is given by the following equation:
Δ long term = Δ L+ λ∞ ΔD + λTΔSL
λ∞ = 2
λT = 2 (( From equation 9-11 in ACI-318- sec 9.5.2.5))
Since the slab is attached to nonstructural elements not likely to be damaged by large deflections then:
The allowable deflection = L /240 = 7470/240 = 31.125 mm.
So the slab deflection = 30.13 mm. < allowable long term def. = 31.125 mm >>>OK.
It's so critical value because it was taken in the max. deflection zone, and the other values was ok too.

## Slide 103
Design of slab for shear and bending
- Chick slab for wide beam shear :
Ø= * = 171.16 KN
the max shear in the max. span = 117.8 KN/m.
Ø>171 > 117.8 >>>OK
So the slab is Ok for wide beam shear.

## Slide 104
- Design Slab for Flexure :
Note that we use prestressed (post-tensioned) design , so here no need to calculate the moments.
* shrinkage steel will be used as follow :
As shrinkage = 0.0018 *1000* 250 = 450mm2
As shrinkage = 450mm2/m. ( use 4Ø 12 / 1000mm )

## Slide 105
Slab Reinforcement
- By taking 2 sections: section 1 in the mid of span and section 2 at the support to see the steel and tendon distribution in the slab section (Frame X3) :

## Slide 106
The figure below show a cross section 1,2 in slab with steel and tendon . - (Note that the 18 strand will be distributed in column and middle strip as before).

## Slide 107
Check Punching Shear :
column number (6) in 2 floor was taken to check punching shear as following :
Column dimension 1000 mm*400 mm (interior column)
The ultimate axial load and moments in X and Y directions was taken from SAP :

## Slide 108
ʈu=
ʈu=
ʈu =0.89+0.082+ 0.036
ʈu = 1.008 < 1.22 MPa. >>>>>> OK
vc = min {1.68 MPa or 1.22 MPa or 1.81MPa}

## Slide 109
Design of Edge Beams :
Note that edge beams used as reinforced concrete member not prestressed .
The beam (B7) in 2nd floor was taken to show the design criteria (this beam has the longer span 9.44m).

## Slide 110
The beam (B7) section dimensions are :
- Total depth (h) = 1200mm.
- The effective depth (d) = 1140mm.
- Beam width (bw) = 600 mm.
- f’c = 30 Mpa.
- fy = 420 Mpa.

## Slide 111
Design Beam for Shear
Vu= 483.58 KN
So,
Vu = 483.58 KN < Vc = >>>>>>> OK
Use =0.31

## Slide 112
Design Beam for Flexure
The figure below shows the moment diagram of beam B7 from SAP :

## Slide 113
all of computed steel ratios are less than so we will use the min. area of steel which is :
Asmin = 0.0033*bw*d = 0.0035*600*1140= 2394mm2 (use 8ø20)

## Slide 114
Design Beam for Torsion
X1=600-2*44.5 = 511mm
Y1= 1200-2*44.5 =1111mm
Ph = 2X+2Y= 2(511+111) =3244mm
Aoh =X*Y= 511*1111=567721mm2
Ao= 0.85*Aoh =482563mm2

## Slide 115
The value of tu = 378.5 KN.m-
1.655 < 3.423 ……….
so the section is adequate

## Slide 116
Travers reinforcement for torsion:
Calculate torsion:
Travers reinforcement 112 /250mm.
use S = 250 mm

## Slide 117
Longitudinal reinforcement for torsion:
Al = * Ph *
Al = 1.25 * 3244 * = 4055 mm2
- For negative moment = 731.2 KN.m:
- top reinforcement use:
As top final = As top + 4055(0.6/1.9)
- bottom reinforcement use:
As bottom final = As bottom + 4055(0.6/1.9)
- For each side :
As each side = 4055(1.14/1.9)

## Slide 118
Three Dimensional Structural Analysis

## Slide 119
Structural Modeling
Figure(4.33):Structural Modal of the Building

## Slide 120
Material Used
1- Concrete :
The compressive strength of concrete
f'c = 30 MPa

## Slide 121
2- Steel :
The steel that used is (A615Gr60)
with maximum yield stress, Fy= 420MPa.

## Slide 122
3- Tendon :
The tendon that used is (A416Gr270)
with maximum tensile stress of 1862 MPa.

## Slide 123
: Loads Used
- (LL) : 5 KN/m2
- (SID) : 5.4 KN/m2
-(WL) : 0.03 KN/m2 at X-direction
and 0.05 KN/m2 at Y-direction -(DL) : calculated by SAP
SID on edge beams from
the external cladding wall = 5 KN/m

## Slide 124
Verification of structural analysis
- Compatibility
The whole building movements
(Joint displacements) are compatible as shown in figure below:

## Slide 125
- Equilibrium
Show the calculation of the structure weight and the variance between the all loads by manually and SAP.

## Slide 126
LL = 5 KN/m2
SID = 5.4 KN/m2
Total LL in all floors = (Area G. floor *LL)*2 + (Area 2nd floor *LL)*8
LLtotal = (773.38*5)*2 + (538.18*5)*8 = 29261 KN/m2
Total SID in all floors = (Area G. floor *SID)*2 + (Area 2nd floor *SID)*8
SIDtotal = (773.38*5.4)*2 + (538.18*5.4)*8
= 31601.8 KN/m2

## Slide 127
Structure Weight)dead load)
- Columns :

## Slide 128
- Beams (1200*600 mm) :
Weight of beams in 2nd floor = beams length * beams dimensions * unit wt. of concrete
= 98.56 * (1.2*0.6) * 25 = 1774 KN
Weight of beams in G. floor = beams length * beams dimensions * unit wt. of concrete
= 153.99 * (1.2*0.6) * 25 = 2771.75 KN
Weight of beams in Structure = 2(Wt. of beams in G.floor) + 8(Wt. of beams in 2nd floor)
= 2(2771.75) + 8(1774) = 19735.5 KN

## Slide 129
- Shear Walls :
Weight of Stairs Wall in Structure = 2(15.42)*10*25 = 7710 KN
Weight of Elevators Wall in Structure = 17.64 *10*25 = 4410 KN
So, The Total Weight of Shear Walls in the Structure = 7710+4410 =12120 KN

## Slide 130
Slabs :
Weight of G. floor slab = 816.63 * 0.25 * 25 = 5104 KN
Weight of 2nd floor slab = 581.43 * 0.25 * 25 = 3634 KN
So, The Total Weight of Slabs in the Structure = 2(5104) + 8(3634) = 39280 KN
From the previous 4 steps , - The Total Weight of the Structure (DL) = 3517.5 + 19735.5 + 12120 + 39280
= 74653 KN

## Slide 131
The figure below show the illustrates the results of DL, LL, SDL from SAP calculations :

## Slide 133: Design of Columns & Footing

## Slide 134: design of columns Manual design
COLUMN DESIGN REQUIRMENT

## Slide 135: Check slenderness ratio for column 11:

## Slide 136: Design of column 11 using interaction diagram

## Slide 139
Footing Design

## Slide 140: Footing design
Single footing:
Is one of the most economical types of footing and is used when columns are spaced at relatively long distances .(12m)
Bearing capacity of the soil=350 KN/m2.

## Slide 141: Design Footing for column 11:

## Slide 143: Design of group F1:
Check for punching shear:
Vn required =9038ton
Vn provided=9072>9038 …………………..OK
Check for wide beam shear:
Vn required =2823 KN
Vn provided=3087>2823 …………………..OK

## Slide 144
Flexural design:
Mu= 892 KN.m
ρ=0.00064 > ρ min = 0.0018( min for shrinkage)
As=8910 mm2 Use 6ϕ20mm/m' in both directions.
Shrinkage steel:
From practical point of view use half of the shrinkage steel on top since footing thickness large( approximately when thickness >60cm).
A shrinkage =0.0018Ag /2
A shrinkage =8100cm2/m.  use 6ϕ20/m in both direction.

## Slide 146: footings details

## Slide 151: Design of Staircase :

## Slide 153: Design of Rectangular Water Tanks :

## Slide 154: Thank you