## Slide 1: INTEGRATED HOSTEL DESIGN
An-Najah National university
Faculty Of Engineering
Building Engineering Department
Supervisor :
Moayad Salhab
Prepared by :
Lama Ahmad
Maha Hilan
Marah Awajneh

## Slide 2: OUTLINES
Introduction
Site description
Architectural design
Environmental design
Structural design
mechanical design
Electrical design
Quantity surveying

## Slide 3: Introduction

## Slide 4: Site description
Location : Nablus city, in
Beit -Wazan town,
near An- Najah University
Area:
5583.24m2
3.2 km form city center
Surrounding
2 main streets
Residential building

## Slide 5: Architectural Design

## Slide 6: Site Accessibility

## Slide 7: Project Description
4 floors, in addition to abasement as a parking .
serves 123 students
Total area of the building equals to 6155.05 m
First floor
1570.2m2
second floor area
1269.8 m2
Third floor area
783.3 m2
Forth floor floor
590.38 m2
Ground floor area
1927.7 m2
Basement
604 m2

## Slide 8: Bedrooms Forms
 | . single bedrooms | double bedrooms | Special need bedrooms
No. | 39 | 42 | 3
Area(m2) | 16-18 | 24-28 | 31-35

## Slide 9: Ground Floor
Ground floor plan

## Slide 10: First Floor Second , And Third Floor
Plans

## Slide 11: Fourth Floor
Forth floor Plan
Space | Area
Store | 7.66
Toilet | 29.10
Gymnasium | 176.4
Entertainment hall | 133.4
Common room | 34.5

## Slide 12: Elevations
East Elevation
West Elevation

## Slide 13: Elevations
South Elevation
North Elevation

## Slide 14: SECTIONS
A-A section
B-B section

## Slide 15: Environmental design
Material properties
Thermal behavior
Acoustical design
Daylighting factor
Shading design

## Slide 16
Material properties
Diathonite
light weight
Elasticity
Mechanical strength
Breathability
Fire resistance
Acoustic insulation
Energy saving
Humidity control
U – value
0.468 w/m2.k
External wall
Internal wall
U – value
1.47w/m2.k

## Slide 17
Second and third floor
U – value
0.528w/m2.k
U – value
0.619w/m2.k
Ground floor

## Slide 18
Roof
U – value
0.491w/m2.k
U – value
0.364w/m2.k
First and forth floor

## Slide 19
Thermal comfort Analysis
Temperature
Air Temp. =22 c˚
Radiant Temp. =19 c˚
Operative Temp. =20.48 c˚
PMV

## Slide 20: Thermal Analysis
Total heating load (KW) | Total cooling load (KW)
226.59 | 388.7
System Load
Total site energy(KWh/m2)
234.59

## Slide 21: Daylighting
Function | min. Recommended Daylighting Factor
Entrance | 0.6%
Kitchens | 2%
Offices | (1.5-2.5)%
Bedrooms | 1%
Common Room | 2%
Living Entrance | 1.5%

## Slide 22: Shading
Horizontal Louvers :
Vertical Louvers :

## Slide 23: Acoustical analysis
STC (Sound Transmission Class )
External wall
Partition

## Slide 24: Acoustical analysis
Floors

## Slide 25: Acoustical analysis
Reverberation time
Material
Partition (acoustical Diathonite plaster
External glazing (6mm)
External wall (cement plaster on block )
Ceiling (gypsum board 1.2cm thick )
Floor (ceramic tile )
Chairs (Fabric )
Gymnasium (1.2-1.6 s)
Frequency | SABINE RT60 (sec)
125Hz | 1.23
250Hz | 1.64
500Hz | 1.38
1KHz | 1.23
2KHz | 1.14
4KHz | 1.03

## Slide 26: Acoustical analysis
Reverberation time
Material
Partition (acoustical Diathonite plaster
External glazing (6mm)
External wall (cement plaster on block )
Ceiling (gypsum board 1.2cm thick )
Floor (ceramic tile )
Door (aluminum )
Chairs (Fabric )
Multipurpose (1.4-1.8 s)
Frequency | SABINE RT60 (sec)
125Hz | 1.68
250Hz | 1.87
500Hz | 1.57
1KHz | 1.51
2KHz | 1.46
4KHz | 1.25

## Slide 27: Structural analysis
Codes
- ACI 318-14
- UBC -97
Material
- Compressive strength ( fʹc ) = 28MPa
- Yielding strength of steel (fy) = 420 Mpa.
Bearing capacity = 250 kN /m2
Designed load
SID = 4 KN/m2
Live load = 2.5 KN/m2

## Slide 28: Structural analysis
seismic zone is 2B with (Z = 0.20).
( I ) = 1
Soil profiles :SD
(Ca) = 0.28
(Cv) = 0.4
(R) for Building frame with shear walls = 5.5

## Slide 29: Structural analysis

## Slide 30: Structural analysis
Checks
Compatibility check
Equilibrium check
Internal Forces check
Deflection check
Period check
Drift check
ok
ok
ok
ok
ok
ok

## Slide 31: STRUCTURAL ANALASIS
Slab structural system
- Thickness =35cm
- Hidden beams
U- boot System

## Slide 32: STRUCTURAL ANALASIS
Shear design
Vu >øVc

## Slide 33: STRUCTURAL ANALASIS
5ø10mm/m
Moment design
5ø14mm/m

## Slide 34: STRUCTURAL ANALASIS
Moment design
Solid slab
U-boot slab

## Slide 35: STRUCTURAL ANALASIS
Beams system
Hidden beams
Beam | Dimension(cm) | Reinforcment (mm)
B1 | 80*35 | 14Ø14
B2 | 35*35 | 8Ø14
B3 | 130*35 | 20Ø14
B4 | 110*35 | 18Ø14

## Slide 36: STRUCTURAL ANALASIS
Columns system
column tag | Dimension (cm) | Reinforcement | Stirrups distribution
C1 | 65*65 | 14ø20 | 3ø10@30cm
C2 | 65*65 | 12ø25 | 3ø10@30cm

## Slide 37: STRUCTURAL ANALASIS
Shear wall design

## Slide 38: STRUCTURAL ANALASIS
Footings type :
Single footing
Wall footing
Matt footing

## Slide 39: STRUCTURAL ANALASIS
Single system

## Slide 40: STRUCTURAL ANALASIS
Footing system
wall footing

## Slide 41: STRUCTURAL ANALASIS
Footing system
Matt footing

## Slide 42
Matt footing
STRUCTURAL ANALASIS

## Slide 43: STRUCTURAL ANALASIS
ok
Block 2
- Checks
- Shear design
-Moment design

## Slide 44: STRUCTURAL ANALASIS
Beam tag | Dimension (cm) | Reinforcement
B1 | 50*35 | 8ø14
B2 | 35*35 | 6ø14
Beams
Columns
column tag | Dimension (cm) | AS (mm2) | Bars Distribution | Stirrups distribution
C3 | D = 40 | 1257 | 8ø14 | 3ø10@30cm
C4 | D= 60 | 3850 | 8ø25 | 3ø10@30cm
C5 | 65*65 | 4225 | 12ø25 | 3ø10@30cm

## Slide 45: STRUCTURAL ANALASIS
Shear Wall

## Slide 46: STRUCTURAL ANALASIS
Footing system
- single footing
Wall footing
Combined footing

## Slide 47: STRUCTURAL ANALASIS
Single footing

## Slide 48: STRUCTURAL ANALASIS
wall footing

## Slide 49: STRUCTURAL ANALASIS
Combined footing

## Slide 50: Mechanical design
Water system
Drainage system
Fire Fighting
HVAC system
Elevators

## Slide 51: Water System
Vertical | Horizontal | Branch
3 '' | 2'' , 1.5'' | 0.75''
Diameter Of Pipes
underground water tank capacity = 80 m3.

## Slide 52: Drainage system

## Slide 53: Drainage system
Storm water

## Slide 54: HVAC System
Outdoor unit
Slot Linear diffuser
Split unit

## Slide 55: Heating Ventilation and Air conditioning HVAC Design:
Total cooling load for the ground floor equals 150.5 kW
Zone | Design Capacity (kW) | Design Flow Rate (m3/s)
Multipurpose | 10.67 | 0.6977
Cafeteria | 14.29 | 1.01
Zone | Design Capacity (kW) | Design Flow Rate (m3/s) | unit
Corridor | 1.57 | 0.1011 | 1
Room11 | 2.21 | 0.1619 | 1
Room10 | 2.61 | 0.1914 | 1
Room4 | 2.96 | 0.2104 | 1
Room5 | 2.38 | 0.1689 | 1
Common Area | 12.62 | 0.7898 | 4
Zone30 | 2.84 | 0.1688 | 1
Room3 | 1.32 | 0.0885 | 1
Room6 | 3.51 | 0.2414 | 1
Room9 | 2.7 | 0.1898 | 1
Room7 | 2.62 | 0.1795 | 1
Room2 | 2.24 | 0.1569 | 1
Room1 | 1.16 | 0.0793 | 1
Room8 | 3.16 | 0.2135 | 1
Hall | 7.2 | 0.4638 | 2
Supervisor Bed Room | 3.07 | 0.2251 | 1
Clinic | 2.54 | 0.1888 | 1
Office3 | 4 | 0.291 | 1
Manager | 3.72 | 0.2685 | 1
room | 1.21 | 0.0829 | 1
Office1 | 2.68 | 0.1818 | 1
Office2 | 2.69 | 0.1949 | 1

## Slide 56: Heating Ventilation and Air conditioning HVAC Design:

## Slide 57: Mechanical Ventilation

## Slide 58: Fire Fighting System
Sprinkler
Smoke Detector
Fire Extinguisher (water)
Fire Extinguisher (CO2)
Heat Detector

## Slide 59: Emergency Exit
Width of corridors = 1.7-2 m
Longest bath = 17m

## Slide 60: Elevators
Capacity | 630kg | 1000kg
speed | 1.00m/s | 

## Slide 61: Electrical design
Socket distribution
Artificial lighting
Load speaker

## Slide 62: Electrical design
Sockets design
 | No . Sockets
Sleeping area | 3 , 1 for hvac system
Kitchenate | 2 , 1 for refrigrator

## Slide 63: Electrical design Artificial lighting
Reception
Luminaires
Underscore Ep77
201 lm
MQ95_J005 Cup
850lm
CHAL 200
1990 lm

## Slide 64: Electrical design Artificial lighting
Bedrooms
Luminaires
QN50 Boss
4500 lm
LYRIC DECO LED
1500 lm
LOGICO TVOLO
2310 lm

## Slide 65: Lighting and switches distribution

## Slide 66: Loud Speaker
PRO-16RC
Frequency Range | 63hz - 23khz +/- 3db
Coverage Angle | 100
Finish | Black Baffle/Frame, White Paintable Grille
Mounting Depth | 6.15” (15.6cm)
Product Weight | 7 Ibs (3.18kg)

## Slide 67: Quantity surveying
 | Cost (NIS)
Structural work | 4,625,440
Finishing | 3,719,891
Mechanical work | 481,555
Electrical work | 349,572
Total Project Cost | 9,441,253
Total Unit Cost (NIS /m2) = 1534

## Slide 68
Thank you for listening
Ramadan Kareem
And You Are “Akram”