## Slide 1
An- Najah National University Faculty of Engineering & Information Technology. Building Engineering Department. Graduation project (2) .
Redesign of Municipal Development and Lending Fund Building in Ramallah. Prepared By:
Amro Jawabreh
Masa Sunallah
Rasha Ismail
Supervisor: Eng. Moayad Salhab

## Slide 2: 2 3 5 6 1 4
TABLE OF CONTENTS
Environmental Aspects
Quantity Surveying and Cost Estimation
Introduction
Structural Aspects
Eloctro-Mechanical Aspects
Architectural Aspects

## Slide 3: 1 Introduction
This project is a building of the Municipal Development and Lending Fund located in the city of Ramallah. It is a Palestinian institution with financial and administrative independence. It was established in 2005 by the Palestinian government to be the main and preferred channel to support the development and reform process for local authorities.

## Slide 4: Objectives
This project aims to modify the Development Trust Fund in order to achieve an attractive architectural design and achieve comfort for employees and customers, and we will conduct a complete environmental analysis of the building, as we seek in our design to make the building more efficient.

## Slide 5: Methodology
Site analysis
Environmental Aspect
Structural Aspect
Eloctro-Mechanical Aspects
Quantity Surveying and Cost Estimation
Architectural Aspects

## Slide 6: Site Analysis
Site Location
Facilities & surrounding
The plot of land for the project is located in the city of Ramallah, west of the main Al-Ersal Street, at the intersection of two secondary streets (Samira Azzam and Ein Semaan Street).
There is also one adjacent apartment building next to it.

## Slide 7: Climate

## Slide 8: Sun path and wind direction

## Slide 9: Topography and contour
In order to the sloped land, the stairs and ramp was designed. The level difference between the highest and lowest point is around 7 meters, reference level (0.00 m) while the subsequent at level )+7.00 m).

## Slide 10: 2 Architectural Aspects
Plans Before and after modification.
Elevation.
3D from Lumion

## Slide 11
Second Basement Before and After modification
Before modification
After modification
2

## Slide 12
First Basement Before and After modification
After modification
Before modification

## Slide 13
Ground Floor Before and After modification
Before modification
After modification

## Slide 14
First Floor Before and After modification
Before modification
After modification

## Slide 15
Second Floor Before and After modification
Before modification
After modification

## Slide 16
(Third – Fifth ) Floor Before and After modification
Before modification
After modification

## Slide 17
ELEVATIONS

## Slide 20: 3 Enviromental Aspects
Daylight Factor
Heating and cooling Load
Shading Analysis

## Slide 21: Daylight Factor
As shown in the picture above, the values of daylight are acceptable

## Slide 22: Heating and cooling Load
the total design heating capacity = 140.94 kw
the total design cooling capacity for the building equal 166 KW.
Heating Load
Cooling Load

## Slide 23: Thermal modification on exterior wall:

## Slide 24: Thermal modification on internal floor

## Slide 25: Thermal modification on Roof

## Slide 26: Thermal modification on glazing

## Slide 27: Design Builder Simulation Result
Simulations provide valuable information on annual energy consumption. Data also helps
to identify the number of hours and other uncomfortable results. According to Pierce PMV
Set, a building will achieve comfort when the PMV ranges from -0.7 to 0.7, as shown in the figure.

## Slide 28: Design Builder Simulation Result
Energy Baseline Comparison
As the figure above shows, the Percentage of saving equal 60.53%, so the design is
good.
"The table above show the total site energy consumed per meter square which is equal 86.85 and the standard requirements from energy portfolio manager standard for mixed use property is 207, so it is acceptable

## Slide 29: Shading Analysis
8:00 AM
12:00 PM
in Summer 21-june
3:00 PM

## Slide 30: Shading Analysis
8:00 AM
12:00 PM
in Winter 21-December
3:00 PM

## Slide 31: environmental treatments
From an environmental aspect, our project originally had louvers in the south (front) elevation .

## Slide 32: 3 Structural Aspects
Structural System
Structural Checks
Seismic Design
Seismic Checks
Design & Details

## Slide 33
Slab thickness

## Slide 34: Structural System
Centre of Column

## Slide 35: Structural Checks
Compatibility Check
All structural elements of the building move with each other, and this indicates that the compatibility Check is acceptable

## Slide 36: Structural Checks
Equilibrium Check
Load | etabs | manual | % Error
Dead | 53161.3939 | 52914.9 | 0.00%
Live | 21125.5396 | 21106.008 | 0.00%
SID | 23933.9657 | 24191.4 | 1.1%
In the Equilibrium Check, the value resulting from the error rate is 1.1% of the dead load, and this value is less than 5% --> The Equilibrium Check is acceptable

## Slide 37: Structural Checks
Stress-Strain Check – Columns
Stress-Strain Check – Slab
Check is acceptable

## Slide 38: Structural Checks
Deflection check from live load for slab:
Limit = short long for span /240= 6800/240=28.3mmCheck is ok.
Immediate deflection
Deflection limitation= 𝐿/ 360 = 12 /360 = 33mm.
Max Deflection from etabs for slab = 4.4mm.Check is ok.
Long term deflection.

## Slide 39: Seismic Design
Seismic Design
Seismic zone: the seismic zone is 2A and the Z is →0.15.
The soil profile is SC , bearing capacity = 400 kg/cm3.
Force Reduction Factor→ R =5.5 (Building Frame System-Shear wall)
Importance factor I=1.25.
Acceleration seismic load coefficient Ca=0.18.
seismic coefficient Cv=0.25.

## Slide 40: Seismic Design
Check Name | ETABs results | Allowable limit/Manual limit | Check status
Period check | 1.2 | 1.1 | ok
Modal participating ratio | 94 – X 97 – Y | >90 | ok
Base shear | 4658.17 | 4658.19 | ok
Drift check | ΔMX=51 | < 80 | ok

## Slide 41
U-Boot plan
Design & Details
Slab Design
Section in slab

## Slide 42: Design & Detailing
Slab Design

## Slide 43: Design & Detailing
slab detailing
Section in slab

## Slide 44: Design & Detailing
Column design & detailing
Column | length | width | AS (mm2 ) | No.of bars
edge column | 800 | 800 | 6400 | 24 Ø20
corner column | 600 | 700 | 4500 | 16 Ø20

## Slide 45: Design & Detailing
Column design & detailing

## Slide 46: Design & Detailing
Shear wall design & detailing

## Slide 47: Design & Detailing
Beam design & detailing

## Slide 48: Design & Detailing
Stairs design & detailing

## Slide 49: Design & Detailing
Ramp design & detailing

## Slide 50: Design & Detailing
Mat Foundation design & detailing

## Slide 51: Design & Detailing
Isolated footing Design

## Slide 52: Design & Detailing
Water Tank Design & detailing

## Slide 53: Design & Detailing
    Basement wall Design & detailing

## Slide 54: Design & Detailing
Tie Beam design & detailing

## Slide 55: 04 Electro-Mechanical Aspects
HVAC System
Water Supply and Drainage
Artificial Lighting
Acoustical Design
Power Design system
Fire Fighting System

## Slide 56: HVAC System
VRF System has been considered.
HVAC System Used Components:
Fan Coil Unit.
Ducts.
Diffusers.
Cassette unit.

## Slide 57: HVAC System
Chart: 
Design cooling Capacity = 166 KW
Total heating Capacity = 140.94KW
Total Design Flowrate = 18.1097
Air Handling Unit Catalogue

## Slide 58: HVAC System
Outdoor unit
The selected outdoor units are from
AIRSTAGE company type J-IVL with 22.4 KW.
Indoor unit
Fan coil unit from Daikin company.

## Slide 59: HVAC System
Diffuser unit
Diffuser unit from Air Master Emirates Company
60×60 cm diffuser will be used for all spaces.

## Slide 60: HAVC System
Chart: 
Duct sizer tool will be used to calculate the diameter of all ducts.
To calculate the size of the main duct and Branches as shown (A-B), the airflow (407.9 L/s) and the velocity (5 m/s) are needed and duct sizer software will calculate the head loss and the equivalent diameter as shown in the figure.
Then all branches diameter was calculated
based on the constant head loss theory
and duct sizer software will calculate

## Slide 61: HAVC System
Indoor unit
also Since The cooling load for all offices is between 1-5 KW, the FXZQ-A Fully flat cassette (Ductless) from Daikin company. (Each office space contains 1 to 2 cassette units only)

## Slide 62: Cassette unit ,Diffuser and duct distribution

## Slide 63: Water Supply and Drainage
The hot water source was relied on the electric boiler. Installation for each floor 2 electric boilers 50 L For Each from CATA company

## Slide 64: Water Supply and Drainage
Drainage System Sample Plans

## Slide 65: Water Supply and Drainage
Rainwater in Drainage System

## Slide 66: Artificial Lighting
Chart: 
1- meeting room
2- manager room
3-traning room
4- Reception
5- cafeteria
6- office
DIALux has been used for Space Analysis and Design.

## Slide 67: Artificial Lighting
For training design: Type of luminaire has been used:

## Slide 68: Artificial Lighting
Chart: 

## Slide 69: Artificial Lighting
Lighting Plans

## Slide 70: Acoustical Design
Standard of RT60(Reverberation time ).
Standard of STC (Sound transmission class).

## Slide 71: Acoustical Design
Ecotect had been used for RT60 analysis
Space | RT60 (sec)
Office | (0.6-0.8)
Manager room | (0.6-0.8)
Meeting room | (0.7-0.9)
Training room | (0.7-0.9)
Multi-purpose hall | (1.2 -1.9)

## Slide 72: Acoustical Design
STC For external Wall
STC For internal Wall
Insul had been used to designed layer of wall and floor

## Slide 73: Acoustical Design
    STC ( Sound transmission class) For external and internal Wall
IIC (Impact Isolation class) for floor
Insul has been used to designed layer of wall and slab
STC & IIC | Value from standard | Value from INSUL
STC for external wall | 50 | 78
STC for glass wall | 40 | 45
STC for internal wall | 50 | 51
IIC for floor | 40 | 110
STC & IIC | Value from standard | Value from INSUL
STC for external wall |  | 78
STC for glass wall |  | 45
STC for internal wall |  | 51
IIC for floor |  | 110

## Slide 74: Power Design
Socket Distribution Plans

## Slide 75: Power Design
Distribution Boards

## Slide 76: Power Design
Low voltage Design
Designed the low voltage circuits such as internet or TV line.

## Slide 77: Fire Fighting System
Used Fire-fighting System
Sprinkler System
Fire Hose Stations
Fire alarm System
Dry Stand Pipe
Fire-fighting Signs
fire extinguishers

## Slide 78: Fire Fighting System
Six Floor Fire-Fighting Plan
Fire-fighting Symbols

## Slide 79: 5 Quantity Surveying & Cost Estimations
In this section, we detailed the activities and quantities needed to set up our project, and we calculated all the necessary quantities and created a Bill of quantity table. The cost includes materials cost, labor costs, and equipment costs.

## Slide 80: Cost Estimation
The total cost of the project ≈ 9 M NIS.
The unit cost of the project ≈ 2300 NIS/m2
.
Working items | Total Cost (NIS)
Structural Work | 3470000
Finishes | 3850000
Electrical Work | 250000
Mechanical and HVAC | 1010000
Firefighting | 65000
Lumpsum | 80000

## Slide 81: Thank you for listening