## Slide 1: Structural Analysis and Design of a Residential Building
Graduation Project Report II
Prepared By:-
Faris Atwan
Tarek Deeb
Mohammad Akhras
Yasmine Habash
Under Supervision of:
Dr. Riyad abdel-karim
Fall 2018

## Slide 2: Outline:
Introduction.
Seismic Analysis Approach.
Preliminary Design.
3D Structural Analysis.
Structural design.

## Slide 3: Project location :

## Slide 4: Project Description:
This Building consists of 7 floors:
Two basement floors.
Ground floor.
Four top floors.
Total Area of building = 4732 m2
+
m2

## Slide 5: Materials:
Structural Materials:
Concrete.( 24 MPa ) ( 28 MPa ) Reinforcement steel.(420 MPa)
Non-Structural Materials:
Material | γ in KN/m3
Aggregate | 18
Tile | 26
Normal weight block | 12
Light weight block | 6
Plaster | 23

## Slide 6: Codes in Our Project:
The Codes used in this project are the following :
ACI 318-14 (American Concrete Institute): building code requirements of structural concrete and commentary.
ASCE7-2010 (American Society of Civil Engineers).
IBC 2012.

## Slide 7: Loads:
Gravity Loads:
Dead Load
Live Load
Lateral Loads:
Earthquake Load.
wind load

## Slide 8: Gravity Loads:
Dead(D)
Own weight (OW)
= 3.7 KN/m2
Superimposed (SID)
= 5.5 KN/m2
Live(L)
Live Load(L)
= 5 KN/m2

## Slide 9: Earthquake Loads:
According to IBC we use response spectrum curve to identify the earthquake loads.

## Slide 10: Load combinations:
1) 1.4D
2) 1.2D+1.6L
3) 1.3D+1L+1.3EQx+0.39EQy
4) 1.3D+1L+1.3EQy+0.39EQx
5) 0.8D+1.3EQx+0.39EQy
6) 0.8D+1.3EQy+0.39EQx
7) 1.07D+0.7EQx+0.21EQy
8) 1.07D+0.7EQy+0.21EQx
9) 1.053D+0.75L+0.525EQx+0.158EQy
10) 1.053D+0.75L+0.525EQy+0158EQx
11) 0.53D+0.7EQx+0.21EQy
12) 0.53D+0.7EQy+0.21EQx
13) D
14) D+L

## Slide 11: Structural System:
-The structural system that we use in our project is frame system (slab-beam-column) system.
-The slab system used in the building is one way ribbed slab for floors

## Slide 12: Software Program:

## Slide 13: 3D Modeling:

## Slide 14: Preliminary Design:
Slab:
The selected system was one – way ribbed slab as shown below:

## Slide 15: Preliminary Design:
Beams:
we will use hidden beams in Y-Direction:

## Slide 16: Preliminary Design:
Columns:
Column distribution.
For basement 2
For basement 1 and Floors

## Slide 17: Preliminary Design:
Columns: Column Cross-section.

## Slide 18: Seismic Analysis Approach:
Ground motion input parameters
Exceedance probability 2%
In 50 years
SS=0.5
S1=0.25
The risk category is “Ⅱ“
The importance factor equal 1

## Slide 19: Seismic Analysis Approach:

## Slide 20: Seismic Analysis Approach:
Damping factor must be less than 10%

## Slide 21: Seismic Analysis Approach:
Seismic Parameters

## Slide 22: Seismic Analysis Approach:
Response Spectrum :

## Slide 23: Seismic Analysis Approach:
Period limit check:
From Etabs:
From Calculation:

## Slide 24: Seismic Analysis Approach:
Diaphragm Rigidity
The length to width ratio of the diaphragms in each block is less than 3 as shown in the table :

## Slide 25: Seismic Analysis Approach:
Drift Check :

## Slide 26: Seismic Analysis Approach:
Second order effect:

## Slide 27: Seismic Analysis Approach:
Irregularity Checks
We have 13 checks in ASCE-10 for irregularity
Horizontal irregularity checks
Vertical irregularity checks

## Slide 28: ETABS 2016 Model and Checks.
ETABS Checks
Equilibrium Check
Stress-Strain Check
Compatibility Check

## Slide 29: ETABS 2016 Model and Checks.
Compatibility Check:
The model moves as one unit so we can say that our modeling is OK.

## Slide 30: ETABS 2016 Model and Checks.
Equilibrium Check:
Manual Live Load:
Etabs Live Load:
The difference less than 5%

## Slide 31: ETABS 2016 Model and Checks.
Stress-Strain Check:
From ETABS
Right -ve M = 13.37 KN.m
Left -ve M = 7.24 KN.m
M ETABS= +
= + 3.234 = 13.54 KN.m
M manually = = = 14.2 KN.m
Error % = | | *100% = 4.6% < 5%

## Slide 32: Design:
We design all the structural elements in our project:
Slabs.
Beams.
Columns.
Shear walls.
Footings.

## Slide 33: Slab Design:
The structural system of slab is one way ribbed slab of 350 mm thickness with hidden beams.
.Slab Thickness = 350mm
.Web width = 150 mm
.Flange Thickness= 70 mm

## Slide 34: Slab Moments:
ØMn +ve = Ø As fy (d- )
= 63.6/.55=115 KN.m / m
Positive Moment:

## Slide 35: Slab Moments:
ØMn –ve = Ø As fy (d- )
= 17.8/.55=32.4 KN.m / m
Negative Moment:

## Slide 36: Slab Moments:
M-ve E-Tabs < ØMn-ve for Green and Yellow areas
ρ min = 0.0033
As min = 153.45 mm2/rib  bottom steel 2Ф10/rib
Mmax-ve E-Tabs = 32.4 KN.m > ØMn-ve for Red areas
ρ = 0.0048
As = 226 mm2/rib  2ϕ12/rib
Mmax+ve E-Tabs < ØMn+ve for All Slabs
ρ = 0.0033
As = 562.65 mm2/550mm 3ϕ16/rib
Use Shrinkage steel ϕ8/300mm

## Slide 37: Slab Shear :
Concrete Resistance of shear :
Vu = 57 KN
If Vu < Ø Vc , No need for shear reinforcement.
Although the slabs does not need shear stirrups. Stirrups must be used to hold the bottom bars.
Stirrups 1ϕ10 / 300mm

## Slide 38: Slab Section:

## Slide 39: Slab Section:

## Slide 40: Beam Design:
All beams in our Building are hidden.
Depth (mm) | Width (mm) | Type | Beam
350 | 700 | Hidden beam | B 70*35
350 | 400 | Hidden beam | B 40*35

## Slide 41: Beam Design (B110 )
Hidden Beam “B110” in the 1st story was chosen to check reinforcements. Beams width and depth are 70cm and 35cm respectively.

## Slide 42: Beam “B110” Internal Forces:
Mu +ve manually = 126 kN.m
Mu -ve manually = 185 kN.m
Vu = 230KN

## Slide 43: Beam “B110” reinforcement:
+ve As = 1218 mm2 > As min = 670 mm2  Top Bars 6ϕ16
-ve As = 1847mm2 > As min = 670 mm2  Bottom Bars 10ϕ16
Tth = 8.8 KN.m > Tu  No need for tensional reinforcement
ØVc = 133 KN < Vu  closed stirrups Ф10/100mm

## Slide 44: Beams Section:

## Slide 45: Columns Design:
Two columns in the project differs in dimensions and lengths:
Type | Length
Typical stories | 3.3m
ground floor story | 8 columns are 5.6m and the rest is 3.3m.
1st basement story | 3.3m
2nd basement story | 3.3m
**the Dimensions of Columns is 700*350 Expect the columns with length 5.6m is 850*400

## Slide 46: Columns Design:
Column “C7” which has the max. compression load was chosen to check reinforcement in the ground floor.

## Slide 47: Ground floor Column “C7” Internal forces:
Pu =1876 KN

## Slide 48: Columns 85cm*40cm Design:
Slenderness ratio:
= 20.5< 22
Slenderness can be neglected.
Ag = 340,000 mm2
ρ min = 0.01
As min = 3400 mm2
ØPn = 4313 KN > Pu

## Slide 49: Walls Design:
Two types of walls in this project
Building Non Bearing walls
Basement Shear walls

## Slide 50: Non Bearing Walls Design:
Thickness = 300mm

## Slide 51: Non Bearing Walls Design:
Sample design and detailing of shear wall:
Almost of piers have min.steel ratio 0.0025 expect two piers have steel ratio 0.0045.

## Slide 52: Non Bearing Walls Design:
ρmin bottomvertically = 0.0025
As min vertically = 0.0025 *300*1000 =750 mm2/m
ρ uppervertically = 0.0045
As min vertically = 0.0045 *300*1000 =1350 mm2/m
Use Ø14/250mm at each face of the wall as vertical steel for
shear walls
ρmin horizontally = 0.0025
As Shrinkage horizontally = 0.0025 *300*1000 = 750 mm2/m
Use Ø12/250mm at each face of the wall as horizontal steel

## Slide 53: Non Bearing Walls Reinforcement

## Slide 54: Basement Wall Design:
Wall thickness = 300mm
γ soil = 20 KN / m3
Ka = 0.27
f’c = 24 MPa
fy = 420 Mpa
q soil = γ Ka * 3.3m = 17.8 KN / m2
q Live = Ka * Live load = 0.54 KN / m2

## Slide 55: Basement Wall Design:
Max +ve Moment = 12.86 KN.m
Max -ve Moment = 5.68 KN.m
ØVc = 53 KN > Vu=23 KN.

## Slide 56: Foundation Design:
The foundation system we used is a mat Foundation system.
We used Safe software program to design the foundations.

## Slide 57: Foundation Details:
The allowable bearing capacity for soil in the location of the
building is 240 KN/m2.
Thickness of each foundation was chosen based on wide beam shear and punching shear.
Our foundation thickness is 1000 mm.

## Slide 58: Foundation Checks:
Wide beam shear check.
Deflection check.
Stresses check.

## Slide 59: Wide Beam Shear Check:
Ø Vc = Ø/6 λ √𝑓′𝑐 b d = 140 KN
As shown in the figure the range is between (-140 to140); the areas with the dark blue exceedes 140 KN
These areas are within the distance of 270mm (effective depth) from the supports.
So there is no need for wide shear reinforcement steel in the foundation.

## Slide 60: Deflection Check:
The maximum allowable deflection for foundation equals 3.5mm
The maximum deflection in this foundation equals 3.15mm < 3.5mm.. OK

## Slide 61: Stresses Check:
Maximum soil pressure equals 75 KN/m2 which is smaller than the allowable bearing capacity of the soil = 240 KN/m2

## Slide 62: Flexure Design using SAFE:
Steel distribution in Y direction.
Steel distribution in X-direction.

## Slide 63: Flexure In Y-Direction:

## Slide 64: Flexure In X-Direction:

## Slide 65: References:
ACI Committee 318 “Building Code Requirements for Structural Concrete (ACI 318M-14)” American concrete institute, Michigan, 2011.
ASCE Committee (2010), “American Society of Civil Engineers, Minimum Design Loads for Buildings and Other Structures” American Society of Civil Engineers, Virginia 20191, 2010.
IBC 2012