## Slide 1: Seismic Design of Abu Gazaleh Building
Done by:
Rania Sabbah
Haneen Hamada
Supervisor:
Dr. Mahmoud Dwaikat

## Slide 2: Outline:
Introduction
Seismic design
Drift check
Design of structural elements :
Footing
Beam
Tie beam
Column
Shear wall
Slab
Stair case

## Slide 3: Introduction
a residential building of five stories
3.32m height each.
The building has an area approximately as 313m2 per floor with minor variation.
It is located in Ma'ajeen area of Nablus city.

## Slide 4: Architectural Plan

## Slide 5: Assumptions made:
Concrete Compressive strength, fc’=28MPa
Steel yielding Strength, fy= 420 MPa.
Live load uniformly distributed on slab= 3KN/m2
Superimposed dead load uniformly distributed on slab= 5.3 KN/m2
Hidden beams with ribbed slab system

## Slide 6: Assumptions used

## Slide 7: Seismic design
Equivalent static (UBC97)
Z=0.2 since building is in Nablus (from seismic map of UBC).
Soil type =D ,Cv= 0.4 ,Ca=0.28.
Weight=DD+SD=27629.3 KN.
R=4.5 ,I=1 .
T =0.42sec.
V=Cv*I*W/R*T = 5847.47 KN
Vmax=2.5*Ca*I*W/R=4297.8 KN
Vmin=0.11Ca*I*W=850.98KN
V>Vmax

## Slide 8: Seismic design
From model and response spectrum analysis the base shear in y = 2669.54KN, x=2502.6KN.
V equivalent >V response
To be in safe condition scale factors are introduced.
Scale factor response=g*I/R*any scaling up

## Slide 9: Drift Check
Max displacement in structure must be checked in this case it occurs in the roof.
Displacement of roof was checked due to earthquake ( Δ ) in x and y directions.
Δplastic= 0.7*R*Δelastic
Δplastic= 0.7*4.5*0.0088=0.027m
Δmax=H/400=0.45m
Check is O.K.

## Slide 10: Design of structural element
Codes used:
ACI318
UBC 97
Assumed Intermediate frame design.

## Slide 11: Load combinations
Ultimate Load combinations according to UBC97:
1.4D
1.2D + 1.6L + 0.5 (Lr or S)
1.2D + 1.6 (Lr or S) + (f1L or 0.8W)
1.2D + 1.3W
+ f1L + 0.5 (Lr or S)
1.2D + 1.0E + (f1L + f2S)
0.9D ±(1.0E or 1.3W)

## Slide 12: Design of Footing
Footing are used:
to transfer safely high concentrated column or wall loads to base ground.
Spreading it on larger area.
Bearing capacity of soil (qall) =300KN/m2
Minimum Area =service load/qall
Thickness from wide beam and punching shear.
Design area of steel from Moment in x and y.
Shrinkage steel(top)=0.0018*width*height /2

## Slide 13: Design of Footing
Footings layout:

## Slide 14: Design of Footing

## Slide 15: Design of Beams
Beams transfer loads from slab to columns.
Hidden beams while dropped beams along perimeter.
Use proper section dimension.
Longitudinal area of steel from moment and torsion.
Transverse area of steel from shear and torsion.

## Slide 16: Beams Layout:

## Slide 17: Beams Detailing

## Slide 18: Tie beams Design
Is used to prevent differential settlement.
Longitudinal area of steel from moment and torsion and tension.
Transverse area of steel from shear and torsion.

## Slide 19: Ground beams Layout

## Slide 20: Ground Beam Design

## Slide 21: Ground beams detailing

## Slide 22: Slab Design
Slabs carries distributed loads to beams and columns.
Thickness suitability by shear check.
Moments in x and y from model to design area of steel.
Ribbed slab : As min=0.0033*bw*d
All area of steel <As min …..minimum is used
Shrinkage steel(top)=0.0018*b*h ..both directions

## Slide 23: Slab layout

## Slide 24: Slab detail

## Slide 25: Shear wall design
Shear walls is distributed to carry lateral load and resist torsion effect.
The moment about axis 1 and axial force ...long area of steel (column)
Moment about axis 2 …long area.
Shear in 1 to check thickness of wall.
Shear in 2 …transverse steel.(beams)

## Slide 26: Design of Shear wall
Check shear in x :
Vux=23.95 KN
φVc=281.11KN.>Vu O.K.
Design shear in y:
Vuy=224.16KN.
Vc=359.82KN
Vc>Vu/φ then use minimum shear reinforcement
Design moment about y:
Muy=43.9KN.m
As=Muy/(φ*fy*(d-d’))
Design for axial force and moment about x:
As column (interaction diagram)

## Slide 27: Shear wall distribution

## Slide 28: Shear wall detailing

## Slide 29: Shear wall detail

## Slide 30: Columns design
Columns transfer loads from beams to footing.
Column section dimensions estimated using relative axial load, then check using model, such that , ρ=1% (give warning)
Area of steel =ρ*Area gross, area of minimum used.
Check manually one column, determine :
1)braced or un-braced
2) long or short column
interaction diagram.
Stirrups , spacing from code requirement.

## Slide 31: Column detail

## Slide 32: Stair case design
Stairs are used to carry people and things from one elevation to another.
A model was used to determine
Internal stress.
treat the run as a slab, check
Shear.
Moment both directions…area of
Steel.

## Slide 33: Stairs Detailing