## Slide 1
An-Najah National University
Faculty Of Engineering
Mechanical Engineering Department
Design and Analysis of Biogas Register
By : Khaled Zaid Ahmed Khader
Taqi-Adyn Atili Aanas Malik
Supervised By : Dr. Basheer Nouri

## Slide 2
RENEWABLE ENERGY

## Slide 3
Definition
Solar Energy
Wind Energy
History
Water Energy
Sources
Biomass
Geothermal
Renewable Energy

## Slide 4
Biomass
Benefits
Composition
Production
Definition

## Slide 5: History
Europe

## Slide 6: History
China

## Slide 7: History
India

## Slide 8
BIOLOGICAL PROCESS

## Slide 9
Complex organic matter
Carbohydrates, proteins, fats
Soluble organic molecules
Sugars, amino acids, fatty acids
Volatile fatty
acids
H2CO2
CH4 + CO2
Acetic acid
1
2
3
4
4
Hydrolysis
Acidogenesis (Fermentation)
Acetogenesis
Methanogenesis

## Slide 10: Factors effecting on the process
pH Value
Temperature
Retention time
Loading rate
Toxicity
C/N ratio
Slurry

## Slide 11
SAMPLE TEST

## Slide 12
Plastic water bottle
Bunsen Burner
T-Connection
Car tire
Gas valve

## Slide 13: Analyze

## Slide 14: Results and conclusions
Days | Mass of gas (g)\Day | Days | Mass of gas (g)\Day
1 | 0 | 26 | 25
2 | 0 | 27 | 27
3 | 0 | 28 | 27
4 | 0 | 29 | 34
5 | 1 | 30 | 35
6 | 1 | 31 | 36
7 | 2 | 32 | 34
8 | 2 | 33 | 39
9 | 2 | 34 | 35
10 | 3 | 35 | 38
11 | 4 | 36 | 38
12 | 5 | 37 | 39
13 | 8 | 38 | 35
14 | 8 | 39 | 37
15 | 9 | 40 | 39
16 | 8 | 41 | 32
17 | 9 | 42 | 36
18 | 11 | 43 | 28
19 | 10 | 44 | 15
20 | 13 | 45 | 9
21 | 15 | 46 | 8
22 | 16 | 47 | 4
23 | 17 | 48 | 0
24 | 16 | 49 | 0
25 | 20 | 50 | 0

## Slide 15: Results and conclusions
Chart: Biogas production\Day
| 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 11 | 12 | 13 | 14 | 15 | 16 | 17 | 18 | 19 | 20 | 21 | 22 | 23 | 24 | 25 | 26 | 27 | 28 | 29 | 30 | 31 | 32 | 33 | 34 | 35 | 36 | 37 | 38 | 39 | 40 | 41 | 42 | 43 | 44 | 45 | 46 | 47 | 48 | 49 | 50
Biogas production \ Day | 0 | 0 | 0 | 0 | 1 | 1 | 2 | 2 | 2 | 3 | 4 | 5 | 8 | 8 | 9 | 8 | 9 | 11 | 10 | 13 | 15 | 16 | 17 | 16 | 20 | 25 | 27 | 27 | 34 | 35 | 36 | 34 | 39 | 35 | 38 | 38 | 39 | 35 | 37 | 39 | 32 | 36 | 28 | 15 | 9 | 8 | 4 | 0 | 0 | 0

## Slide 16: Results and conclusions
Theoretically, 1 kg of solid poultry manure will produce 100 liter of biogas
Experimentally, the weight of biogas produced is 0.830 kg for 9 kg of manure
That leads to an error of 20.49%

## Slide 17
MECHANISM OF THE OPERATION

## Slide 18: Mechanism of the operation
Waste collection
Dry matter tank
Screw pump
The digester
Gas holder
Filtration unit
Gas tank
Cogeneration
unit

## Slide 19
Easy visual control for daily feeding input
Or using inclined surface
Waste collection

## Slide 20
Can be constructed from concrete or galvanized steel plate
Dry matter tank

## Slide 21
Diameter >= 12”
Length = 50’
Used for handling liquids containing solid in suspension with horizontal transport
Speed 30-60 rpm
Capacity 15 L/s -11 m3 /s
Screw pump

## Slide 22
Floating drum planet
The digester

## Slide 23
Fixed dome planet
The digester

## Slide 24
Floating drum gasholder
Fixed dome gasholder
Plastic gasholder
Separate gasholder
Gas holder

## Slide 25
Chemical absorption
High pressure water scrubbing
Pressure swing absorption
Cryogenic separation
Membrane separation
Filtration unit

## Slide 26
Using propane gas cylinders
Gas tank

## Slide 27
Two type of cogeneration:
Topping cycle
Bottoming cycle
Cogeneration
unit

## Slide 28
CASE STUDY
CHICKEN FARM

## Slide 30: Demand Production method
Energy demand for lamps
Heating and cooling loads
Cogeneration unit
Biogas demand
D
P > D
P
Biogas production
Gasholder volume
Plant parameters
Digester volume – size of plant
Type and quantity of available biomass
Digester temperature

## Slide 31: Chicken farm specifications
Length = 110 m
Width = 12 m
Height = 3.5 m
Front door
Back door

## Slide 32: Chicken farm specifications
20,000 chicken head
Consist of ten rows
Each row contain 1000 chicken head

## Slide 33: Demand calculations
Lighting
  53 lamps are used.
  Each lamp uses 400 watts to cover 25 m2 of floor area.
  Operated for 18 hours
Heating
  Qtot = 255 Kwatt
  Operates with an electrical motor having 80 hp.
  Consumes 60 Kwatts electricity
Total biogas demand equals 280 m3 daily.

## Slide 34: Production calculations
Each chicken gives 150 – 200 gm of dung daily.
Dung production equals to 3200 Kg daily
Each 1 Kg of dry matter produces 100 liter of biogas.
Gas yield production equals 320 m3 .

## Slide 35: Design of digester
Motors for collectors operate every three hours and has a power of 1 Kwatt.
Dry mass tank construct from galvanized steel plate, has a dimension of 1.5 X 1.5 X 2 .
Screw pump feeding once a day , has a velocity of 1 m/s, flow rate 50 L/s.
Digester size is calculated depending on the equation :
Vd (m3) = Sd (m3/day) * RT (days)
Substrate input (Sd) = biomass (B) + water (W) (m3/d)
Digester size equals to 320 m3 , for factor of safety it assumed to be 430 m3 .
Gasholder size is calculated depending on the equation :
Vg1 = Gc max* Tc max
Gasholder size equals to 240 m3 .

## Slide 36
PAYBACK

## Slide 37: Estimated system components cost
Item | Cost
Collecting waste | 250 $
Dry mater tank | 100$
Screw pump | 650 $
Digester | 4000 $
Gas holder | 200 $
Filtration unit | 1000 $
Gas tank | 300 $
Cogeneration unit | 3000 $
Piping | 300 $
Total | 9800 $

## Slide 38: Estimating Payback point
One labor is needed to run the system, works for 30 hours per month and get 300 $ per month.
Maintenance is assumed to be 10% of the system cost and equals to 980 $ per year.
Electricity cost due to heating and lighting ( 1 Kwatt = 0.143 $ ) equals to 2220 $ per month.
Total cost per month equals to 2600 $.
Payback point = system cost / monthly cost
Payback point = 9800 / 2600
Payback point = 3.7 months

## Slide 39
RECOMMENDATIONS

## Slide 40: recommendations
Palestine is a rich country of plants and animals, which can give a large amount of manures, which in result can be the fuel of biogas digesters that can provide the Palestinian farms the needed energy for its various operations.
Authorities must concentrate more on the renewable energy sources, especially the biogas and biomass sources, in which Palestine is rich with. This alternative energy sources can help us to become independent in consuming gas from other sides, it helped the farm to become alive, so it definitely will help Palestinians too.

## Slide 41
THANK YOU !!