## Slide 1: Design of A Sewer Network For Dair-Istiya Village
Prepared by :
Uday Fuad Arabasi.
Qosay Hamid Awad.
Mosa'b Mahmoud Qtait.
Submitted to : Dr. Abd-Alhaleem Khader

## Slide 2: ISTIYA VILLAGE- DAIR

## Slide 3: Outline
Objectives and significance of the project.
Study area.
Methodology.
Modeling, and design.
Results, Conclusions, And,
Recommendation

## Slide 4: Objectives
The main objectives of this project are:
To hydraulically design a wastewater collection network for Dair-Istiya Village Area using SewarCAD program.

## Slide 5: SIGNIFICANCE OF THE WORK

## Slide 6: Approach
To design Sewer Collection Network.
Use SewerCAD software to design the network.

## Slide 7: STUDY AREA

## Slide 8: LOCATION

## Slide 9: TOPOGRAPHY
Maximum elevation = 440 m above MSL
Minimum elevation = 362 m above MSL
Mean elevation = 406 m above MSL

## Slide 10: AREA AND LAND USE
Total Area = 34164 donums
Built up Area = 610 donums
Agricultural land = 11000 donums
Forests and open areas = 19000 donums
The rest of the land has been confiscated by the Israeli occupation authorities

## Slide 11: POPULATION
Population | Year
674 | 1922
1190 | 1945
1500 | 1967
2100 | 1987
2803 | 1997
3831 | 2007

## Slide 12: Sewage Sources
Domestic Wastewater
Industrial Wastewater
Storm water
Infiltration

## Slide 13: CONSTRAINTS
Velocity [ 0.6 – 3 ]m/s
Cover ( 1 – 5 )m.
Slope( 1 – 15 )%.

## Slide 14: Methodology
Data Collection.
Training on SewerCAD Software.
Selection of the study area.
Designing by SewerCAD program.
Giving results and recommendations.
Preparation of data.

## Slide 15: Selection of the study area

## Slide 16: DATA COLLECTION
Boundary of the study area.
Contour map
Roads network
Structural plane
Population number
Outfall location

## Slide 17: PREPARATION OF DATA
Population forecasting using constant growth rate equation
Pn = P0( 1 + r )^n
Population in 2016 = 4800 capita ( from council )
Future population ( 2046 ) = 8970 capita
Growth rate | Time interval
0.0305 | 1997 – 2007
0.0254 | 2007 – 2016
0.022 | 2016 – 2026
0.020 | 2026 – 2036
0.019 | 2036 - 2046

## Slide 18: PREPARATION OF DATA
Demand = 120L /day / capita
Assume hourly factor = 3.5
Load calculation = Waste water generation + infiltration
Waste water generation = 0.8 * 0.12 * 8790 * 3.5 = 2953.4 CM /day
Infiltration = 0.2 * 0.8 * 0.12 * 8790 = 168.8 CM /day
Sanitary load = 3122.2 CM / day

## Slide 19: Sewer Collection Network
Sewer Systems
Sewerage Elements

## Slide 20: Related hydraulic concepts
Distance between manholes.
A General procedure for design flow rates quantification.
Friction Loss Methods.

## Slide 21: Design the Network by SewerCAD program.
Preparation of data

## Slide 22: Design the Network by SewerCAD program.
and conduit. Layout of Manholes

## Slide 23: Design the Network by SewerCAD program.
Sanitary load distributed using ArchHydro.

## Slide 24: Design the Network by SewerCAD program.
Load distribution in excel sheet to make Model builder

## Slide 25: Layout the network
Layout of Outfalls
We have two outfalls in the area.

## Slide 26: RESULTS

## Slide 27: RESULTS

## Slide 28: RESULTS

## Slide 29: Conclosion:
We recommend constructing a sewer network because the people will be very pleased and most of their problems will be removed.
All constraints are achieved and there are no any problems in the model, and all the results are in the ranges as specifications and criteria.
We use 8 inch diameter for all conduits and PVC material.

## Slide 30: THANK YOU