## Slide 1: An-Najah National University Faculty of Engineering and Information Technology Department of Industrial Engineering
Graduation Project
December 2014

## Slide 2: Investigating The Feasibility of Recycling The Various Categories of Solid Waste in Northern West Bank
Presented To:
Eng. Suleiman Daifi
Dr. Ayham Ja’roun
Prepared By :
    Laith Kittani
    Yousef Dwaikat
    Morshed Mhanna
    Firas Salahat
    WaleedTuffaha

## Slide 3: Overview
Introduction
SWM in Palestine
Zahret Al-Finjan Sanitary Landfill
Recycling Processes and Proposed Products
Decision-Making Model
Results and Recommendations

## Slide 4: Problem Statement
The Solid Waste issue is one of the most urgent problems in Palestine, only a small segment of the currently existing landfill sites are sanitary (i.e. waste is covered and leachate is gathered rather than drained into the ground).
The rest of waste disposal sites are either random dumpsites or controlled but unhealthy landfills (i.e. waste is covered but leachate is not gathered).

## Slide 5: Continued…
This situation is not sustainable and there are enormous risks and threats that are becoming more and more likely as nothing is done such as :
Polluting groundwater reserves
Serious health issues to the population.

## Slide 6: Continued…
Moreover, the political situation makes it extremely difficult to create more landfills as it requires a long and complicated process to acquire permissions and licensure from PNA departments and Israeli authorities.

## Slide 7: Continued…
This means that the current landfill sites, with their limited capacity, are filling up in a very high rate that their originally planned life expectancy is getting shorter.

## Slide 8: Scope of the Project
Geographically: Northern West Bank.
This study will not address :
  Collection
  Transportation Operations

## Slide 9: Objectives
Diagnose the existing Solid Waste Management Systems in Northern West Bank.
Investigate the possible options at every stage.
Investigate the feasibility of the option\s that resulted from the selection process.

## Slide 10: Methodology
1) Background Formation & Literature Review
2) Study of the Current Situation of SWM
Site Vistis and Idetification of Waste Compostion
Decison Making Model &Selection of the Best Recycling Options
Feasibility Study of the Selected Categories

## Slide 11: Current Situation of SWM in Palestine
Issues to consider:
Waste Generation
  total amount (1.4 million tons in 2013)
  annual growth (4%: 3% population growth and 1% generation increase per capita)
  per-capita rates (varies by region , avg. 0.94 kg\day)
Collection Rates
  Around 92% of households are covered (in1994 it was 64%)
  Also varies by the type of region (Rural (88%) vs. Urban (92.6%) vs. Camps (94%) and NWB (97%) vs. SWB (94%) vs. MidWB (92%) vs. Gaza (88%)
  Source : PCBS Publications & SWEEP Network studies

## Slide 12: Current Sanitary Landfills
# | Name | Location | Opening Year | Closure Year | Area (m2) | Annual Capacity (2013)
1 | Zahret Al-Finjan | Jenin | 2007 | 2017 | 95,000* (Current) | 304,000 ton
2 | Al-Menya | Bethlehem | 2013 | 2033 | 100,000 | 230,000 ton
3 | Jericho | Jericho | 2007 | 2015 | 10,300 | 11,500 ton

## Slide 13: Zahret Al-Finjan SFL
Design and construction of the ZF landfill began in 2005, with completion and the first waste received in June 2007.
Its’ construction was funded by the World Bank and the European Union , with a total cost of 14m USD. It is managed by the Jenin Joint Services Council.

## Slide 14: Zahret Al-Finjan SFL
The map shows its’ location in NWB.

## Slide 15: Site Description
The site consists of three main areas: waste reception and weighing area, sanitary waste deposition cells and the services area with the main building which houses the management offices.
The following map illustrates the main areas of the site with the access roads and the fences :
cells area
services area
waste reception area

## Slide 16: ZF Capacity
The land purchased for the project is 240,000 m2, but the used area is currently 95,000m2
It was supposed to serve northern governorates for about 15 years during the first stage of the project.

## Slide 17: Waste Quantities Received by Year
 | 2008 | 2009 | 2010 | 2011 | 2012 | 2013
January | 7,995 | 10,522 | 12,673 | 19,745 | 22,055 | 24,222
February | 9,089 | 10,032 | 11,162 | 19,694 | 20,880 | 22,811
March | 12,271 | 11,959 | 12,144 | 20,916 | 22,299 | 24,874
April | 12,483 | 11,357 | 10,698 | 19,595 | 22,145 | 25,355
May | 10,599 | 10,001 | 13,628 | 21,970 | 23,177 | 27,479
June | 10,599 | 10,836 | 14,618 | 22,533 | 22,956 | 27,024
July | 10,080 | 10,818 | 16,598 | 22,757 | 25,683 | 28,148
August | 11,006 | 11,880 | 18,668 | 22,593 | 24,070 | 26,122
September | 10,726 | 11,549 | 17,468 | 19,720 | 21,497 | 24,046
October | 10,580 | 11,648 | 17,094 | 20,442 | 23,394 | 25,499
November | 10,409 | 11,340 | 17,994 | 20,729 | 23,269 | 24,202
December | 9,964 | 13,325 | 18,517 | 20,484 | 26,266 | 24,572
Total | 125,800 | 135,267 | 181,262 | 251,178 | 277,692 | 304,354
Daily avg. | 344.66 | 370.59 | 496.61 | 688.16 | 760.80 | 833.85

## Slide 18: Continued…
The current capacity of the landfill is approximately 3 million tons of waste.
During the year 2014, the landfill started receiving waste from Ramallah and Al-Bireh, and currently it receives around 1000 tons every day, which means that the amount added this year will be around 360,000 tons.

## Slide 19: Continued…
By the end of the year, the total amount of waste that is dumped in ZF will be approximately 1.65 million tons.
By a simple calculation we conclude that the site will reach its maximum capacity in less than three and a half years.

## Slide 20: Separation site at ZF
At the moment, there is a waste separation line at the landfill.
It is currently offline because of some technical and administrative issues.

## Slide 21: Continued…
The separation line was operated in 2011 for a few months, during which valuable data was gathered on the operation of this line.
If the line is operated for two ten-hours shifts per day, it can process approximately 400 tons of waste.

## Slide 22: Waste Composition
Category |  | Percentage | Quantity | Percentage separated | Qty. separated per day | Qty. separated per day
Organics |  | 0.51 | 204 | 0.5 | 102 | 31824
Plastics | PP | 0.024 | 9.6 | 0.25 | 2.4 | 748.8
 | HDPE | 0.04 | 16 | 0.25 | 4 | 1248
 | PET | 0.06 | 24 | 0 | 0 | 0
Cardboard and paper |  | 0.16 | 64 | 0.4 | 25.6 | 7987.2
Metals |  | 0.028 | 11.2 | 0.5 | 5.6 | 1747.2
Glass |  | 0.033 | 13.2 | 0.1 | 1.32 | 411.84
Textile |  | 0.086 | 34.4 | 0 | 0 | 0
Others |  | 0.059 | 23.6 | 0 | 0 | 0
 |  | 1 | 400 |  | 140.92 | 43967.04

## Slide 23: Waste Composition
Chart: Waste Composition
| Organics | PP | HDPE | PET | Cardboard and paper | Metals | Glass | Textile | Others
Sales | 0.51 | 0.024 | 0.04 | 0.06 | 0.16 | 0.028 | 0.033 | 0.086 | 0.059

## Slide 24: Separation Remarks
Plastics in particular were separated into three categories, Polypropylene(PP), High Density Polyethylene (HDPE) and Polyethylene Terephthalate(PET).
The first two (PP&HDPE) can be recycled easily and several products can be made out of them but the PET requires very complicated and lengthy processing which makes it inefficient to recycle on the current scale.

## Slide 25: Separation Remarks
The yearly quantities were also extrapolated by multiplying the daily output by 312 days per year.
Paper and cardboard were treated as one category because most production lines can process them together to make an intermediate material called pulp.

## Slide 26: The Separation Line

## Slide 27: Recycling Options
  There are four main categories of waste that can be recycled at the current scale:
  Paper and Cardboard
  Plastics (PP & HDPE)
  Glass
  Organic Materials
Metals need larger plants and more complicated processes, therefore they were excluded and the separated amounts can be sold as is.

## Slide 28: Suggested Products
Raw Material | Proposed Product | Picture | Machine/Production Line
Paper and Cardboard | Paper grocery and shopping bags |  | Sunhope SBH-290W
 | Fruit trays |  | BST FP5000
 | Corrugated Cardboard |  | Champion 2PPCL
Plastics | Chairs |  | BorgMould HFL003
 | Sanitary pipes |  | Xinron TXA841162
Glass | Concrete Aggregates |  | FTM-251P
Organics | Compost |  | (none)

## Slide 29: Integer Programming Model
An Integer Programming model was constructed and solved using LINGO software, this model will optimize an objective function while considering a set of constraints.
Since the initial investment for any production plant is relatively large, the investment will have a negative net cash flow for the first year, then after one year, revenues will start to come in as the plant starts making products.

## Slide 30: Integer Programming Model
The Net Present Value for each of the options was calculated for each investment and was used as the objective Function for the LINGO Model.
Selling prices for the final products were obtained from people working in the corresponding sector.
The Model calculations are listed below:
Objective function:
Where Cj is the Net Present Value for the net cash flow of the jth investment.

## Slide 31: Integer Programming Model: Constraints
There were three constraints:
The total investment should not exceed 1 million USD.
ai is the initial cost for the ith investment
Only one of the paper and cardboard products can be selected (Mutually Exclusive).
Only one of the plastic products can be selected.

## Slide 32
Production Line(1) price |  |  | 500000 | Production Line(2) price | 100000
Production Line(1) cost |  |  | 598000 | Production Line(2) cost | 126000
selling price |  |  | 200 | Yearly Amount | 7987.2
 | year | cash flow in | cash flow out |  | 
 | 0 | 0 | 724000 | -724000 | 
 | 1 | 1597440 | 528266.6667 | 1069173.333 | 
 | 2 | 1597440 | 528266.6667 | 1069173.333 | 
 | 3 | 1597440 | 528266.6667 | 1069173.333 | 
 | 4 | 1597440 | 528266.6667 | 1069173.333 | 
 | 5 | 1597440 | 528266.6667 | 1069173.333 | 
 | 6 | 1597440 | 528266.6667 | 1069173.333 | 
 | 7 | 1597440 | 528266.6667 | 1069173.333 | 
 | 8 | 1597440 | 528266.6667 | 1069173.333 | 
 | 9 | 1597440 | 528266.6667 | 1069173.333 | 
 | 10 | 1597440 | 528266.6667 | 1069173.333 | 
 | 11 | 1597440 | 528266.6667 | 1069173.333 | 
 | 12 | 1597440 | 528266.6667 | 1069173.333 | 
 | 13 | 1597440 | 528266.6667 | 1069173.333 | 
 | 14 | 1597440 | 528266.6667 | 1069173.333 | 
 | 15 | 1597440 | 528266.6667 | 1069173.333 | 
 |  |  |  | $1,701,406.37 | 

## Slide 33: Integer Programming Model
The model is shown below:
max= 1.701*X1+1.41*X2+1.602*X3+0.936*X4+1.446*X5+0.525*X6+5.443*X7; X1+X2+X3<=1; X4+X5<=1; 724*X1+311*X2+1019*X3+1874.5*X4+1697.5*X5+626.7*X6+150*X7<=1000; @bin(X1); @bin(X2); @bin(X3); @bin(X4); @bin(X5); @bin(X6); @bin(X7);

## Slide 34: Decision Variables
X1: Whether to invest in Paper Bags manufacturing plant.
X2: Whether to invest in Fruit Trays manufacturing plant.
X3: Whether to invest in Corrugated Cardboard manufacturing plant.
X4: Whether to invest in Chairs manufacturing plant.
X5: Whether to invest in Plastic Pipes manufacturing plant.
X6: Whether to invest in Concrete Aggregate manufacturing plant.
X7: Whether to invest in Compost production.

## Slide 35: The Results
The model results showed that the optimal solution would be to invest in making the Paper grocery\shopping bags production line as well as the composting line.

## Slide 36: The Results
We notice that the model yielded two investments :
X1 which is the Paper Bag Production Line.
X7 which is the Compost production.

## Slide 37: Model Assumptions
There is a number of assumptions and simplifications that were suggested to make the model more convenient without compromising its’ authenticity. Following is a list of these assumptions:

## Slide 38: Model Assumptions (Continued…)
The estimated lifetime of the project is 15 years.
For the purpose of calculating Net Present Value for each investment, the interest rate will be set at 3.5%.
The available investment shall not exceed 1m USD.

## Slide 39: Model Assumptions (Continued…)
The administrative costs (administrative salaries and utilities ) were excluded from the cost calculations because they do not depend on the selected investment.

## Slide 40: Model Assumptions (Continued…)
Plastics and paper\cardboard require some processing before they can be used as raw materials to the production line.
The total cost of owning a production line was calculated by adding 18% tax to its price and 8000$ in transportation cost.
The depreciation was calculated using the Straight Line method with zero residual value.

## Slide 41: Conclusions and Recommendations:
Conclusions:
The Solid Waste Management sector in Palestine is a relatively new sector and has substantial potentials for improvement and investment.
Large amounts of waste are being dumped randomly and the landfills are filling up in a much faster rate than it was first expected when they were designed.

## Slide 42: Conclusions
Awareness of the importance of recycling and sustainability issues in general remains relatively low among Palestinians compared to the global population.
Governmental institutions and NGOs play a modest role in promoting this sector and encouraging investment in recycling projects.

## Slide 43: Recommendations
All stakeholders, governmental and non-governmental, must combine efforts to solve the current issues and achieve a better utilization of the huge opportunities in the field of SWM in Palestine in general.
The private sector should play a greater role in this field by investing in recycling projects such as the ones descried in this study.

## Slide 44: Recommendations
Further research should be undertaken to investigate the feasibility of other recycling options and also exploring innovating and non-traditional ways and approaches in reusing and recycling.

## Slide 45: Upcoming Work
In the second part of our project, we will investigate the feasibility of the investments that resulted from the model. Market Studies, Social and Environmental Impact, Technical Study and Financial Analysis.

## Slide 46
Thanks for Listening