## Slide 1
An-Najah National University Building Engineering Department
Designing the “4 stars” Hotel
Prepared by:
Rawan Bozyah
Mohammad AbuHamma
Muath Qaradeh
Supervisor:
Eng. Moayad Salhab

## Slide 2
2
CONTENTS:
Site and location
Architectural plans
Environmental design
Thermal design
structural Aspects
Artificial lighting
HVAC System design
Electrical system design
Acoustical design
Elevator system design
Supply Water design
Drainage System design
Fire Fighting System design
Quantity surveying and cost estimation

## Slide 3: Site and location

## Slide 4: Site location
The land location in Nablus city Rafidia street AL- Junaid
Specifically in the East of An-Najah National University and it located at 32.2°N latitude and 35.2° E longitude.
And the area of land is 1080 m2 , it located in a classification area A.

## Slide 5: Architectural Plans

## Slide 6: The 3D model for the existed architectural plan.

## Slide 7: Basement floor (Parking) – Before

## Slide 8: Third Basement floor (Parking) – After

## Slide 9: Second Basement floor (Parking)- After

## Slide 10: First Basement floor (Storage) – Before

## Slide 11: First Basement floor (Entertainment) – After

## Slide 12: Ground floor (Storage) – Before

## Slide 13: Ground floor (Reception) – After

## Slide 14: First floor (Storage) - Before

## Slide 15: First Floor (Cafeteria) – After

## Slide 16: Second ,Third and Fourth Floors (Offices) - Before

## Slide 17: Second Floor (Restaurant) – After

## Slide 18: Third, Fourth and Fifth Floors (Bed rooms) – After

## Slide 19: Fifth and Sixth Floors (Bed rooms) - Before

## Slide 20: Sixth Floors (Bedrooms) – After

## Slide 21: Seventh Floor (Bedrooms) – Before

## Slide 22: Seventh Floors (Bedrooms) – After

## Slide 23: North West Elevation
North East Elevation

## Slide 24: South West Elevation
South East Elevation

## Slide 25: Section A-A

## Slide 26: Environmental Design

## Slide 27: Daylighting
The model of the facility from Design Builder after modification
The model of the facility from Revit before modification
Main modification for day lighting:
Adding Louvers.
Using low transmission glass.

## Slide 28: Daylight analysis for the model for the First Basement Floor and fourth floors before and after modification
Before
After

## Slide 29: Daylight analysis for the model for the Ground Floor and fourth floors before and after modification
Before
After

## Slide 30: Daylight analysis for the model for the First Floor and fourth floors before and after modification
Before
After

## Slide 31: Daylight analysis for the model for the Second Floor and fourth floors before and after modification
Before
After

## Slide 32: Daylight analysis for the model for the Third ,Forth , fifth and Sixth Floor and fourth floors before and after modification
Before
After

## Slide 33: Daylight analysis for the model for the Seventh Floor and fourth floors before and after modification
Before
After

## Slide 34: Thermal Design

## Slide 35: the materials that were used in the walls and slabs in the faculty
External wall
U- value for external wall equal 0.289 (W/m2.k )
Internal slab
the U- value for Internal slab equal 1.746 (W/m2.k )
Internal wall
the U- value for internal wall equal 2.186 (W/m2.k)

## Slide 36: The comfort graph for the faculty from Design Builder

## Slide 37
Temperature and heat gain (cooling load)
Temperature and heat loss (heating load )

## Slide 38: Structural Aspect

## Slide 39: Structural Aspects
Design codes
ACI 318-14
UBC-97
Specifications
Concrete’s Compressive strength (f’c) = 28 MPa
Yielding strength of steel (Fy) = 420 MPa
Bearing capacity of soil = 250 kN/m2
Design loads
SID = 4.5 kN/m2
L.D = 5 kN/m2

## Slide 40: Structural Aspects
Site analysis
seismic zone : 2B (Z = 0.20).
( I ) = 1
Soil profiles : Sc
(Ca) = 0.24
(Cv) = 0.32
(R) = 5.5

## Slide 41: Structural Aspects
Load combinations on Etabs (according to UBC97)
1.4D 12-1
1.2D+1.6L 12-2
1.34D+1L+1EQx+0.3EQy 12-3
1.34D+1L+1EQy+0.3EQx 12-4
0.76D+1EQx+0.3EQy 12-5
0.76D+1EQy+0.3EQx 12-6
1D 12-7
1D+1L 12-8
1D+0.71EQx+0.21EQy 12-9a
1D+0.71EQy+0.21EQx 12-9b
0.9D+0.71EQx+0.21EQy 12-10 a
0.9D+0.71EQy+0.21EQx 12-10b
1D+0.54EQx+0.16EQy+0.75L 12-11a
1D+0.54EQy+0.16EQx+0.75L 12-11b

## Slide 42: Structural Aspects
Checks
Compatibility check
Equilibrium check
Internal Forces check
Deflection check
Period check
Base shear check
Drift check
All checks are OK

## Slide 43: Structural Aspects
Column design
Columns Dimensions
C1/C2 : circular 120 cm diameter
C3 : rectangular 40*90 cm
C4 : circular 80 cm diameter
C4 starts from the 3rd floor
C3
C3
C4
C4
C4
C4

## Slide 44: Structural Aspects
Column detailing
C2
D-D
C2
C1
C1
D-D

## Slide 45: Structural Aspects
Column detailing
C4
C4
D-D
C3

## Slide 46: Structural Aspects

## Slide 47: Structural Aspects
Beam design
Standard beam detailing

## Slide 48: Structural Aspects
Beam detailing

## Slide 49: Structural Aspects
Shear wall detailing

## Slide 50: Structural Aspects
Basement wall design & detailing
Ɣ for soil =18 KN/m3
ᴓ for backfilling soil = 30 degrees
F= 0.5 * 10.1 *18 = 91 KN/m
The basement wall design was done with Etabs.
(uniform reinforcement)
Wall thickness = 50 cm
As wall from Etabs = As min

## Slide 51: Structural Aspects
Foundation design and checks
Safe 2016 software is used to check and design footings
The foundation is a mat footing with 100cm thickness
Bearing capacity of soil =250KN/M3
f`c=28MPa

## Slide 52: Structural Aspects
Foundation design and checks
Checks
Soil pressure Check : All values are less than 250KN/M3
Punching shear check : All values are less than 1 , Ok
Deflection Check : All values are less than 10 mm , Ok

## Slide 53: Structural Aspects
Foundation design and checks
Detailing
Mat footing section
Mat footing reinforcement

## Slide 54: Structural Aspects
Foundation design and checks
Detailing
Mat footing additional reinforcement

## Slide 55: Structural Aspects
Foundation design and checks
Wall footing detailing
This footing is used to support the Laundry room next to the building.

## Slide 56: Structural Aspects
Ramp design and checks
The Ramp is 35cm thick.
M 11 and 22 on ramp slabs in Safe are checked, to find if any region on slabs has a moment larger than 67kn.m/m^2. none found. Ok

## Slide 57: Structural Aspects
Ramp design and checks
Detailing

## Slide 58: Electro-mechanical Aspects
Artificial lighting system
HVAC system
Electrical system
Acoustical aspects and design
Elevator system
Water supply
Drainage
Safety system

## Slide 59: Lighting design

## Slide 60: Artificial lighting Design

## Slide 61: 3D result from DIALUX evo for the Lobby hotel

## Slide 62: The result from DIALUX evo for the Multipurpose Hall

## Slide 63: 3D result from DIALUX evo for the Restaurant

## Slide 64: 3D result from DIALUX evo for the Kitchen

## Slide 65: 3D result from DIALUX evo for the GYM

## Slide 66: 3D result from DIALUX evo for the Bed room

## Slide 67: 3D result from DIALUX evo for the Office

## Slide 68: HVAC System design

## Slide 69: Electro-mechanical Aspects
HVAC system design
Variable Refrigerant Flow (VRF) system is used
VRF consists of an out-door unit feeding multiple in-door units via a BC-controller
Indoor units
Mitsubishi Ceiling concealed low static pressure units (1.2, 1.7, 2.2, 2.8 kW)
Mitsubishi Way Airflow Compact Cassette (3.6, 4.5 kW)
Outdoor unit
Mitsubishi PURY-EP200YNW-A
BC-controller
The CMB-WP108V-GA1 (8 branches)
The CMB-WP1016V-GA1 (16 branches)

## Slide 70: Electro-mechanical Aspects
HVAC system design
Indoor and Outdoor unit calculations

## Slide 71: Electro-mechanical Aspects
HVAC system design
HVAC units distribution in the 6th floor

## Slide 72: Electro-mechanical Aspects
HVAC system design
Ducting (fresh air and exhaust) 1st floor kitchen

## Slide 73: Electrical system design

## Slide 74: Electro-mechanical Aspects
Electrical system design
Single line diagram

## Slide 75: Electro-mechanical Aspects
Electrical system design
Socket and lighting distribution
B1

## Slide 76: Electro-mechanical Aspects
Electrical system design
Socket and lighting distribution
F1

## Slide 77: Electro-mechanical Aspects
Electrical system design
Socket and lighting distribution
F7

## Slide 78: Acoustical Design

## Slide 79: Acoustical Design
Objective: is to achieve auditory satisfaction for people within spaces
by achieving the requirements of the following Parameters:
Reverberation Time [RT60]
Noise Criteria [NC]
Sound Transmission Class [STC]
Impact Insulation Class [IIC]
Sound Pressure Level [SPL]

## Slide 80
Reverberation Time Standard

## Slide 81
Reverberation Time Design
Hotel Bedroom
We've done a treat for all spaces, but for time constraints we show you the most important Space in the hotel has designed for.
Construction Element | Internal Finished Material
Ceiling | Brick Plaster
Walls | Brick Plaster, Framed Plasterboard
Floor | Moquette_
Door | Plywood
Window | Generic LoE SPEC SEL CLEAR 6MM Rev
Drapes | Drapes_Absorber

## Slide 82
Sound Transmission Class
For Masonry Walls:
STC Designing value was 35 dB
Layers of Masonry Walls
5 cm stone
10 cm concrete
8 cm polytherane
10 cm hollow block
13 mm plaster

## Slide 83
For Curtain Walls:
STC Designing value was 35 db

## Slide 84
For Partitions
Layer of Partitions
Plaster 13 mm
Hollow Block 10 cm
Plaster 13 mm

## Slide 85
Impact Insulation Class
For Roof
IIC when designing the roof depends on the rate of Rainwater falling, such as the rate of rainfall in Nablus city in the last of 10 years = 253 mm
Layer of Roof Slab
4 cm lightweight concrete
8 cm polytherane
6 cm reinforcement concrete
26 cm hollowblock with reinforcemet concrete
13 mm plaster

## Slide 86
For Internal Floors
We designed the internal floors based on the relationship between the space and the above, as shown in the following table, such as taking a worst-case and circular on all internal floors:
Worst case it was between the bedroom above the bedroom
Layer of Internal Floors
Terrazo tiles 2 mm
3 cm mortar
5 cm sand
8 cm reinforcement concrete
30 cm u- boots with Reinforcemet concrete
13 mm plaster

## Slide 87
Speakers System Design
Objective: improve sound pressure level and intelligibility inside spaces
By using the EASE Program, we designed a speakers system for many spaces, But for lack of time we will review the design for the Multipurpose
%AL
cons
100
-
33%
33
-
15%
15
-
7%
7
-
3%
3
-
0%
appreciation
unacceptable
problem
acceptable
good
excellent

## Slide 88
Total Sound Pressure Level:
this value represented direct & indirect SPL:

## Slide 89: Elevator System Design

## Slide 90
Elevator System Design
Elevator Specification | 
# of Elevator | 2 and additional one for service
Capacity | 2500lb/elevator
 | 13 person / elevator
Speed | 300 fps
Interval | 30 – 50 sec
Waiting Time | 18 – 30 sec

## Slide 91: Supply Water Design

## Slide 92
Pump Specification | 
Head | Up to 45 meter
Pressure | 72 Psi
Supply Water Design
Use Central Tank with Pump System, as shown in the inside Section:
We need 28 CM of Water added to 15 CM for Firefighting System,
which means we need to Central Tank it has 43 CM and pumps
pumping the water to the roof tanks it has the following specification:

## Slide 93
Central Tank Specification
Product Type | Storage Tank
Weight (lbs) | 2800
Material | Polyethylene
Capacity (CM) | 45
Height (m) | 4.90
Width (m) | 3.60

## Slide 94
Water FU`s Value
Fixture Type | Occupancy | Load Value of FU’s |  | 
 |  | Cold | Hot | Total
Lavatory | Private | 0.5 | 0.5 | 0.7
 | Public | 1.5 | 1.5 | 2
Water closet | Private | 2.2 | - | 2.2
 | Public | 5 | - | 5
Shower | Private | 1 | 1 | 1.4
 | Public | 3 | 3 | 4
Bathtub | Private | 1 | 1 | 1.4
Kitchen Sink | Hotel, Restaurant | 3 | 3 | 4
Sink Service | Various | 2.25 | 2.25 | 3
Dishwashing mash | Public | 2.25 | 2.25 | 3
Total Fus for the building |  |  |  | 454.6
Pipes of Collectors

## Slide 95
Water Supply Distribution
Bedroom Floors Distribution

## Slide 96
Restaurant & Cafeteria Floors Distribution

## Slide 97
B1 & GF Floors Distribution

## Slide 98: Drainage System Design

## Slide 99
Drainage System Design
Total DFUs in the Project = 651

## Slide 100
Type of Pipe | Fixture Type | Pipe Diameter (Inch)
Vertical Branch | Lavatory | 1.25"
 | Kitchen Sink | 
 | Sink Service | 
` Horizontal Branch | Lavatory | 
 | Kitchen Sink | 
 | Sink Service | 
 | Bathtub | 
 | shower | 
 | Dishwashing mash | 2"
 | Water closet | 4"
 | Public water closet | 4"
Sewer or Drain | Lavatory with Bathtub | 2” – 1% slope
 | Lavatory with shower | 
 | Bathtub with kitchen sink with Lavatory | 
 | Service sink with Service sink | 3” – 1% slope
 | Dishwashing mash with Dishwashing mash | 2” – 2% slope
 | kitchen sink with kitchen sink | 2” – 1% slope
 | Shower with Shower | 2” – 2% slope
 | Water Closet | 4” – 1% slope
 | Public Water Closet | 
Main Sewers |  | 
Stacks |  | 4" - 5 stacks
 |  | 5" - 2 stacks
 |  | 6" - 1 stacks
Vent |  | 2" inside building then convert 4" on a roof with 4 ft length
Main Sewer network in the ceiling of the Parking |  | 4" - 6 stacks – 1% slope
 |  | 5" - 6 stacks – 1% slope
 |  | 6" - 3 stacks - 1% slope
Sewer between Manholes |  | 6" - 1% slope
Size of Drainage Piping

## Slide 101
Network of Drainage System

## Slide 102: Fire Fighting System Design

## Slide 103
Fire Fighting System Design
To Jordanian & Palestinian Safety Code, the bedrooms fall under moderate hazard, so
used to smoke & heat flame Alarms integrated sprinklers network

## Slide 104
Tree configuration of Sprinklers
Each sprinklers network Consists of :
Branches line
Main cross line
Sprinkler head
Risers
Underground Supply
Fire dept connection

## Slide 105
Sizing of Pipes

## Slide 106
Tank Size Needed: 14.5 CM
The pressure o the Pump used: 45 Psi
Tank & Pump Sizing
We used the same Central tank for Fresh water
Fire Hose
The diameter of Supply Pipes always equals 2.5 Inches

## Slide 107
Extinguishers
Number & Location determined by :
square footage
The layout of an area
proximity to people and the presence of different types of combustible material.

## Slide 108
Kitchen in the Restaurant
Used Class K
Foam Generators
Flam Detectors Alarm Used

## Slide 109
Escape Routs

## Slide 110: Quantity surveying and Cost Estimate

## Slide 111: Cost Estimation
Cost Estimation | 
Total Cost (NIS) | 15110000
Unit Cost (NIS)/SM | 2727
Unit Cost (JOD)/SM | 579
Unit Cost ($)/SM | 816

## Slide 112: thank you all for listening