## Slide 1: Integrative design of masjed
Presented by:
Supervisor :
21/12/2015
An-Najah National University
Motaz Abu Al-Adas
Mo’men Zaghloul
Hammam Al-basheer
Ibrahim Abu Sarah
Eng. Abdelhakeem Al-Jawhari

## Slide 2: outline
Introduction
Site analysis
Architectural design
Structural design
Environmental design
Electrical design
Mechanical design
Quantity Survey
safety

## Slide 3: Introduction
The masjed is a house of worship for Muslims . The masjed typically consists of a large lounge building and services places

## Slide 4: Proposed Location
The site of the project is located in Arrabah Town .
The area of land about 3500 m² .
The land has slight slope , and stands at an elevation of around 400m above Sea level.

## Slide 5: Architectural design
Site plan

## Slide 6: Spaces area in masjed designed:

## Slide 7: Spaces area in masjed designed:

## Slide 8: Spaces area in masjed designed:
The women pray hall has an area of 73m² and its capacity approximately 70 women.

## Slide 9: Architectural analysis
The different level between bathroom and ablution unit is used to many purposes 1) provide the space for windows to the purpose of ventilation and lighting inside the bathrooms 2) this different in level keep the tanks at the same cover level. With using solarium water tank . By setting the solarium mirrors on the low level and their tanks on high level

## Slide 10: Architectural design
South Elevation

## Slide 11: Architectural design
North elevation

## Slide 12: Architectural design
East Elevation :

## Slide 13: Architectural design
West Elevation

## Slide 14: Architectural design
sections

## Slide 15: Architectural design
sections

## Slide 16: Environmental Design
Codes and specifications:
Energy Efficient Palestinian Building Code
Software:
Autodesk Ecotect Analysis, 2011

## Slide 17: Integrative design of masjed
Presented by:
Supervisor :
21/12/2015
An-Najah National University
Motaz Abu Al-Adas
Mo’men Zaghloul
Hammam Al-basheer
Ibrahim Abu Sarah
Eng. Abdelhakeem Al-Jawhari

## Slide 18: outline
Introduction
Site analysis
Architectural design
Structural design
Environmental design
Electrical design
Mechanical design
Quantity Survey
safety

## Slide 19: Introduction
The masjed is a house of worship for Muslims . The masjed typically consists of a large lounge building and services places

## Slide 20: Proposed Location
The site of the project is located in Arrabah Town .
The area of land about 3500 m² .
The land has slight slope , and stands at an elevation of around 400m above Sea level.

## Slide 21: Architectural design
Site plan

## Slide 22: Spaces area in masjed designed:

## Slide 23: Spaces area in masjed designed:

## Slide 24: Spaces area in masjed designed:
The women pray hall has an area of 73m² and its capacity approximately 70 women.

## Slide 25: Architectural analysis
The different level between bathroom and ablution unit is used to many purposes 1) provide the space for windows to the purpose of ventilation and lighting inside the bathrooms 2) this different in level keep the tanks at the same cover level. With using solarium water tank . By setting the solarium mirrors on the low level and their tanks on high level

## Slide 26: Architectural design
South Elevation

## Slide 27: Architectural design
North elevation

## Slide 28: Architectural design
East Elevation :

## Slide 29: Architectural design
West Elevation

## Slide 30: Architectural design
sections

## Slide 31: Architectural design
sections

## Slide 32: Structural design
The design was done according to the following codes and standards:
ACI -318-2011 for reinforced concrete structural design.
UBC -97 for earthquake and wind load computations

## Slide 33: Structural design
The software's used for analysis and design is:
Etabs program and sap2000: for structural analysis & design.
AutoCAD for all drawings.

## Slide 34: Structural design.
The structure of the masjed will be built on clay soil with 250 KN/m2 bearing capacity according to soil test.
The structure were designed for static and dynamic cases

## Slide 35: Structural design
The materials used in the construction are have the following characteristics:
Compressive strength of Concrete (fc`) = 24 MPa for all structural elements and Concrete (fc`) = 28 MP for water tanks
Yielding strength of reinforcement steel fy = 420 MPa

## Slide 36: Structural design

## Slide 37: Structural design

## Slide 38: Structural design
Equilibrium check for main hall:
Internal forces check:
Loads | etab (KN) | Manual (KN) | % of error
Dead | 7520.176 | 7107.3 | 3.2
Live | 1896.571 | 1895.4 | 0.2
Element | σu from etab (KN/m2) | σu from manual (KN/m2) | % of error
Beam | 238.5 | 240.2 | 0.71
Slab | 30 | 30.03 | 0.1

## Slide 39: Structural design
Slabs design: (one way solid slab)
Max. Moment in the main direction=490.6/16.3=30 KN.m/m
5Ф12/m (Use upper and lower grid with 5Ф12/m in two directions for all slabs except the WC roofs)

## Slide 40: Structural design
Max. Moment in the main direction=554/8.2=67.6 KN.m/m
Use 7Ф16/m in the main direction (parallel to Y) and5Ф12/m in the secondary direction (parallel to X)

## Slide 41: Structural design
Max. Moment M22 (NØ) form etab model=-18.9
Area of steel=432mm2use 6Ø10/m
Max. Moment M11 (Nθ) form etab model=-3.93
Area of steel=87mm2
ASshrinkage=270mm2 use 6Ø8/m

## Slide 42: Structural design
Beams design:
The min depth of beams are specified according ACI-Code318-08
Beams dimension, 30x60 cm for all beams in the main prayer hall and 30x40 for main beams in the other parts and 40x20 for secondary beams.

## Slide 43: Structural design
Columns design:
The equation has to be used to calculate the area for the column.
𝑃𝑢= ∅ (0.85(0.85(1−𝜌) 𝑓𝑐′+𝜌𝐹𝑦)) 𝐴𝑔
The minimum dimension used is 30cm

## Slide 44: Structural design
Column name | Column dimensions in cm
C1 | 30X30
C2 | 30X90
C3 | 40X90
C4 | CER.70

## Slide 45: Structural design
Design of Footings:
Isolated footing for columns and wall footing for walls were chosen

## Slide 46: Structural design
Dynamic Design:
Dynamic analysis and design for the building using UBC1997 design code.
1. Importance factor: I =1.25
2. Z=rock acceleration=0.2
3. Soil profiles is (Sd).

## Slide 47: Structural design
The period was computed manually(𝑇) = 0.187sec
The period was checked using etab: (T) = 0.133sec
When ((1.3*Tmanual) =1.3*0.187=0.24)> (Tetab=0.133) ok
Check if more than 90% of model movements are included in our design

## Slide 48: Structural design
Design of septic tank:
-Interior dimensions (5*5*3)
-This Septic tank will be underground
-The design has two cases of Loading:
Full liquid without soil exposed
Empty Case with soil exposed

## Slide 49: Structural design
Design of Retaining wall:
When the walls are not high, gravity walls are used.

## Slide 50: Structural design
Over turning chick:
F.S = 2.01>2 OK
Sliding chick:
F.S=1.73>1.5 OK

## Slide 51: Structural design
The other boundary walls were designed as the common boundary wall with 40*20cm columns and beams

## Slide 52: Structural design
Design of Stairs:
Mehrab staircase:
The staircase is simply supported by two shear walls

## Slide 53: Structural design
Design of Minaret:
The height of minaret is 15 m.

## Slide 54: Environmental Design
Codes and specifications:
Energy Efficient Palestinian Building Code
Software:
Autodesk Ecotect Analysis, 2011

## Slide 55: Some Facilities Used to Achieve Environmental Design
Project have a dome in the main hall that give Daylight and natural ventilation.
In the south elevation ,horizontal stone frame use to shading the windows by 60 cm.

## Slide 56: Sun path on the building at 21 July

## Slide 57: Sun path on the building at 21 January

## Slide 58: Zones of building in ecotect

## Slide 59: Thermal insulation
The external wall section

## Slide 60: Thermal insulation

## Slide 61: Simulation the Model with insulation
Heating and Cooling Loads With Insulation(50Kw/m2)

## Slide 62: Thermal comfort(PMV&PPD)

## Slide 63: Natural day light
Natural lighting distribution in main hall(without dome)280Lux

## Slide 64: Natural day light
Dome effect on Natural lighting add (180Lux)

## Slide 65: Acoustical design

## Slide 66: Acoustical treatments
plywood panel (4*7) m
Acoustical proprieties

## Slide 67: Dome effects at sound waves
Sound source in Mihrab
Creep of sound under the dome

## Slide 68: Acoustical design
STC after adding material

## Slide 69: Loudspeakers design and distribution
F-121C/M Type
Specifications

## Slide 70: Speaker distribution

## Slide 71: Artificial lighting design
Accurately, Comfortably and Safely

## Slide 72: Artificial lighting design
Zonal Cavity method

## Slide 73: Artificial lighting

## Slide 74: Artificial lighting Distribution

## Slide 75: Electrical Design
Rated current for circuit breaker (lighting): 10 Amp
Rated current for circuit breaker (sockets): 16 Amp
One Branch for (4-5) 2Amp sockets.
Branches for lighting: 1 branch for each 50 m²

## Slide 76: Mechanical design
Content
Water Supply system.
Rain water .
Drainage system .
HVAC system .
Code : ASHREA 2009

## Slide 77: Water supply Network

## Slide 78: Water supply Network
Vertical pipe diameter = 2 inch
horizontal pipe diameter = 1.5 inch
Branches diameter = 1.25 inch.
use an auxiliary pump> 6psi to get suitable pressure in ground floor

## Slide 79: Footing Dryer

## Slide 80: Rain Water

## Slide 81: Drainage System
Diameter of drainage pipe between manholes 6’’

## Slide 82: HVAC system “Air to Air System”
Air handle unit :
The type of AHU used in our design: Quantum Climate Changer “QUANTUM XP”

## Slide 83: HVAC system
Characteristic of linear slot diffuser used in side wall in main pray hall:

## Slide 84: HVAC system

## Slide 85: Safety
Fire protection system is essential where the fire hazard is possible in every minute and expected. In a place like a masjed, the most sensitive region is the prayer hall because of the carpets on the floor, and the wood used in the decoration inside. The fire hose cabinet and the fire extinguisher in addition to the smoke detector and alarm system are used

## Slide 86: Quantities surveying
Total cost = 540000 $
for each meter square: five hundred seventy-two (572$).

## Slide 87: Some Facilities Used to Achieve Environmental Design
Project have a dome in the main hall that give Daylight and natural ventilation.
In the south elevation ,horizontal stone frame use to shading the windows by 60 cm.

## Slide 88: Sun path on the building at 21 July

## Slide 89: Sun path on the building at 21 January

## Slide 90: Zones of building in ecotect

## Slide 91: Thermal insulation
The external wall section

## Slide 92: Thermal insulation

## Slide 93: Simulation the Model with insulation
Heating and Cooling Loads With Insulation(50Kw/m2)

## Slide 94: Thermal comfort(PMV&PPD)

## Slide 95: Natural day light
Natural lighting distribution in main hall(without dome)280Lux

## Slide 96: Natural day light
Dome effect on Natural lighting add (180Lux)

## Slide 97: Acoustical design

## Slide 98: Acoustical treatments
plywood panel (4*7) m
Acoustical proprieties

## Slide 99: Dome effects at sound waves
Sound source in Mihrab
Creep of sound under the dome

## Slide 100: Acoustical design
STC after adding material

## Slide 101: Loudspeakers design and distribution
F-121C/M Type
Specifications

## Slide 102: Speaker distribution

## Slide 103: Artificial lighting design
Accurately, Comfortably and Safely

## Slide 104: Artificial lighting design
Zonal Cavity method

## Slide 105: Artificial lighting

## Slide 106: Artificial lighting Distribution

## Slide 107: Electrical Design
Rated current for circuit breaker (lighting): 10 Amp
Rated current for circuit breaker (sockets): 16 Amp
One Branch for (4-5) 2Amp sockets.
Branches for lighting: 1 branch for each 50 m²

## Slide 108: Mechanical design
Content
Water Supply system.
Rain water .
Drainage system .
HVAC system .
Code : ASHREA 2009

## Slide 109: Water supply Network

## Slide 110: Water supply Network
Vertical pipe diameter = 2 inch
horizontal pipe diameter = 1.5 inch
Branches diameter = 1.25 inch.
use an auxiliary pump> 6psi to get suitable pressure in ground floor

## Slide 111: Footing Dryer

## Slide 112: Rain Water

## Slide 113: Drainage System
Diameter of drainage pipe between manholes 6’’

## Slide 114: HVAC system “Air to Air System”
Air handle unit :
The type of AHU used in our design: Quantum Climate Changer “QUANTUM XP”

## Slide 115: HVAC system
Characteristic of linear slot diffuser used in side wall in main pray hall:

## Slide 116: HVAC system

## Slide 117: Safety
Fire protection system is essential where the fire hazard is possible in every minute and expected. In a place like a masjed, the most sensitive region is the prayer hall because of the carpets on the floor, and the wood used in the decoration inside. The fire hose cabinet and the fire extinguisher in addition to the smoke detector and alarm system are used

## Slide 118: Quantities surveying
Total cost = 540000 $
for each meter square: five hundred seventy-two (572$).